## Slide 1
State of art of the ECAL
for LC experiment
Jean-Claude BRIENT
Laboratoire Leprince-Ringuet
Ecole polytechnique- CNRS/IN2P3

## Slide 2
The CERN Boson X(125GeV) is coupled to the Z boson (Signal in ZZ)
Not yet a clear
signal in WW
2 jets+X(125) @ 65%
YES, if the jets measurement is sufficiently good
to disentangle Z,W and X(125) by the recoil to the
di-jets mass
Would it be possible to separate it
from 2 jets+Z or from 2 jets+W ?
X(125)
X(125)
PFA reconstruction ,
Partially demonstrated by ALEPH
Proposed and studied for TESLA project (1998-2003)
Used by CMS
Use to design ILC detector (SID, ILD)
What is PFA ??
See talk by H.Yamamoto san

## Slide 3
Goal for the ECAL
Separate the photon(s) from neutral and charged hadrons
Identify the electron
Follow the hadronic showers development (need good connection with HCAL)
Estimate as precisely as possible the photon(s) direction, position and energy
Granularity , compactness, homogeneity
Stop, Identify and Measure photon (s) , electron(s)
If possible, follow all the other particles
Following e.m. showers development and optimising
separation between close showers leads to readout
of large segmentation, small pixel readout size,
compactness (small Molière radius), minimal distance
between ECAL-HCAL (pattern ECAL-HCAL), ….
For HEP community members
Particle Flow Algorithm
Make a photography
of the particles created
by beams collisions
Create a camera with
Radiator between 2 layers
of pixels to make interaction
for electron(s) , photon(s)
A large number of pixels
No hole
Uniform response to have
good picture

## Slide 4
LHC-CMS
From this
to that
WANT an
IMAGING DEVICE
Detector for LHC at CERN
ECAL
HCAL
This talk
LC Proposed detector
Illustration
100M pixels every 300 ns
PHOTO with

## Slide 5
External constraints from
  The large B-Field (protection against machine background),
  The accelerator time structure,
  and of course the COST
Granularity , compactness, homogeneity
--------------------------------------------------------------------
large number of pixel layers, small pixel size, compactness
with
The camera ….. (we call that sampling calorimeter)
Radiator in Tungsten for compactness, small width for em showers
and for the active layers
  Pixels in silicon PIN diode (R&D on MAPS with digital readout)
  Possible small size scintillator strips , read by SiPM (R&D on going)
  Micromegas (possible but not demonstrated)
leads to

## Slide 6
It is opening the following questions
Calibration of 100 millions channels and signal stability (we want same response for same collision)
Capability to make zero suppress “on site” (we don’t want to read empty pixel)
Keep S/N ≥ 10 at MIP level and coherent noise under control (noise , radio/TV , telephone call )
Multiplexing for the quantity of signal line out (we don’t want to have 100M cables)
Power management due to large number of channels (we don’t want to burn our electronics readout)
KEEP the COST UNDER CONTROL (we want an affordable cost)
Choose stable device (silicon) or control & monitor the signal stability (Scint. or Micromegas)
ADC& digital memory in readout chip, close to active layer. Read memories at each end of bunch train
i.e. Silicon PIN diodes …. AC/DC coupling , ground loop , etc… a lot of R&D (EMC study)
Large number of Channels/VFE ASIC… (KPIX, SKIROC), but only few readout line
Power pulsing (thanks to machine structure)  reduced the power to dissipate… no cooling inside
Reduce the overall surface or use lower cost active device (Micromegas, scintillator) BUT warning versus point a) and c) . Contact with producers and try to define R&D to reduce cost
A set of answers

## Slide 7
The answers open new set of questions
For scintillator … signal stability vs temp., dark rate, linearity , uniformity inside strip, COST
VFE inside ….. Power dissipation, e.m. shower effect on VFE, very high level of integration
Very thin PCB …. Crosstalk, EMC, Industrial Yield , COST !!
Power pulsing …. Gain amplifier stability, Eddy current, power distribution, induced NOISE
Trade off between cost vs performances … Define the cost drivers, the right level of realism
for simulation and disentangle detector from PFA program effects
define R&D on cost …….
1 - Convince the producers to give us the information on the cost drivers
2 - Establish a FAIR comparison on the cost (contingency, construction model, manpower,..)

## Slide 8
First prototype (2006) : validation of physics perf. for high density channels device
First generation prototype
tested on beam 2006-2010
30 layers - ~10000 channels
Mechanical structure: carbon fibre
composite, incorporating tungsten layers
Standard printed circuit slabs hold
silicon sensors & electronics
(outside detection area)
FIRST ATTEMPT

## Slide 9
9
Pedestal MIP
ECAL calibrated with cosmics and muon beams
Shows very stable behaviour
S/N ~ 7.5
Energy resolution =
16.5/sqrt(E)+1.1%
Longitudinal
shower profiles
non-linearity<1%
SILICON - TUNGSTEN
FIRST ATTEMPT

## Slide 10
And now the tests of the camera
Efficiency finding electron
close to muon
Electron - muon
pion - pion
pion - pion
pion
Quantitative test has been published by CALICE (test of PANDORA PFA with TB data)

## Slide 11
NOW develop a scalable version.
Here the example of ILD ECAL
Carbon fiber –Tungsten structure with Alveola
to slide in the active layers.
No DEAD ZONE !!!
GEOMETRY

## Slide 12
Slide off
the detector slab
GEOMETRY

## Slide 13
Chip « inside »
7 “unit” PCB = A.S.U.
Interface card
Short sample
Connection between 2 PCB
90
1616 pixels (55 mm)
and below
PCB is critical :
1 mm tick, 8 layers,
1% flatness ,
chips bounded into
ACTIVE LAYERs

## Slide 14
 Gaps (slab integration) : 500 µm
 Heat Shield: 500 µm
 Thickness of BGA : 1700 µm
 PCB : ~1200 µm
 Thickness of Glue : 100 µm
 Thickness of SiWafer : 325 µm
 Kapton® film HV : 100 µm
 Thickness of W : 2100/4200 µm (± 80 µm)
TOTAL/ Active Layer : 3.8 mm
Level of Integration !!!!!
TUNGSTEN
VFE ASIC
PCB
Silicon
Carbon
fiber
PCB with Silicon diodes on one side
VFE and cooling plate on the other side
Heat shield
PCB
Silicon wafer
glue
Kapton film
Equivalent with scintillator strips
ACTIVE LAYERs

## Slide 15
At the extreme of integration :
Readout chip directly bonded on Silicon Wafers
KPIX
Gap ≤ 1 mm
ACTIVE LAYERs

## Slide 16
ACTIVE MEDIUM
A simple design to control the cost
  Few thousands of m² needed for ILD
  Glued on PCB : Floating Guard Rings
Drawbacks :
  Large dead zone at the edges (~1 mm)
  Crosstalk with GR
R&D in (if possible in collaboration with producers)
  Split GR and/or complete removal of GR
  Laser dicing : gain a factor 2 on dead zone
  Smaller size abutted matrices may improve yield
Simple Silicon Matrices
256 pixels of 5x5 mm²
Alternative - 1
SCINTILLATOR 45x5 mm² , read by SiPM
Seems promising
Need to be “validated”
by detailed comparison
data/MC (TB soon)
R&D on
Engineering model
overall cost estimation
Hexagonal silicon wafers
Alternative - 2
A mix up of Scintillator-silicon (Hybrid) . Interesting on paper (simulation)
CMOS – MAPS with digital readout (at a very preliminary stage, some first TB )
Resistive Glass - Micromegas (seems very promising but at the level of first simulation..)
Maximize the use of silicon wafers
Strips on surface to connect to readout
chip bump bonded on Si wafer itself

## Slide 17
Silicon Kalorimeter Integrated Read Out Chip
  Technology SiGe 0.35µm AMS. (7229 µm x 8650 µm)
  Production batch received Q3’10
  64 channels, variable gain charge amp, 12-bit ADC, digital logic
  Power-pulsed → 25 μW/channel
Power pulsing
  Variable current consumption according to state
  1 slab : 0 to 10 Amps pulses
  of 1 ms at 5 Hz
Readout for the ECAL with silicon diodes
SKIROC-2
KPIX
1024 channels intended to bump bond to Si detectors, optimized for the ILC (1 ms trains, 5 Hz rate):
  Low noise dual range charge amplifier w 17 bit dynamic range.
  Power modulation w average power <20 μW/channel (ILC mode).
  Up to 4 measurements during ILC train; each measurement is amplitude and bunch number.
  Digitization and readout during the inter-train period.
  Internal calibration system
  Noise Floor: 0.15 fC (1000 e- )
  Peak signal (Auto-ranging) 10 pC
  Trigger Threshold Selectable (0.1 – 10 fC)
READOUT CHIP

## Slide 18
S/N ~ 14
Test beam@DESY
Summer 2012
The scintillator strips version
TB at DESY (Oct. 2012)
Silicon ECAL – EHI (Extremely High Integration)
from US colleagues will start TB soon at SLAC
ILD within CALICE
LLR, LAL, LPNHE, LPC, LPSC, OMEGA,
Kyushu University, Tokyo University, Nippon Dental University, SKKU
ILD-CALICE,
Univ. Shinshu, SKKU
SiD coll.
SLAC, UO,
UCSD,BNL

## Slide 19
Developing a leakless water
cooling system
Total ECAL power dissipation O(10 kW) even at 25 µW/ch
Need active cooling system (cold water pipe + radiator), but OUTSIDE
Limit : temperature differences within ECAL
heat transfer to neighboring detectors
Thermal simulations of the full size module of the detector
Measurements in
the Tungsten-Cfi structure
Validation of the limit conditions for simulation
POWER DISSIPATION

## Slide 20
Project stages
 Concept
 Prototype test performances
Prototype scalable
 Engineering model
Optimization (cost vs perf.)
Project organisation (& funds)
Productions & Quality tests
construction & in-situ Integration
Trong Hieu Tran (LLR)
Trong Hieu Tran (LLR)

## Slide 21
SUMMARY -1
For the LC physics program, we need an ultra granular
electromagnetic calorimeter. (a Camera or FAST electronic bubble chamber)
R&D for 10 years leads to a version with High Level of Integration
Tungsten is the baseline for the radiator
Silicon diodes , scintillator strips for active medium (on 20-30 layers)
VFE ASIC inside detector with large number of channels/ASIC
The PERFORMANCE tests goes through RECONSTRUCTION program !!!
Single particle is important, but it is not the right test !!!!
Don’t use a camera to measure temperature !!

## Slide 22
SUMMARY -2
Not yet to the point where we can write
“we area ready to construct the ECAL”
a lot of VERY interesting R&D !!! JOIN US

## Slide 23
Not yet to the point where we can write
“we area ready to construct the ECAL”
a lot of VERY interesting R&D !!! JOIN US
BUT at the point where we can write
“we are approaching to be ready,
at least for a baseline version”
SUMMARY -2

## Slide 24
Not yet to the point where we can write
“we area ready to construct the ECAL”
a lot of VERY interesting R&D !!! JOIN US
BUT at the point where we can write
“we are approaching to be ready,
at least for a baseline version”
We even start the next step :
“ optimise …
cost, performance, industrial close contacts”
SUMMARY -2

## Slide 25
Le danger qui guette le chasseur
The danger which wait for the hunter

## Slide 26
BACK UP

## Slide 28
R&D for silicon wafers
Square pattern in wafer response
Xtalk with continous guardring <-> Pixel
Segmented guardring
Attenuation of Xtalk
dB
0
-30

## Slide 29
Calibration – Uniformity of Response
Calibration with with wide spread µ-beam
18 Mio. Events
Uniform response of all cells
only 1.4‰ dead cells
Differences in Response can
attributed to different
- Manufacturers
- Production series
Experience to deal with different
manufacturers and production series
Essential for final detector
~3000m2 of Silicon needed

## Slide 30
Stability of Calibration?
Important Criterium during evaluation process by IDAG
Affects both: precision and operability of detector: ~108 calo cells in ILC Detector
Calibration Constants on testbench and in beam test campaign
High Correlation between calibration constants
For “final” detector:
Detector modules can be calibrated in beam test prior to installation

## Slide 31
Example for SKIROC characterisation – Trigger efficiency

## Slide 32
Resolution on the charged track(s) ∆p/p ~ few 10-5
Resolution on the photon(s) ∆E/E ~ 12%
Resolution on the h° ∆E/E ~ 45%
In our detectors, the charged tracks are better measured than photon(s)
which are themselves better measured than neutral hadron(s)
Ejet fraction = Echarged tracks + E + Eh0
65% 26% 9%
PFA : « Particle Flow » Algorithm
2 jet = 2ch. + 2  + 2 h0 gives about 2 jet = (0.14)2 Ejet
With a perfect detector, no confusion between species and individual reconstruction
2confusion
2threshold
 Energy threshold to be rec. (depends on species)
 Mixing between particles in the calorimeter
Real life and
real detector
2efficiency
 loss of particles (not reconstructed)

## Slide 33
e+e–  W+W– at s = 800 GeV
Display from the true MC informations
With K0
Is it possible ?

## Slide 34
e+e–  W+W– at s = 800 GeV
Display from the true MC informations
Charged pads
photons
e+e-  W+W– at s = 800 GeV
Reconstruction
Display of the reconstructed event
With K0
Neutral hadron ECAL
Reconstruction