## Slide 1: Alignment challenges for a future linear collider

## Slide 2
OUTLINE
Introduction: alignment tolerances achieved for the LHC
Specifications for alignment of CLIC and ILC, and alignment challenges
Solutions being studied
    Long range alignment system
    Short range alignment system
    Fiducialisation
    Case of the Machine Detector Interface area
Conclusion

## Slide 3
Introduction : state of the art
Installation and determination of the Survey network
Transfer of reference into tunnel
Installation and determination of the tunnel network
Fiducialisation
Relative alignment of the elements: smoothing
Monitoring and remote adjustment in remote areas
Control and maintenance of the alignment
Absolute alignment
Steps of alignment of an accelerator
Injection of pilot beam
Implementation of beam based alignment and beam based feedbacks
Surface
Underground

## Slide 4
Introduction: state of the art (case of the LHC)
Fiducialisation
Relative alignment of the elements
Monitoring and remote adjustment in specific areas
Control and maintenance of the alignment
Absolute alignment
Operation during which the position of the fiducials is measured w.r.t. a reference axis (magnetic, mechanic)
 Uncertainty of measurement < 0.1 mm (1σ)
Initial alignment of each component w.r.t underground geodetic network  uncertainty of measurement < 0.3 mm (1σ)
Smoothing : relative position of components w.r.t to the trend curve  uncertainty of measurement < 0.1 mm (1σ) over 150 m
Monitoring of the relative displacements w.r.t a given reference time or position σ = a few microns using alignment systems and remote adjustment using motorized jacks

## Slide 5
Specification for ILC & CLIC
Area | Nb of beam | Error of misalignment on the fiducials (1σ)
Main linac | 1 | 0.2 mm rms over 600 m
BDS | 1 | 0.02 mm over 200 m
Fiducialisation: : 0.05 mm rms
Above state of the art for ILC:
Above state of the art for CLIC:
The zero of each component will be included in a cylinder with a radius of a few microns:
14 μm over 200 m (RF structures)
17 μm over 200 m (MB quadrupoles)
10μm over 500m (BDS and final focus components)
Adjustment required: step size below 1 µm
Special case of main linac and BDS

## Slide 6
Alignment challenges for a future linear collider
Fiducialisation
Smoothing
Active pre-alignment for CLIC
Active determination of the position for ILC
Stable alignment reference, known at the micron level
Submicrometric sensors providing « absolute » measurements
Measure objects within a few microns
Submicrometric displacements along 3/5 DOF
replaced by
Up to a few microns
Long range alignment system
Short range alignment system
Fiducialisation at a micron level

## Slide 7
Special case of MDI area
Taking into account:
Push pull detectors
Last component (QD0) inside the
detector (L*=3.5m)
Requirements (CLIC):
Determination of left reference line w.r.t right reference line : within ± 0.1 mm rms
Monitoring of left reference line w.r.t right reference line : within a few microns
Monitoring of the position of left QD0 / right QD0 within ± 5 μm rms

## Slide 8
Long range alignment system
As it is not possible to implement a straight alignment reference over kilometers:  use of overlapping references

## Slide 9
Long range alignment system
Stretched wire
Laser beam under vacuum
Reference over hundreds of meters
(n - points)
(3 - points)
Raschain
Λ-system
Solution consisting of overlapping stretched wires and WPS sensors chosen for CDR of CLIC and RDR of ILC
Wire Positioning Sensors (WPS)

## Slide 10
Main issue: long term stability of a wire
        (effects of temperature, humidity, creeping effects, air currents)
    Modelization of the wire using Hydrostatic Levelling Systems (HLS)
  but only in the vertical direction
  but HLS system follows the equipotential of gravity which needs then to be known
   studies undertaken concerning the determination of the equipotential of gravity
  Subject of a PhD thesis:
  « Determination of a precise gravity field for the CLIC feasibility studies »
Long range alignment system
Stretched wire
Notes: Se

## Slide 11
Position & orientation of the metrological plates in the coordinate system of the tunnel
Monte Carlo method using theoretical readings of sensors
 in 97.5% of the cases, all the pre-alignment errors fit in a cylinder with a radius of 10 µm.
TT1 facility
One of the objectives  to determine the precision and accuracy of a reference network consisting of overlapping stretched wires.
Simulations
Long range alignment system

## Slide 12
Results in TT1
    Precision on a 140 m wire: better than 2 microns over 33 days
    Accuracy: 11 microns in vertical, 17 microns in radial. Can be improved!
  Vertical residuals of the 2 longest wires:
    σ (wire 1) = 1.6 µm
    σ (wire 2) = 0.5 µm
  Accuracy of the TT1 network adjusted by the least squares method in vertical:
    σ = 11 µm r.m.s (27 µm max. value)
Long range alignment system

## Slide 13
Long range alignment system
Development of laser based alternatives
Basic laboratory experiments with low cost elements and simple methods done at short distance (about 2 m)
Measurement repeatability within an interval of
[−4 μm,4 μm] around the mean values
Standard deviation less than 5 μm
Latest achievements on λ- system:
First simulations performed: angular orientation & repeatability of shutter should be better than 0.2 mrad and 12 μm in order to detect a micrometric displacement
Latest achievements on RasDif:
First configuration installed successfully in 2009
  Resolution below 0.1µm
  Appears to behave as a very precise seismometer
Double configuration showed non coherent results
 inter-comparison needed with WPS

## Slide 14
Short range alignment system
Issue: WPS sensor fulfilling the requirements
    « absolute measurements » (known zero w.r.t mechanical interface)
    no drift
    sub micrometric measurements
Optical based WPS (oWPS)
Capacitive based WPS (cWPS)
Upgrade of an existing WPS
Development of a new WPS
WPS (Wire Positioning Sensor)

## Slide 15
Short range alignment sensors
Sensors : cWPS
60 sensors installed in the LHC on the low beta triplets
Rad Hard (sensors up to 300 kGy, Remote electronics up to 50 kGy)
Resolution: 0.2 µm
But relative measurements only!
Latest achievements:
An isostatic mechanical interface allowing a repositioning within 1µm and an absolute calibration has been developed
A very accurate linearity bench
An « absolute » bench
Dedicated lab with a temperature stable within ± 1ºC
Status / current issues:
Linearity depends of the generation of carbon peek wire used: < 5 μm over the whole range (better in middle range)
Repeatability & interchangeability < 1μm
Accuracy (“absolute calibration”) of cWPS < 20 μm (bench recalibrated last week in the metrology lab).

## Slide 16
Short range alignment sensors
Sensors : oWPS
Main characteristics (from the manufacturer)
Resolution: < 0.1 μm
Range : +/- 5 mm (along two axes)
Repeatability: 2μm
Accuracy : < 5μm
Wire: Vectran
Latest achievements:
A very accurate linearity bench
A vectran wire (manufactured fiber spun from a liquid crystal polymer) visible to infra-red light and not antistatic  silver plasma coated wire.
Status
Resolution < 1 µm, interchangeability < 5 µm
Noise problem to be solved
Impact of temperature: ~ 6µm/°C to be corrected
Absolute calibration to be controlled.

## Slide 17
Short range alignment sensors
Sensors : RasChain
2 possibilities: RasNik versus RasDif
Status:
Test setup to validate RasNik & Rasdif on 4 m
First results: jitter and refractive bending of light  thermal shielding needed
Preparation of sensors for two beam modules and inter-comparison tests with other sensors
RasNik
RasDif

## Slide 18
Fiducialisation
  Laser tracker: AT 401
  Micro triangulation
  Romer arm
Most accurate but for very short components
 Development of portable means
MPE = 0.3 µm + L/1000 (L in mm)
First solution: CMM measurements (dimensional control, pre-alignment of components on their supports, fiducialisation), but STATIC
Latest achievements:
Fiducials developed
Several means developed and validated:
  AT401 ~ 5µm @ 2m
  Micro triangulation ~ 5µm @ 2m
  Romer arm ~ 10 µm @ 2m
Test of fiducialisation strategy:
  Very precise for short objects on CMM
  Accuracy ~ 20 µm on 2m long objects

## Slide 19
Special case of MDI area
Monitoring on both sides of the detector:
No direct line of sight at the level of the beam
Status and next steps :
A mock-up real size will be built @CERN to validate the whole concept
Design ready
External line of sight at 3m in “dead space”
Spokes equipped at both ends by alignment sensors linking the components and line of sights

## Slide 20
MDI area
Link between left and right sides:
Parallel survey galleries
Laser system shielding coupled to the push-pulled detector
Next steps:
Distance reference to reference : means to be developed
N-point laser based alignment system over ~ 100 m to be developed

## Slide 21
Conclusion
In comparison with alignment requirements of the LHC, the alignment of linear colliders is a real challenge, with precision and accuracy of a few microns over several hundreds of meters, including the fiducialisation process.
Solutions are under development concerning long range alignment system:
  A stretched wire solution has been proposed for the RDR of ILC and CDR of CLIC.
  Results from test setup have shown that an uncertainty in the determination of the position of a sensor over 140m is of the order of 11 μm.
  Alternatives, based on laser beam under vacuum, are under development, first to validate the stretched wire solution, and why not to replace it.
Short range sensors are under development as well, and the latest results show that an accuracy below 5 μm and a repeatability below 1μm are reachable.
Fiducialisation at a micron level is a challenge too, with a level of difficulty depending of the size of the component. For very short components (length <1m), CMM are a must, but will need to be replaced by portable means that are under development and validation.
CONCLUSION