## Slide 1: Detector Calibration Concepts and Status of the Calibration Working Group
Jola Sztuk-Dambietz (XFEL)
on behalf of
the Calibration Group
November, 19th 2012 13th Meeting of the XFEL Detector Advisory Committee
European XFEL GmbH, Hamburg
Notes: How to edit the title slide
Upper area: Title of your talk, max. 2 rows of the defined size (55 pt)
Lower area (subtitle): Conference/meeting/workshop, location, date, your name and affiliation, max. 4 rows of the defined size (32 pt)
Change the partner logos or add others in the last row.

## Slide 2: Outline
Introduction
Detector calibration group – status update
Highlights from the last Calibration Meeting
Infrastructure for detector calibration and tests
Calibration software – status update
Summary & plans

## Slide 3
3
Calibration Working Group – Update
Structure of the group:
Physicist for Software Development
S. Hauf started in September:
interface to and support of external detector consortia in terms of calibration and data analysis software
develop and maintain:
calibration software & calibration data base for imaging detectors
detector-specific data analysis and image processing algorithms
detector response & performance simulation software
Meetings: every 6 months
 next meeting in March

## Slide 4: Highlights From the Last Calibration Meeting (I)
Last calibration meeting took place in September
Participants: Consortia, XFEL WP-75 and WP76 representatives
Status of calibration activities in the consortia and XFEL was shown:
AGIPD:
Memory droop:
  @ room temperature, a droop effect smaller than 4 % up to 100ms was observed
  Further steps: dependence of droop effects on temperature and irradiation

## Slide 5: Highlights From the Last Calibration Meeting (II)
DSSC: calibration of DSSC prototype
DSSC prototype = pxd-7 prototype + ASIC prototype
Two independent scans of pixel characteristic:
pulsed internal charge injection via inner substrate contact
pulsed LED
Software development is ongoing in parallel to experiments and covers all calibration steps.
Calibration of non-linear system gain (NLSG) for 1 keV photons
First step: scan the linear region with 55Fe and fit the 8-bit 55Fe spectrum using a spectral model obtained from the high resolution 14-bits ADC
Second step: scan the dynamic range of the prototype system, both linear and non-linear region, by pulsed charge injection and calibrate charge injected per pulse by comparison to 55Fe signal
preliminary

## Slide 6
LPD: Characterization of two-tile system (memory droop, gain variation, offset)
LPD
Infrastructure requirements for the calibration and characterization of the LPD systems were defined
First version of calibration document (calibration concept ) is available
A two-tile system will be delivered to the XFEL in Q4 2012.
Memory leakage is not an issue
<< Memory and ADC noise
Offset and dead pixels
Gain variation
Memory droop
 More details in the consortia talks at the general and closed sessions
Highlights From the Last Calibration Meeting (III)

## Slide 7: Highlights From the Last Calibration Meeting (IV)
XFEL:
Status of the test infrastructure at the XFEL  see later in the talk
Status update of the XFEL scientific framework (Karabo)
  Work on a software framework for distributed applications is ongoing  serves control framework and data analysis framework.
  Initial version to be distributed to the consortia in Q2/Q3 2013 (mandatory !!!)
  Calibration constants and files will be stored in HDF5 files and included in the XFEL database
   Work on definition of data format, structure and data base is ongoing
   First stable version needed in mid-2013

## Slide 8: Calibration Status – update
Activity | AGIPD | DSSC | LPD
Noise performance study |  |  | 
Characterization of memory cell droop after irradiation & at different temperatures |  | Not applicable | Not an issue
Develop strategy for non-linear gain response | Not applicable |  | Not applicable
PSF measurement |  |  | 
QE measurement |  |  | 
Optimization of calibration strategies with test structures | AGIPD0.1-0.4 | pxd-7+ASIC | Two-tile system
Optimization of calibration strategies with simulation |  |  | 
Performance characteristic
ready
ongoing
to be done

## Slide 9: Calibration Concept & Infrastructure Requirements
Requirements for calibration infrastructure were defined
Proposal for parameters to be calibrated or characterized was prepared
Requirement document including proposal for responsibilities assignment was distributed to the Consortia
 feedback from the Consortia by the end of November

## Slide 10: Proposal for Responsibilities/Work Assignment
Calibration group is responsible for calibration and characterization of all detectors at XFEL
For detectors not developed by external developers the calibration methodology and tools (software + infrastructure) shall be developed by WP-75
External developers shall provide calibration procedures and develop the methodology taking into account the following requirements:
  The methodology shall be reproducible in the XFEL environment (laboratory or at the XFEL beamlines).
  The calibration and characterization software has to be compatible with the XFEL scientific software framework (Karabo) and developed in close cooperation with the XFEL WP-75 and WP-76 groups.
WP-75 shall be responsible for the calibration software integration in the XFEL framework.

## Slide 11: Proposal for Responsibilities/Work Assignment
WP-75 shall take over the calibration responsibility from the consortia as soon as the detectors are assembled in the XFEL experimental environment. Mandatory for the efficient transfer of information and responsibilities:
    an early involvement of WP-75 in the test (calibration/characterization) activity
    test devices for each technology at the XFEL to start with integration and test measurements as early as possible
WP-75 shall provide the infrastructure needed for detector calibration and characterization at the XFEL including the infrastructure requirements from the detector consortia
DAQ and control system shall be provided by WP-76
Definition of the data format and solutions for data management shall be developed by WP-76 in cooperation with WP-75

## Slide 12: PETRA III - almost ideal calibration X-ray source
PETRA III:
40-bunch mode at 5.2 MHz (34, 60-,240-bunch modes possible)
High-intensity (104-106 photons/pulse) monochromatic beam
Pink beam (108 photons/pulse)
Photon energy covers XFEL requirements
Regular access to PETRA should be established  common effort XFEL & consortia
PETRA III access:
Standard user procedure proposals
  Proposal for PETRAIII (1st half of 2013) has been accepted  application for beam time has been sent  outcome in November
“Unofficial” procedure:
  PETRA beamline scientists interested in testing new technologies develop for the XFEL has been contacted

## Slide 13: Laboratory Infrastructure for “in situ” Detector Tests
Synchrotrons/FELs – almost ideal calibration X-ray source, BUT
Limited access  cannot be used on a daily basis
Detector setup has to be transported  risky and time consuming
Time structure of the beam not always appropriate
Iron-55 setup ( radioactive source + housing)
electrodeposited as Fe metal on the face of a Cu substrate with protective Ni layer
Nominal activity: 1.85 GBq (>36x106 photons/s per steradian)
First design of source housing (operation in ambient and vacuum) ready
Work on safety regulations finished  application accepted by HH authority
 First X-ray setups available in Q1/Q2 2013
First Alternatives:
Amptek Mini-X setup (X-ray tube + detector test chamber)
50 kV/80 μA power supply, Ag or Au transmission target, Be end window
Filters: Al, Cu, Mo, Ag, W
Vacuum feedthrough coupling

## Slide 14: Multi-Target X-ray Generator Setup
Work on TDR started  X-ray generator setup foreseen Q3 2014
Laboratory Multi-target X-ray generator setup for detector characterization and calibration
  complementary to synchrotrons and FELs on daily use
  electron source for direct electron illumination
Main components:
Pulsed electron source:
  30 < Ee < 100 keV
  Current nA < Ibeam< 20 A
  Pulse width: ~ 20ns - 100 ms
Multi-target anode  X-ray energies (0.2-25 keV)
X-ray optics (filters, monochromator, focusing optics, collimator,..)
  monochromatic beam
  beam spot down to 20mm
  collimated beam with size range from a few mm to 10 cm
Chopper (optional)
Detector test chamber
Reference detector

## Slide 15: X-ray Generator - GEANT4 Simulation
Optimization of X-ray generator setup parameters using GEANT4 simulation*
  target material and angles
  filter material and thickness
  beam current
  geometry
Estimation of beam intensity
Shielding definition
Input to TDR
Courtesy S. Hauf
Coordinate definition:
Work on simulation of X-ray source started  first version of the software is ready
Geometry definition:
Electron gun
Target
Virtual detector
Detector
Collimator
Filter
* Code validation based on arXiv:1205.1973

## Slide 16: Different Targets - Comparison
Simulation parameters
20 M primary e-
 3.2 x 10-12 sec @ 1A*
Ee=100 keV
Target materials:
Cr, Cu, Mo…
Target angle: a =18°
* 1 A = 6.2415 x 1018 electrons/sec.
Efficiency of X-ray production ~ 1-2 %

## Slide 17: Different Electron Energies - Comparison
Simulation parameters
20 M primary e-
Ee=50,100,160 keV
Target materials: Cu, Fe, Ag…
Target angle: a =18°
Cu
Fe
Ag

## Slide 18: Calibration Software Development at WP-75 (S. Hauf)
Calibration Analysis and Application within the Karabo-Framework
Currently, implementation of calibration pipeline for test detectors is proceeding  First steps for 2D-detector calibration on dark images (status report by S. Hauf in subsequent session)
Direct feedback from/ to WP-76 regarding feature requests and improvements
Will lay path for user training and integration of consortia-developed software
Feedback from the Consortia on the type and status of the software activities was provided
Notes: Before you start editing the slides of your talk change to the Master Slide view:
Menu button “View” > Slide Master:
Edit the following items:
1. On the Title slide (second master slide)
a) Click to add title of your talk
b) Click to add subtitle (conference, location, name of the speaker, date)
2. On the Slide Master (first master slide)
a) The 1st row in the violet header: Delete the existent text and write the title of your talk into this text field b) The 2 rows in the footer area: Delete the text and write the information regarding your talk (same as on the Title Slide) into this text field.
Close Master View

## Slide 19: Karabo Readiness of Consortia Software
 | AGIPD | LPD | DSSC
Pipeline | NO | NO | PARTIAL
File format | ROOT, ASCII | BINARY | ROOT, ASCII
Language | C++ | PYTHON | C++
Dependencies | ROOT | Numpy | ROOT
 |  | Scipy | (MEGALIB)
 |  | Matplotlib | 
Plot production | MANUAL | MANUAL | SEMI-AUTO
Multiprocessing/Threading* | NO | NO | NO
Computing on GPU* | NO | NO | NO
KARABO - Readiness |  |  | 
Current assessment based on feedback from consortia
Note!: Karabo is currently not available outside XFEL  assessment reflects design compatibility with Karabo but critical
* Not necessary critical but favorable
Internal work for pnCCD will be used as example implementation alongside guidelines
Computational performance not assessed yet but critical (usability for 1M pixel device?)
Notes: Before you start editing the slides of your talk change to the Master Slide view:
Menu button “View” > Slide Master:
Edit the following items:
1. On the Title slide (second master slide)
a) Click to add title of your talk
b) Click to add subtitle (conference, location, name of the speaker, date)
2. On the Slide Master (first master slide)
a) The 1st row in the violet header: Delete the existent text and write the title of your talk into this text field b) The 2 rows in the footer area: Delete the text and write the information regarding your talk (same as on the Title Slide) into this text field.
Close Master View

## Slide 20: Schedule
to be discussed

## Slide 21: Schedule
First X-ray sources at XFEL
Data Base & Data format ready for use
First lab. prototypes at the XFEL
Calibration Software for CCDs
to be discussed

## Slide 22: Summary
Work on calibration is ongoing in the Consortia and discussed in regular meetings
Setup of the calibration infrastructure is ongoing  Fe-55 source and a portable X-ray tube will be available in Q1/Q2 2013
Work on calibration software and simulation at the XFEL started
X-ray generator concept being elaborated  first simulation is available
First attempt to access PETRAIII was done  regular access to PETRAIII requires a combined effort of XFEL and consortia

## Slide 23
Answers to the Questions
of the XDAC
Committee

## Slide 24: Comments from the last XDAC report
“The XDAC appreciates the start of the activities of the calibration working group and encourages the efforts initiated to define an action plan. In that sense it suggests to look into methodology in which the responsibilities of the various actors are well defined”
Proposal for responsibility/work assignment was included in the technical note “Calibration Concept and Infrastructure Requirements” and distributed to the consortia for comments. Feedback is expected by the end of November.
“It would be convenient to have easy and regular access to a test station at a storage ring facility that could deliver X-ray photons with a time structure and intensity to the values expected to be seen by the XFEL detectors. Such a station could be used for both testing and calibration for all detectors. An option to be explored could be setting up a long term agreement with a SR facility with the a appropriate modes (few bunch filling with the right timing).’’
First step was done slide 12 of this talk
Next step: regular Access to PETRA should be established including common effort XFEL & consortia. In addition we planning detector tests at different light sources (LCLS, ..)
“Eventually calibration and alignment devices have to be integrated into the beam line, and so an early generic layout seems helpful for further discussion.”
The mentioned devices are planned at the beamlines and will be included in the instrument TDRs.

## Slide 25
Backup slides

## Slide 26: Detectors to be calibrated & characterized - reminder
2-D Mpixel X-ray imaging detectors
..and more to come
  1D detectors
  Avalanche PhotoDiode (APD)
  Silicon Drift Detector (SDD)
  …
High repetition rate detectors: AGIPD, DSSC, LPD
Low repetition rate detectors:
pn CCD, other CCDs
LPD
pn CCD

## Slide 27: X-ray Generators - Requirements
X-ray source(s) for detector calibration & characterization purpose
Photon energy: Energy range 0.2-25 keV, monochromatic
Time structure:
- pulsed source with repetition rate if possible up to 4.5MHz or at least
two pulses delivered with Dt=220 ns
- short pulses <1ps
Adjustable and stable intensity (1ph/pixel/pulse – 104ph/pixel/pulse)
Two types of illumination:
- point-like illumination (ideal case: possibility for one pixel illumination)
- flat field illumination with homogeneity of the order of 10% (ideal
case: size of the flat field compatible with the size of the full
detector module: 20x20cm, or as large as possible)
Well calibrated reference detector
Vacuum/ambient compatibility

## Slide 28: X-ray Generator Setup
X-ray generator setup with different targets and filters for detector characterization
Description | Material | Thickness
Multilayer Thin | Al Polyimide | 40 nm 160nm
Multilayer Medium | Al Polyimide | 80 nm 160 nm
Multilayer Thick | Sn Al Polypropylen Al | 45 nm 55 nm 330 nm 55 nm
Al Thin | Al | XX nm
Al Think | Al | XX nm
Cu Thin | Cu | XX nm
Cu Thick | Cu | XX nm
Ni Thin | Ni | XX nm
Ni Thick | Ni | XX nm
Target material |  | Emission Line Energy [keV] |  |  |  |  | 
Z | Symbol | Ka1 | Ka2 | Kb1 | La1 | La2 | Lb1
6 | C | 0.277 |  |  |  |  | 
12 | Mg | 1.25 | 1.25 | 1.30 |  |  | 
13 | Al | 1.49 | 1.49 | 1.56 |  |  | 
8 14 | O Si | 0.525 1.74 | 1.74 | 1.84 |  |  | 
22 | Ti | 4.51 | 4.50 | 4.93 | 0.452 | 0.452 | 0.458
24 | Cr | 5.41 | 5.41 | 5.95 | 0.573 | 0.573 | 0.583
26 | Fe | 6.40 | 6.39 | 7.06 | 0.705 | 0.705 | 0.719
27 | Co | 6.93 | 6.92 | 7.65 | 0.776 | 0.776 | 0.791
28 | Ni | 7.48 | 7.46 | 8.26 | 0.852 | 0.852 | 0.868
29 | Cu | 8.045 | 8.027 | 8.905 | 0.929 | 0.929 | 0.950
42 | Mo | 17.48 | 17.38 | 19.61 | 2.29 | 2.29 | 2.39
47 | Ag | 22.16 | 21.99 | 24.94 | 2.98 | 2.98 | 3.15
74 | W | 59.32 | 57.98 | 67.24 | 8.40 | 8.36 | 9.67
79 | Au | 68.80 | 66.99 | 77.98 | 9.71 | 9.63 | 11.44
 | Makrolon (ceramics) | 0.52 | 0.68 | 0.93 | 1.25 | 1.49 | 1.74
 |  | 2.62 | 3.31 | 3.59 | 6.40 | 7.06 | 8.04
Filters
Targets