## Slide 1: Studies for Particle Driven Plasma Acceleration at PITZ
Experiments planned utilizing PITZ (Photo Injector Test facility at DESY, Zeuthen site)
Matthias Gross
Helmholtz Virtual Institute on Plasma Acceleration Meeting
SLAC, 8. October 2012

## Slide 2: Contents
Introduction
Unique positioning of Photo Injector Test Facility (PITZ)
State of development of plasma cell experiment
Outlook: high transformer ratio

## Slide 3: DESY, Location Zeuthen
Former Institute for High Energy Physics in Zeuthen (Academy of Sciences of the GDR). Was merged with DESY on 1st January 1992
200 employees of which 50 are scientists

## Slide 4: Photo Injector Test facility at Zeuthen – PITZ
Goals & research activities
  Study, development, characterization and conditioning of electron beam sources for FLASH and the European XFEL
  Testing new developments e.g. laser system, accelerating structures (e.g. PWA), deflecting structure, cathodes, and beam diagnostics
History – some highlights
  1999: DESY directorate decision to build PITZ in Zeuthen
  2002: 1st photoelectrons produced
  2005: 10 MW Multi Beam Klystron (MBK)
  2006: Three emittance measurement systems (EMSY)
  2008: New Yb:YAG photocathode laser system
  2009: New Cut Disk Structure (CDS) booster – Maximum beam energy: 25 MeV
  2010: 10 MW In-vacuum directional coupler and a new LLRF system
  2012: Deflection cavity and 3rd dispersive arm HEDA2

## Slide 5
current PITZ 2.0 setup

## Slide 6: Background
Courtesy of Carl Schröder, LBNL
Does this work ?
Dephasing ?
Hose instability ?
Background:

## Slide 7: Why Experiments at PITZ?
Favorable circumstances
  Pure R&D facility (no users)
  Unique laser system (pulse shaper)
  Well developed diagnostics (high resolution electron spectrometer, etc.); soon: transverse deflecting cavity + dispersive section for longitudinal phase space measurements
Possible contribution from PITZ:
  Self modulation of electron beam
  Later: High transformer ratio (needs bunch compressor)

## Slide 8: Flexible Laser Pulse Formation at PITZ
Photoinjector laser
Developed and built by Max-Born Institute Berlin
Key element: the pulse shaper
  Contains 13 birefringent crystals. Pulses are split according to polarization. Delay is given by crystal thickness; relative amplitude can be varied freely by adjusting relative angle between crystals
Gaussian input pulses
Shaped ouput pulses
Will, Klemz, Optics Express 16 (2008) , 4922-14935
motorized rotation stage
temperature controlled birefringent crystal
birefringent shaper, 13 crystals
FWHM = 25 ps
edge10-90 ~ 2.2 ps
edge10-90 ~ 2 ps
birefringent shaper, 13 crystals
OSS signal (UV)

## Slide 9: Experimentally Demonstrated Pulse Shapes
Driver + witness bunch
Modulated driver + witness bunch
Modulated driver
Multi bunches

## Slide 10: PIC (Particle in Cell) Simulation of PITZ Experiment
Simulations:
Alberto Martinez de la Ossa
PITZ resolution window
Expected energy modulation 600 keV. PITZ beam energy spread as low as 60keV. Resolution of TDS/HEDA2: 10keV and 100m (Malyutin et al. “Simulation of the Longitudinal Phase Space Measurements With the Transverse Deflecting Structure at PITZ”, Proc. of IPAC 2012, MOPPP034  Measurable
Beam parameters | Setup 1
Total charge, pC | 100
Longitudinal beam position, m | 6.35
Horizontal rms beam size, um | 49.8
Vertical rms beam size, mm | 51.2
Bunch length in FWHM, mm | 5.92
Average kinetic energy, MeV | 24.55
Rms energy spread, keV | 27.5
Peak slice current, A | 5.2
Horizontal rms emittance, mm mrad | 0.37
Horizontal beam divergence, mrad | 0.008
Vertical rms emittance, mm mrad | 0.38
Vertical beam divergence, mrad | 0.002
Longitudinal rms emittance, keV mm | 42.4
Peak beam density, 10^12 e / cm^3 | 9.1

## Slide 11: Lithium Plasma Cell
Principle:
  Evaporate Lithium in central pipe (700°C)
  Define beginning and end of Lithium zone with steep temperature gradient and Helium buffer gas
  Once pressure regions have stabilized:
    Ionize Lithium gas with laser (Photoionization with ArF or field ionization with Ti:Sa)
    Inject particle beam for PWA experiment
Figure from: P. Muggli et al. “Photo-Ionized Lithium Source for Plasma Accelerator Applications”, IEEE Trans. Plasma Science 27 (1999), pp. 791-799

## Slide 12: Optics for Laser Plasma Generation
Axicon for homogeneous ionization profile
  Adjustable aperture to define length of plasma channel
Simple focusing mirror
  Length of plasma channel defined by Li gas volume
e- beam
Aperture
e- beam
Plasma channel
Li gas
Li gas

## Slide 13: Simulation: Scenarios for Plasma Cell Insertion
Schematic views
Electron beam rms size
  More complex beam focusing for setup 2
Setup 1
Setup 2
Simulations:
Martin Khojoyan

## Slide 14: Simulation: Beam Properties
Beam properties for Setup 1 (Imain = 363A) Comparison of setups
Setup 1: beam properties acceptable. Smaller beam size, less divergence, higher peak density – overall preferable
Beam parameters | Before dipole | After dipole
Total charge, pC | 100 | 100
Longitudinal beam position, m | 6.35 | 9.45
Horizontal rms beam size, um | 49.8 | 59.4
Vertical rms beam size, mm | 51.2 | 59.4
Rms bunch length, mm | 1.71 | 1.71
Bunch length in FWHM, mm | 5.92 | 5.92
Average kinetic energy, MeV | 24.55 | 24.55
Rms energy spread, keV | 27.5 | 27.8
Peak slice current, A | 5.2 | 5.2
Horizontal rms emittance, mm mrad | 0.37 | 0.38
Horizontal beam divergence, mrad | 0.008 | 0.09
Vertical rms emittance, mm mrad | 0.38 | 0.36
Vertical beam divergence, mrad | 0.002 | 0.13
Longitudinal rms emittance, keV mm | 42.4 | 42.4
Peak beam density, 10^12 e / cm^3 | 9.1 | 6.6
Simulations:
Martin Khojoyan

## Slide 15: Plasma Cell Assembly: Sketch
Electron
Beam /
Laser
Design:
Gerald Koss
Plasma cell
Preliminary Version
Screen stations
Quadru-
poles

## Slide 16: Multi Bunches: High Transformer Ratio
Plasma Acceleration: e.g. 5 bunchlets within bunch  transformer ratio >2
Longitudinal laser profile at the cathode
10pC 30pC 50pC 70pC 10pC
ASTRA simulations through gun and booster up to z=5m
Setup: - use PITZ2 beamline with gun, booster, and matching quads up to z=7m
  - install a short bunch compressor (dogleg)
use Elegant for matching
and the dogleg design (ongoing)
Longitudinal phase space at z=5m
Parameters:
Q = 170 pC in 5 pulses
100 000 particles
Gun phase: 10 deg
Booster phase: 40 deg
BC layout:
compression factor C = 4
R56 = 0.15
Total length l = 1m
dipoles: r = 0.6m, α = 60 deg
D1
D2
Q1
Q2
Q3
S1
S2
l=1m
Design with 2 doglegs (↑↓) on the way
Simulation by Anne Oppelt

## Slide 17: Very Preliminary Results: Needs Optimization
~λp
Driver bunch
Witness bunch
Energy gain!
Bunches at the beginning:
Bunches after 1 cm in plasma:
The witness bunch falls in the region where the wakefield is maximum.
In approx. 1 cm of propagation in the plasma, a fraction of the electrons in the witness bunch double their energy.
/n0
Driver bunch
Witness bunch
Simulation by Alberto Martinez de la Ossa

## Slide 18: Outlook
2013: First experiments with plasma cell
2014: Characterization of energy modulation of electron beam in plasma
Then: Insertion of bunch compressor – experiments with high transformer ratio etc.
Cooperation with SLAC, CERN etc.

## Slide 19: Summary
PWA Experiments are planned at PITZ
  Now: Characterization of electron beam self modulation
  Later: High transformer ratio
Utilization of good diagnostics and unique laser system
Simulations show promising results
  Electron sub bunching and energy modulation with current setup
  Energy gain with bunch compressor
Current main work
  Detailed plasma cell design
  Insertion of plasma cell into PITZ beam line

## Slide 20
Backup

## Slide 21: How to Increase the Transformer Ratio