## Slide 1: MSK Collaboration Meeting Advanced Techniques in LLRF control for XFEL 19-21 February 2013, Otwock-Swierk
Presented by: Christopher Gerth
XFEL WP18 Hardware requirements and schedule
Notes: How to edit the title slide
Fill in the text written in brown

## Slide 2: Scope of WP-18
Scope of WP-18 Special Diagnostics:
  Distribution of fs-stable optical timing signals and measurement of
  longitudinal momentum (beam energy), bunch length and bunch arrival time.
Energy change (x 100) after accelerating sections: I0, L1, L2, L3
Bunch length change (x 100) after bunch compressors: BC0, BC1, BC3
Bunch arrival change after dispersive sections: BC0, BC1, BC3
E = 0.15 GeV
σs = 2 mm
Ipeak = 50 A
E = 0.6 GeV
σs = 0.1 mm
Ipeak = 1 kA
E = 2.0 GeV
σs = 0.02 mm
Ipeak = 5 kA
E = 17.5 GeV
σs = 0.02 mm
Ipeak = 5 kA
L1
L2
L3
I0
BC0
BC1
BC2
E = 0.15 GeV
σs = 1 mm
Ipeak = 50 A
  => Complex systems of which only very few items will be installed!
Notes: Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of the EoI for WPnumber 2) The row in the footer area: write the institute name
Close Master View

## Slide 3: Overview on devices
femtosecond optical
timing distribution
MLO – master laser oscillator
FSD – free-space distribution
OXC/RF Link – stabilized links
L2RF
RF
Synchronization
L2L
Laser
Synchronization
BAM
Bunch Arrival
Monitor
Synchrotron
Radiation
Monitors
SRM
Energy BPM
EBPM(1)
Bunch arrival
Beam energy
Beam Energy
Energy profile
Beam energy
Beam energy
Bunch arrival
EO
Diagnostics
EOD
Coherent
Radiation
Diagnostics
CRD
Transverse
Deflecting
Structure
TDS(1)
Bunch profile
Compression
Bunch profile
Bunch profile
Slice emittance
Phase space
Bunch profile
1)
High-Power RF system and TDS are part of contract between European XFEL GmbH and Inst. for Nuclear Research (INR).
Suite of devices required to cover full range of beam energies and bunch lengths
Optical Synchronization System about half of the WP (cost, personnel)
TDS System largest diagnostic device
Notes: Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of the EoI for WPnumber 2) The row in the footer area: write the institute name
Close Master View

## Slide 4: General Comments and Generic Layout
4
WP18 in comparison to the LLRF system: Only very few devices of a large variety of complex systems
Reduce development costs and achieve 20 years maintenance => Try to use commercial parts or hardware of ‘big brother’ LLRF => Try to use same hardware for all devices where possible
=> Partyline: First get series production of LLRF systems finished but try to incorporate specs of WP18 where possible.
Vacuum
setup
Signal conversion to electrical signals
Control of Hardware
Signal detection
Computation
FB
Notes: 4
Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of your talk into this text field 2) The 2 rows in the footer area: Delete the text and write the information regarding your talk (same as on the Title Slide) into this text field.
If you want to use more partner logos position them left beside the DESY logo in the footer area Close Master View

## Slide 5: Overview TDS
5
TDS: disk-loaded travelling wave structure
MSK is responsible for the LLRF System: LLRF system for single cavity regulation ( 1 – 4 μs, Struck SIS8300 + DWC) but at special frequency.
The High-Power RF system and Transverse Deflecting Structures are part of contract between European XFEL GmbH and Inst. for Nuclear Research (INR), Troitsk, Russia.
Prototype system to be build at PITZ at DESY Zeuthen.
PITZ Prototype
Notes: 5
Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of your talk into this text field 2) The 2 rows in the footer area: Delete the text and write the information regarding your talk (same as on the Title Slide) into this text field.
If you want to use more partner logos position them left beside the DESY logo in the footer area Close Master View

## Slide 6: TDS Measurement Principle and choice of Frequency
View screen
“Streak Strength (Shear Parameter):
Vy : TDS Voltage => Powerful commercial klystron
ω : TDS Frequency => As high as possible
Wakefields => Iris > 40 mm => TDS Frequency < 4GHz
=> S-Band at around 3 GHz
Notes: Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of the EoI for WPnumber 2) The row in the footer area: write the institute name
Close Master View

## Slide 7: TDS Frequency
LOLA : fTDS = 2.856 GHz => ~ 100 deg phase change per bunch at 1 MHz)
TDS: fTDS = 332 · fMO = 332/144 · f1.3GHz
fTDS = 2 · f1.3GHz + 1/3 · f1.3GHz - 1/12 · (1/3 · f1.3GHz) = 2997 MHz
fLO = 2 · f1.3GHz + 1/3 · f1.3GHz = 3033 MHz
=> fIF = 36 MHz
fCLK = 81 MHz
Find frequency that is a harmonic of fMO = 9 MHz and can be generated from the 1.3 GHz:

## Slide 8: Specification FGB
Notes: Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of the EoI for WPnumber 2) The row in the footer area: write the institute name
Close Master View

## Slide 9: Frequency Generation Box (1): DESY Prototype
Bottom View
Top View
Specs fulfilled!
Make PCB Design => Erhard Salow (RALAB, INWAVE)
Notes: Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of the EoI for WPnumber 2) The row in the footer area: write the institute name
Close Master View

## Slide 10: FGB (2): 1st PCB Protoype by RALAB
Few smaller changes required and 2.997MHz output level too low and board too hot!
=> Make 3 separate modules in ZG4 housings
Notes: Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of the EoI for WPnumber 2) The row in the footer area: write the institute name
Close Master View

## Slide 11: FGB (3a): 3 PCBs in ZG4 housings
1300 MHz
from MO
1300 MHz
4 x Clock
Clock Generator Module: CDM
433 MHz
433 MHz
2600 MHz
3033 MHz
3033 MHz
TV
M
12
1
2 x 2997 MHz
Local Oscillator Module: LOM
L-to-S band
Module: LSM
TV
M
2600 MHz
TDS LO
TDS Frequency
TDS ADC Clock: 81MHz
2 x HMC794 (divider 1, 2,3 or 4)
433 MHz – 27MHz
Notes: Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of the EoI for WPnumber 2) The row in the footer area: write the institute name
Close Master View

## Slide 12: FGB (3b): 3 PCBs in ZG4 housings
=> (Revision 2) delivered last Friday
Notes: Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of the EoI for WPnumber 2) The row in the footer area: write the institute name
Close Master View

## Slide 13
FGB (4): 19’’ Crate
CDM1
LOM1
LSM1
Space for filers, rf switches, etc.
Ground plate
Front
Power Supply
230 VAC
15V
12V
7V
TMCB:
Communication
Temperatures
DC Monitors
PS Monitors
Power Amp
for Peltier
DPM340
+ Schalter
Rear
1300 MHz in
RF connectors
CLK
1300 MHz
433 MHz
3033 MHz
2997 MHz
RF Monitors
Temperature
Isolation (foam)
Peltier cooling
from below

## Slide 14: TDS Summary
TDS
TDS
TDS
First system for XFEL injector commissioning required 06/2014: FGB, DWC, SIS8300, pulse-power Pre-amp (200 W) available TMCB for DC monitors and temp stabilization required 08/13 for tests.
Notes: Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of the EoI for WPnumber 2) The row in the footer area: write the institute name
Close Master View

## Slide 15: Overview EBPM
15
Experience with signal detection from EBPM at FLASH: - optical front-end: high resolution but complex/expensive and very limited dynamic range - RF front-end: also complex and included VMs => very prone to temp drifts
New RF detection scheme based on LLRF signal detection.
EBPM Firmware has been integrated in general LLRF firmware.
RF Design of pickup for XFEL vacuum chambers (400 x 40 mm2 ) done by Technical University of Darmstadt
EBPM
Measures the centre-of-gravity of bunch
Relative energy  dE/E ≈ dx / R16
Absolute energy  cross-calibration required
Beam Path
Pickup
φ, t ~ x
Notes: 15
Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of your talk into this text field 2) The 2 rows in the footer area: Delete the text and write the information regarding your talk (same as on the Title Slide) into this text field.
If you want to use more partner logos position them left beside the DESY logo in the footer area Close Master View

## Slide 16: EBPM: LO Generation
1300 MHz from MO
1300 MHz
4 x Clock
Clock Generator Module: CDM
433 MHz
433 MHz
2600 MHz
3033 MHz
3033 MHz
Local Oscillator Module: LOM
TV
M
2600 MHz
EBPM LO (1)
EBPM ADC Clock 108 MHz
EBPM LO(2)
The detection frequencies ():
  LO(1) Fine Measurement: High resolution but several wavelengths fit into vacuum chamber length L~400 mm.
  LO(2) Coarse Measurements: Unambiguous detection of phase in vacuum chamber.
2 x HMC794 (divider 1, 2,3 or 4)
433 MHz – 27MHz
Notes: Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of the EoI for WPnumber 2) The row in the footer area: write the institute name
Close Master View

## Slide 17: EBPM: DWC Detection Scheme
Dark Current
Coarse Meas.
Fine Meas.
4 x
Notes: Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of the EoI for WPnumber 2) The row in the footer area: write the institute name
Close Master View

## Slide 18: EBPM Summary
TDS
TDS
TDS
EBPM
EBPM
EBPM
First system for XFEL required 01/2016: LO Generation, DWC, SIS8300 all available TMCB for DC monitor channels and temp stabilization required for tests.
Open point: Study Influence of signal reflections on detection scheme.
Notes: Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of the EoI for WPnumber 2) The row in the footer area: write the institute name
Close Master View

## Slide 19: Overview EOD
19
Coulomb field of e-beam changes optical properties of the crystal and imprints longitudinal profile on the laser pulse. => Measurement of longitudinal bunch profile by spectral analysis of laser: time resolution > 200fs
Goal: Complete system to fit into 28U rack in XTL
Development of fast 1D detector for multi-bunch readout => changes in the bunch profile within bunch train can be detected (1MHz, 256 pixels)
e-
Beamline Unit
Notes: 19
Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of your talk into this text field 2) The 2 rows in the footer area: Delete the text and write the information regarding your talk (same as on the Title Slide) into this text field.
If you want to use more partner logos position them left beside the DESY logo in the footer area Close Master View

## Slide 20: EOD electronics layout - baseline

## Slide 21
EOD electronics layout – ‘wish’

## Slide 22: EOD Summary (1)
EBPM
EBPM
TDS
TDS
TDS
EBPM
EOD
EOD
EOD
First system for Lab tests required latest 09/2013.
Notes: Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of the EoI for WPnumber 2) The row in the footer area: write the institute name
Close Master View

## Slide 23: EOD Summary (2)
Baseline Layout : LO Generation, DWC, SIS8300 available LDD + CAN Bus required
TMCB for DC monitor channels and temp stabilization required
Upgrade: LDD and filters for LO generation to be integrated in to Yb-Laser crate Wish: DWC-DAC Board with ADC-CLK generation from 1.3GHz and 2 DACs Wish: uPZT2 with local DC Piezo voltage generation on-board => reduces electronics in external crate: TMCB and CDM not required
=> to be ‘synchronized’ with other laser synchronization needs (session by M. Felber)
Notes: Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of the EoI for WPnumber 2) The row in the footer area: write the institute name
Close Master View

## Slide 24: Bunch Compression Monitor: Overview
Detection of Coherent Diffraction Radiation
Coherent ratiation at wavelengths ~ bunch length
Radiated coherent intensity scales with N2
=> very sensitive to ACC phase => FB
Pyro detector:
Generation of surface charges due to change of temperature during absorption of diffraction radiation
Aim: Detect these charge signals
Postdoc will start in April 2013
Define vacuum chamber
Define detector to be used
Define detection scheme
e-

## Slide 25: BCM/CRD: Summary
EBPM
EBPM
EOD
CRD
BCM
BCM
BCM
BCM
TDS
TDS
TDS
EBPM
EOD
EOD
First systems required for XFEL operation ≈ 06/2015 => not time critical
Notes: Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of the EoI for WPnumber 2) The row in the footer area: write the institute name
Close Master View

## Slide 26: Synchrotron Radiation Monitor: Overview
26
Measurement of beam position in the bunch compressor chicanes by imaging the visible SR emitted in the 3rd dipole
Beam energy measurement  EBPM
SR port in vacuum chamber is defined
Complicated vacuum setup to out-couple SR due to large chambers
Detection scheme to be decided (1D line detector, ICCD, PMT, Fast camera, …) to be installed outside of vacuum
FLASH
Notes: 26
Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of your talk into this text field 2) The 2 rows in the footer area: Delete the text and write the information regarding your talk (same as on the Title Slide) into this text field.
If you want to use more partner logos position them left beside the DESY logo in the footer area Close Master View

## Slide 27: SRM: Summary
EBPM
SRM
SRM
EBPM
CRD
BAM
BAM
BAM
BAM
EOD
BCM
BCM
BCM
BCM
TDS
TDS
TDS
EBPM
EOD
EOD
First systems required for XFEL operation ≈ 06/2015
Notes: Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of the EoI for WPnumber 2) The row in the footer area: write the institute name
Close Master View

## Slide 28: Devices
28
Plus OXC-links. RF links, L2R, L2L
 | INJ | BC0 | BC1 | BC2 | COLL | UND | Sum
BAM | 1 | - | 2 | 2 | - | 3 | 8
EOD | 1 | 1 | 1 | - | - | - | 3
BCM | - | 1 | 1 | 2 | - | - | 4
CRD | - | - | - | - | 1 | - | 1
SRM | - | - | 1 | 1 | - | - | 2
TDS | 1 | - | 1 | 1 | - | - | 3
EBPM | - | 1 | 1 | 1 | - | - | 3
Sum | 3 | 3 | 7 | 7 | 1 | 2 | 23
Notes: 28
Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of your talk into this text field 2) The 2 rows in the footer area: Delete the text and write the information regarding your talk (same as on the Title Slide) into this text field.
If you want to use more partner logos position them left beside the DESY logo in the footer area Close Master View

## Slide 29
Conclusions
TMCB needed as soon as possible
DWC-DAC Board with ADC-CLK generation from 1.3GHz and 2 DACs
uPZT2 with local DC Piezo voltage generation on-board
Thanks for your attention

## Slide 30: MSK in a ‘nutshell’
Controller
I, Q
Field Detection
LLRF Regulation
(XFEL WP02)
E, C, Δt, …
Beam Diagnostics
Beam-Based FB
(XFEL WP18)
MLO
Optical
Laser
WP-18 was integrated into MSK in beginning of 2010.
(M. Felber, Ch. Gerth, H. Schlarb from MPY)

## Slide 31: CRD: Overview
31
4-stage THz spectrometer CRISP4 developed by FLA (B. Schmidt)
Pyro line-detector was developed together with company InfraTec
Signal readout is being developed by FLA in MTCA standard => 120 ADC channels
Works best with compressed bunches and at high beam energies => installation in XFEL collimator
Notes: 31
Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of your talk into this text field 2) The 2 rows in the footer area: Delete the text and write the information regarding your talk (same as on the Title Slide) into this text field.
If you want to use more partner logos position them left beside the DESY logo in the footer area Close Master View

## Slide 32: Milestones
32
Devices in XTIN for Injector Commissioning
  09/2013 - Vacuum components delivered to vacuum group
  03/2014 – TDS LLRF system ready
  06/2014 – TDS system conditioned
  12/2013 – Optical Front-ends and electronics BAM and EOD ready
  06/2014 – Synchronization room functional
  06/2014 – All devices installed and ready for beam commissioning
Devices in XTL and XTD
  06/2014 - Vacuum components delivered to vacuum group
  06/2015 – All devices assembled
  11/2015 – TDS systems conditioned
  12/2015 – All devices ready for operation
Devices in HEXP
  12/2015 – Synchronization hutch for sub-distribution functional
Notes: 32
Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of your talk into this text field 2) The 2 rows in the footer area: Delete the text and write the information regarding your talk (same as on the Title Slide) into this text field.
If you want to use more partner logos position them left beside the DESY logo in the footer area Close Master View

## Slide 33: Time schedule
33
We are planning to have all devices installed and ready for operation when beam operation starts
  Beginning 2014 – Devices in XTIN: Laser-based synchronization system with link to photo-cathode laser and BAM, TDS system and kicker, EOD Monitor
  Mid 2015 – All devices in B1, B2, COLL installed
  End 2015 – All devices in SASE1/2 installed and synchronization hutch in HEXP in operation for sub-distribution to pump-probe lasers, all devices ready for operation
Notes: 33
Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of your talk into this text field 2) The 2 rows in the footer area: Delete the text and write the information regarding your talk (same as on the Title Slide) into this text field.
If you want to use more partner logos position them left beside the DESY logo in the footer area Close Master View

## Slide 34: Equipment manufacturing
34
Where possible, commercial systems will be used
  E.g. master laser oscillator (MLO) of laser-based synchronization system (Origami of company OneFive)
Where applicable, we are trying and will try to industrialize sub-systems
  This is the goal for all electronic developments for MTCA.4 standard (larger amount required by other WPs, e.g. WP-02 LLRF)
  Support by Post-doc (C Sydlo) funded by Helmholtz Beschleuniger-Initiative – ARD
  However, usually the amount is too small to benefit from industry
Most systems will be manufactured and assembled in-house
  1 mechanics is working full time for WP-18
  1 system-engineer for assembly of opto-mechanics
Quality insurance is typically in the hand of experts or expert knowledge
  We try to establish ‘standard routines’ where applicable
Keep in mind we have only very few items per diagnostics device
Notes: 34
Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of your talk into this text field 2) The 2 rows in the footer area: Delete the text and write the information regarding your talk (same as on the Title Slide) into this text field.
If you want to use more partner logos position them left beside the DESY logo in the footer area Close Master View

## Slide 35: Team organization
35
Lb Sync System / BAM
EOD
CRD
SRM
TDS
EBPM
U Mavric
Post-doc
B Steffen
Post-doc
Post-doc
(from 2014)
Ch Gerth
LLRF:
M Hoffmann
Coordiantion: M Bousonville
BAM: M Bock
L2RF: T Lamb
L2L: S Schulz
System Engineer
Mechanics, Technician
High-level software engineer (position open)
Notes: 35
Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of your talk into this text field 2) The 2 rows in the footer area: Delete the text and write the information regarding your talk (same as on the Title Slide) into this text field.
If you want to use more partner logos position them left beside the DESY logo in the footer area Close Master View

## Slide 36: Value
36
According to the BB2005 these contributions amounted to 4308 k€ Invest and 71.3 FTE.
Notes: 36
Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of your talk into this text field 2) The 2 rows in the footer area: Delete the text and write the information regarding your talk (same as on the Title Slide) into this text field.
If you want to use more partner logos position them left beside the DESY logo in the footer area Close Master View

## Slide 37: Scope of the contribution
 | Measurement | Pros | Cons
BAM | Arrival time Beam energy | Multi bunch resolution High resolution | Laser-based synchronization system Small dynamic range
EBPM | Beam energy | Multi bunch resolution Large dynamic range | -
SRM | Beam energy profile | Energy profile | Single bunch resolution Limited resolution
View Screen (WP17) | Beam energy profile | Absolute reference | Destructive Method Single Bunch Operation
TDS | Longitudinal beam profile Longitudinal phase space slice emittance | Direct method | Single bunch resolution Destructive to measured bunch
EOD | Longitudinal beam profile | Multi bunch resolution | Limited resolution (> 200 fs)
CRD | Spectral dist. of THz radiation (Longitudinal beam Pprofile) | Multi bunch resolution High resolution | Reconstruction depends on profile Only compressed bunches (< 1ps)
BCM | Integrated THz radiation Compression | Multi bunch resolution Simple RF phase monitor | Only compressed bunches (< 1ps) No reconstruction of profile possible
All devices to be designed as monitors with single bunch resolution
All devices have pros and cons: One diagnostics is no diagnostics
Notes: Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of the EoI for WPnumber 2) The row in the footer area: write the institute name
Close Master View

## Slide 38: Evidence of competence: LBSync / BAM
38
Laser-based Synchronization system based on pulsed 1550 nm radiation (Er-fibre laser) in operation at FLASH
Many components have gone through 3 - 4 revisions (stability, reliability) and are close to ‘industrialization’
Interfaces to other lasers and LLRF are still under development for FLASH
4 BAMs in operation at FLASH
Advanced 40 GHz Pick-up design (developed by industry) for higher resolution
readout electronics in MTCA.4 standard is being developed
Beam-based feedback at FLASH
< 20fs rms arrival time jitter
Pick-up with CF16 flange manufactured to specifications by Orient Microwave Corp.
Courtesy of WP-17
Notes: 38
Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of your talk into this text field 2) The 2 rows in the footer area: Delete the text and write the information regarding your talk (same as on the Title Slide) into this text field.
If you want to use more partner logos position them left beside the DESY logo in the footer area Close Master View