## Slide 1: uLOG Carrier and RF.
Uros Mavric
Collaboration Meeting, Świerk, 20.2.2013

## Slide 2: Current Staus of the Project.
RF Board :
  Changes in the Schematic:
    REF auxiliary output (e.g. for KLMs), 1.3 GHz , +15 dBm output
    By-passable (resistors) RF amp on the main REF distribution probably not enough power for the REF and LO
    Resistor transformers for voltage and RF power readings on the side of the RF board instead of carrier
    LoPro Dielectric instead of normal RO4003C -> smaller roughness with thicker copper
    1.5 oz copper -> better thermal characteristics
    Pinout change of the interface connector to simplify routing on the carrier
  Complete re-routing of the ver. 1 RF board was needed
  power layers still to be routed
Carrier Board :
  Schematic defined (MMC section still to be changed due to MMC1.0 compatibility)
  To be finished:
    Application MC connections to the MMC, ADCs, JTAG
    MMC
    Final pouring and RF via stitching
    Power layers almost done

## Slide 3: Next Steps.
Define the missing sections:
  MMC
  All the rest that comes up every week
Manufacturing of 3 prototypes (RF and Carrier):
  Exception PCB – PCB manufacturer
  Screaming circuits – Assembly house
The first tests will be done at DESY
None of the components is critical from the point of view of lead time:
  ERNI connectors – 6 spares anywhere?
In parallel the shields are being manufactured

## Slide 4: Open Questions.
MMC
Temperature regulation:
  General principle (fully isolated system or regulation of specific areas)
  Mechanics will be defined by the temp. regulation principle
  The TEC mezz. will be manufactured after the prototypes have been delivered.

## Slide 5: Current 3D Views.
RF Board
Carrier Board - Top
Carrier Board - Bottom
RF&Carrier
LO Gen
Distribution Mezz. boards