## Slide 1: DRTM-AD84
General 16-bit (8 Channel ADC, 4 Channel DAC Board)
Robert Meyer
Advanced Techniques in LLRF control for XFEL
Otwock-Swierk, 20.02.2013

## Slide 2: Specification
RTM-Board Interface D1.0 / D1.1
8 Channel 16-bit ADC
  Selectable 50Ω or 1kΩ Input impedance
  Selectable 2MHz LPF for antialiasing
  10MSPS Data rate
  Inputbandwidth of 90MHz or 2 MHz
4 Channel 16-bit DAC
  High Gain Output ±3V@50r
  Low Gain Output ±1V@50r
  1 MSPS direct Data rate / 16MSPS with interpolation
Independent Timing on each Channel

## Slide 3: Filterstage

## Slide 4: FFT on RAW-Data

## Slide 5: Next Steps
Change RTM-Interface to D1.1
Change DAC-Outputfilter from Passive to Active
Improve Voltagegenaration
See how it works in “real life”