## Slide 1: Studies for Particle Driven Plasma Acceleration at PITZ
Experiments planned utilizing PITZ (Photo Injector Test facility at DESY, Zeuthen site)
Matthias Gross
Grömitz,
21. March 2013

## Slide 2: Background
Courtesy of Carl Schröder, LBNL
Does this work ?
Dephasing ?
Hose instability ?
Background:

## Slide 3: Why Experiments at PITZ?
Favorable circumstances
  Pure R&D facility (no users)
  Unique laser system (pulse shaper)
  Well developed diagnostics (high resolution electron spectrometer, etc.); soon: transverse deflecting cavity + dispersive section for longitudinal phase space measurements
Possible contribution from PITZ:
  Self modulation of electron beam
  Later: High transformer ratio (needs bunch compressor)

## Slide 4: Flexible Laser Pulse Formation at PITZ
Photoinjector laser
Developed and built by Max-Born Institute Berlin
Key element: the pulse shaper
  Contains 13 birefringent crystals. Pulses are split according to polarization. Delay is given by crystal thickness; relative amplitude can be varied freely by adjusting relative angle between crystals
Gaussian input pulses
Shaped ouput pulses
Will, Klemz, Optics Express 16 (2008) , 4922-14935
motorized rotation stage
temperature controlled birefringent crystal
birefringent shaper, 13 crystals
FWHM = 25 ps
edge10-90 ~ 2.2 ps
edge10-90 ~ 2 ps
birefringent shaper, 13 crystals
OSS signal (UV)

## Slide 5: Experimentally Demonstrated Pulse Shapes
Driver + witness bunch
Modulated driver + witness bunch
Modulated driver
Multi bunches

## Slide 6: 3D PIC (Particle in Cell) Simulation of PITZ Experiment
Simulations:
Alberto Martinez de la Ossa
Beam parameters | Setup 1
Total charge, pC | 100
Longitudinal beam position, m | 6.44
Horizontal rms beam size, um | 42.0
Vertical rms beam size, mm | 42.0
Bunch length in FWHM, mm | 5.93
Average kinetic energy, MeV | 21.5
Peak slice current, A | 5.3
Horizontal rms emittance, mm mrad | 0.372
Vertical rms emittance, mm mrad | 0.372
Peak beam density, 10^13 e / cm^3 | 1.9
PITZ resolution window
Expected energy modulation 400 keV. PITZ beam energy spread as low as 60keV. Resolution of TDS/HEDA2: 10keV and 100m (Malyutin et al. “Simulation of the Longitudinal Phase Space Measurements With the Transverse Deflecting Structure at PITZ”, Proc. of IPAC 2012, MOPPP034  Measurable

## Slide 7: Insertion of Plasma Cell into PITZ Setup
PITZ 2 setup to be used for first plasma experiments
Plasma cell has to be between booster and TDS
Two possible positions, both with a length of about 1m
Beam dynamics simulations to determine which position is more favorable
<7 MeV
<25 MeV
plasma cell
or

## Slide 8: Simulation: Scenarios for Plasma Cell Insertion
Schematic views
Electron beam rms size
  More complex beam focusing for setup 2
Setup 1
Setup 2
Simulations:
Martin Khojoyan

## Slide 9: Simulation: Beam Properties
Beam properties for Setup 1 (Imain = 363A) Comparison of setups
Setup 1: beam properties acceptable. Smaller beam size, less divergence, higher peak density – overall preferable
Beam parameters | Before dipole | After dipole
Total charge, pC | 100 | 100
Longitudinal beam position, m | 6.35 | 9.45
Horizontal rms beam size, um | 49.8 | 59.4
Vertical rms beam size, mm | 51.2 | 59.4
Rms bunch length, mm | 1.71 | 1.71
Bunch length in FWHM, mm | 5.92 | 5.92
Average kinetic energy, MeV | 24.55 | 24.55
Rms energy spread, keV | 27.5 | 27.8
Peak slice current, A | 5.2 | 5.2
Horizontal rms emittance, mm mrad | 0.37 | 0.38
Horizontal beam divergence, mrad | 0.008 | 0.09
Vertical rms emittance, mm mrad | 0.38 | 0.36
Vertical beam divergence, mrad | 0.002 | 0.13
Longitudinal rms emittance, keV mm | 42.4 | 42.4
Peak beam density, 10^12 e / cm^3 | 9.1 | 6.6
Simulations:
Martin Khojoyan

## Slide 10: Key Topic: Ionization of Plasma Channel
Three approaches:
  Plasma discharge
  RF wave (helicon wave)
  Laser ionization
    Single photon ionization
      Linear process
      Need UV light (< 230nm), e.g. ArF laser
      Normally partial ionization  percentage is function of local laser intensity (saturation curve)
    Field ionization
      Nonlinear process
      Laser wavelength not important, e.g. Ti:Sapphire or CO2 laser
      Threshold process  Complete ionization in well defined volume

## Slide 11: Lithium Plasma Cell
Principle:
  Evaporate Lithium in central pipe (700°C)
  Define beginning and end of Lithium zone with steep temperature gradient and Helium buffer gas
  Once pressure regions have stabilized:
    Ionize Lithium gas with laser
    Inject particle beam for PWA experiment
Figure from: P. Muggli et al. “Photo-Ionized Lithium Source for Plasma Accelerator Applications”, IEEE Trans. Plasma Science 27 (1999), pp. 791-799

## Slide 12: Optics for Laser Plasma Generation – Axial Coupling
Axicon for homogeneous ionization profile
  Adjustable aperture to define length of plasma channel
Simple focusing mirror
  Length of plasma channel defined by Li gas volume
e- beam
Aperture
e- beam
Plasma channel
Li gas
Li gas

## Slide 13: Plasma Ionization –Side Coupling
Independent optimization of electron and laser paths possible
Setup:
Ionized region
e-
Dump
Li
He
He
He
He
z
x

## Slide 14: Plasma Cell Assembly: Sketch
Electron
Beam
Design:
Gerald Koss
Plasma cell
Preliminary Version
Turbo pump
Quadru-
poles
Ionization
laser
To
diagnostics

## Slide 15: Heat Pipe Oven Prototype
Inner glass tube; outer copper tube with spiral groove to hold heating wire (Thermocoax TET; 1.5mm diameter; 5.5/m)
Length of heating region: 30cm

## Slide 16: Experiments have started with Plasma Cell Prototype
Temperature probe with measurement
Power supply for heater
Plasma cell with
heat insulation
First: Measurement of temperature profile with air in plasma cell tube
Copper tube helps to homogenize temperature distribution: 2°C (<1%) over 10cm
Temperature is high enough: need 650°C in PITZ experiment

## Slide 17: Multi Bunches: High Transformer Ratio
Plasma Acceleration: e.g. 5 bunchlets within bunch  transformer ratio >2
Longitudinal laser profile at the cathode
10pC 30pC 50pC 70pC 10pC
ASTRA simulations through gun and booster up to z=5m
Setup: - use PITZ2 beamline with gun, booster, and matching quads up to z=7m
  - install a short bunch compressor (dogleg)
use Elegant for matching
and the dogleg design (ongoing)
Longitudinal phase space at z=5m
Parameters:
Q = 170 pC in 5 pulses
100 000 particles
Gun phase: 10 deg
Booster phase: 40 deg
BC layout:
compression factor C = 4
R56 = 0.15
Total length l = 1m
dipoles: r = 0.6m, α = 60 deg
D1
D2
Q1
Q2
Q3
S1
S2
l=1m
Design with 2 doglegs (↑↓) on the way
Simulation by Anne Oppelt

## Slide 18: Very Preliminary Results: Needs Optimization
~λp
Driver bunch
Witness bunch
Energy gain!
Bunches at the beginning:
Bunches after 1 cm in plasma:
The witness bunch falls in the region where the wakefield is maximum.
In approx. 1 cm of propagation in the plasma, a fraction of the electrons in the witness bunch double their energy.
/n0
Driver bunch
Witness bunch
Simulation by Alberto Martinez de la Ossa

## Slide 19: Outlook
2013: First experiments with plasma cell in laboratory
2014: Characterization of energy modulation of electron beam in plasma
Then: Insertion of bunch compressor – experiments with high transformer ratio etc.
Cooperation with SLAC, CERN etc.

## Slide 20: Summary
PWA Experiments are planned at PITZ
  Now: Characterization of electron beam self modulation
  Later: High transformer ratio
Utilization of good diagnostics and unique laser system
Simulations show promising results
  Electron sub bunching and energy modulation with current setup
  Energy gain with bunch compressor
First experiments with plasma cell prototype

## Slide 21
Backup

## Slide 22: Transformer Ratio (TR)

## Slide 23: How to Increase the Transformer Ratio

## Slide 24: Simulation of Beam-driven Plasma Wakefields
The driver bunch enables a longitudinal wakefield of 4.3 GeV/m approx. λp behind the beam’s front.
n0 = 2×1015 e/cm3
ωp = (4πn0e2/m)1/2 = 2.5×10-3 fs-1
λp = 2πc/ωp = 750 μm
E0 = mcωp/e = 4.3 GeV/m
PITZ’s beam layout after the BC (0.034T)
2-heads shape separated by ~ 550μm
1. Driver bunch
Q=526 pC, σz=15μm, <E>=13 MeV
2. Witness bunch
Q=158 pC, σz=10μm, <E>=12 MeV
~λp
accelerating field
focusing field
Driver bunch
Plasma
/n0
/E0
/E0
Simulation by Alberto Martinez de la Ossa

## Slide 25: Ionization Processes
1. (Multi) photon
absorption
2. Tunneling
ionization
3. Barrier suppressed
ionization (BSI)
χ(4) – process for
Li and Ti:Sa laser
(Low probability)
Described by
ADK theory
(Exponential law)
Full ionization
possible
Vacuum
level
Electronic
level
Ti:Sa
ArF
Low field
High field
Highest field

## Slide 26: Estimation of Ti:Sa Laser Peak Power
Laser power needed for ideal case (uniform power density over lateral and longitudinal channel dimensions and DC case): Pid=Ithπr02
  Channel radius: r0 ; BSI Ionization threshold Ith (3.4*1012 W/cm2 for Li)
Power increased by 24
  Lateral distribution: factor 2
  Longitudinal: factor 2
  Short pulse: factor 3
  Transport loss etc.: factor 2
DC
threshold
from: Tong et al., J. Phys. B 38 (2005) p. 2593
I
Ipeak
Ith
ro
r
I
z
Ipeak
Ith
z1
z2

## Slide 27: Ionization Energies: Single Photon and Field Ionization
From Z. Najmudin’s talk at PDPWA workshop (Munich, Dec 1st 2011)
  Energy required to completely ionize a 1m long, 1mm2 plasma channel (Single Photon)
  BSI Intensity: Threshold intensity for complete ionization (Field Ionization)

## Slide 28: Additional use of Ti:Sa laser
Problem
  Measurement of density fluctuation in a plasma for PWA at PITZ
Facts
  Alkali metal vapor (e.g. Rb) with density of about 1015 cm-3
  Basic Idea from Markus Drescher: Focus laser within gas to ionize small volume, then collect ions
Idea
  Use Ti:Sa laser for this measurement and ionization for PWA: gas density = plasma density
  Focus laser coaxially into gas volume so that field ionization threshold is exceeded only in small volume around beam waist – scan this focus around plasma cell
  Pick up ions with big electrodes, e.g. plates or wires: the electrodes do not need high resolution since that is done by the laser focus – no need for local detector

## Slide 29: Setup Details / Back of the envelope Calculation
Assume: Gaussian beam
  Dmax = (300+100+200+100+100)mm = 800mm
  r = 5mm (half diameter of vacuum window – worst case: put at Dmax)
   max = 6 mrad
  Lateral resolution: 2w0,max = 2/  80m
  Calculation of axial resolution also leads to value <100m
High resolution measurement possible, could be evaluated at PITZ
Axial scan
Lateral scan
Vacuum
window
300mm
100mm
200mm
100mm
100mm
Rb
He

w0
r
Dmax
Ti:Sa  =800nm
He

## Slide 30: Plasma Cell Assembly: Sketch
Electron
Beam /
Laser
Design:
Gerald Koss
Plasma cell
Preliminary Version
Screen stations
Quadru-
poles