## Slide 1
Algebraic Reconstruction of X-ray Tomography on parallel computing Architecture of LSDF
Xiaoli Yang, Thomas Jejkal, Halil Pasic, Rainer Stotzka, Achim Streit, Jos van Wezel, Tomy dos Santos Rolo

## Slide 2: Motivation for X-ray tomography
ANKA
  Synchrotron light source at KIT: storage ring, beamline labs
  Topo-Tomo beamline: parallel X-ray, tomography experiment platform
  Studying moving biological objects in 3D

## Slide 3: Motivation for X-ray tomography
World fastest tomography system
  Rotation: continuously, high speed
  Several GB/s  hundreds TB per day
  200 - 400 projections in [0°-180°]
Reconstruction
  Standard reconstruction method: filtered-back projection
     artifacts
Better reconstruction algorithm needed
  CS-ART(Compressive Sampling-based Algebraic Reconstruction Technique)

## Slide 4: Reconstruction method CS-ART
Algebraic Reconstruction Technique : Equation system (ill-posed)
  Flexible for forward models
  Prior knowledge
Precise forward model
  Geometry of sensor
  X-ray: beam with width and distance
Compressive Sampling theory
  Image restoring from less samples
  Sparse representation in some space
  Total Variation: assuming that the gradient space is sparse

## Slide 5: Reconstruction images
CS-ART algorithm produces high quality images using only a few projections.
(a) reference (b) (c)
Standard: 1500 projections
Standard: 60 projections
CS-ART: 60 projections
Data reduction
High quality image
Computing expensive
Thousand parallel slices: 1~3 min (standard), tens of hours (CS-ART)
 Parallelization required

## Slide 6: LSDF
LSDF: Large Scale Data Facility at KIT for data intensive scientific experiments
  Storage facility: at Petabyte scale
  Data storage, archives and access
  Computer cluster with 58 nodes: each with 8 cores, 36GB memory
  Data computing and analysis in parallel
Workflow of LSDF in application of ANKA
Online Storage
Computing & Analysis
Archives

## Slide 7: Parallel computing
Data parallel
  Each slice: MATLAB software, independently
  1024 slices  37 nodes (of 58 nodes)
Mapping Task
Mapping Task
Mapping Task
Mapping Task
Mapping Task
1024 slices
node
node
node
Computing cluster
3D Reconstruction
  a number of tasks
  (slice-sequential)
Tasks  cluster nodes
  (in parallel)
1 task : sequential
Up to 222 tasks in parallel (37 nodes* 6)

## Slide 8: Parallel computing performance
Measured time and speedup factor
Parallel tasks | Time [s] | Speedup
1 | 39727 (~11 hours) | --
12 | 3415 | 11.63
24 | 1747 | 22.73
37 | 1107 | 35.85
74 | 650 | 61.08
111 | 488 | 81.39
148 | 417 | 95.20
185 | 360 | 110.2
222 | 330 (5.5 min) | 120.0

## Slide 9: Parallel computing performance
Comparison with theoretical value

## Slide 10: Parallel computing performace
Comparison with theoretical value
  Lower increasing speed
  Reason: multiple tasks in one node
    Share cores
    Share memory
    Share data access bandwidth
High computing performance achieved
  330 seconds (less than 6 min), 120 speedup
Enable the application of novel algorithm
   better images for ultrafast tomography

## Slide 11: Conclusions
Algorithm CS-ART shows high potential to reconstruct better images for reduced data.
Workflow of LSDF will enhance the data storage, management and automatic data intensive computing for ANKA.
  (finished at the end of the year 2013)
The promising reconstruction result and high computing performance at LSDF greatly support the construction of the world fastest tomography system at ANKA.
Workflow of LSDF is not limited to ANKA. It also supports other institutes involving data intensive computing (micro-tomograph and other tomograph experiments).