## Slide 1: BHM Detector Motivation: FLUKA Simulations, Frontend Design and Test Beam Results
Orfanelli Stella
(CERN-NTUA)
R & D Team:
A. Dabrowski(CERN), M. Giunta(CERN), S. Orfanelli (CERN-NTUA)
M. Ambrose(Univ Minnesota), R. Rusack (Univ Minnesota), & D. Stickland (Princeton)
Workshop on CMS Beam Conditions, Radiation Monitoring and Luminosity Systems
DESY, Zeuthen, 24th April 2013

## Slide 2: Outline
Detector Motivation and Concept
  Choice of Location
  Challenges and Principles of Detection
    Expected rate
    Background suppression
Design
  Geometry and Material
  Orientation
  Photomultiplier choice

## Slide 3: Detector Motivation
Purpose:
To provide an on-line measurement of the Machine Induced Background(MIB) in CMS .
    At High Radius with overlapping acceptance with the CMS CSC chambers
    During both colliding and circulating beams
    Separate B1 and B2 measurements
After LS1:
    Exceeding nominal luminosity.
    25ns bunch spacing.
    Increasing bunch charge.
    Tighter LHC collimators settings.
    Electron cloud effects.
Why?
    MIB contaminates Level 1 trigger rate and results in low data taking efficiency.
    At High radius, to complement BCM1F MIB measurement at small radius.
    Verification of FLUKA model.
    Flag poor beam conditions for CMS and LHC by lumi-section.
Higher MIB expected,
Beam Halo & Beam Gas.

## Slide 4: Detector concept- Challenges
Goal to reach | Challenge | Requirement | Solution
Measure MIB arriving in time with the incoming bunches from the tunnel side. | CMS cavern environment dominated by the pp products arriving from the IP side. | DIRECTIONALITY | CHERENKOV RADIATION
 | Stay shielded from IP  pp products should be shielded and albedo reduced | SENSITIVE TO LESS BACKGROUND SIGNAL | LOCATION IN THE CAVERN SHIELDED BY CMS DETECTOR FROM IP
CMS cavern environment. | High radiation exposure | RADIATION HARDNESS | RADIATION HARD COMPONENTS CHERENKOV RADIATION
 | Mostly gammas and thermal neutrons | SENSITIVITY ONLY TO CHARGED PARTICLES | CHERENKOV RADIATION
Be able to cope with the 25ns bunch spacing. | Maximum time separation between MIB and the collision products = 12.5ns. | FASTER THAN 10ns | CHERENKOV RADIATION FAST ELECTRONIC COMPONENTS (PMT, READ-OUT)
Cost | Limited budget. | COST EFFECTIVE | MAKE WISE CHOICES.

## Slide 5: Detector Location in CMS cavern
GL1
6.25ns
GL2
18.75ns
GL3
31.25ns
GL4
43.75ns
GL5
56.25ns
GL6
68.75ns
Beam1
COLLISION=1
IP
Beam2
t = 0.0 ns
B1
B1
B1
Golden locations:
where it’s easier to discriminate the MIB products from the collisions products based on the fact they are arriving well separated in time.
For the 25ns this maximum timing separation corresponds to 25/2=12.5ns.
Must sit in one of the golden locations.

## Slide 6: Detector Location in CMS cavern
GL1
6.25ns
GL2
18.75ns
GL3
31.25ns
GL4
43.75ns
GL5
56.25ns
GL6
68.75ns
t = 6.25 ns
IP
Beam2
B1
B1
B1
Beam1
B2
Golden locations:
where it’s easier to discriminate the MIB products from the collisions products based on the fact they are arriving well separated in time.
For the 25ns this maximum timing separation corresponds to 25/2=12.5ns.
Must sit in one of the golden locations.

## Slide 7: Detector Location in CMS cavern
GL1
6.25ns
GL2
18.75ns
GL3
31.25ns
GL4
43.75ns
GL5
56.25ns
GL6
68.75ns
IP
B1
B1
B1
B2
t = 12.5 ns
Beam2
Beam1
Golden locations:
where it’s easier to discriminate the MIB products from the collisions products based on the fact they are arriving well separated in time.
For the 25ns this maximum timing separation corresponds to 25/2=12.5ns.
Must sit in one of the golden locations.

## Slide 8: Detector Location in CMS cavern
GL1
6.25ns
GL2
18.75ns
GL3
31.25ns
GL4
43.75ns
GL5
56.25ns
GL6
68.75ns
t = 18.75 ns
IP
Beam2
Beam1
B2
B1
B1
B1
Golden locations:
where it’s easier to discriminate the MIB products from the collisions products based on the fact they are arriving well separated in time.
For the 25ns this maximum timing separation corresponds to 25/2=12.5ns.
Must sit in one of the golden locations.

## Slide 9: Detector Location in CMS cavern
GL1
6.25ns
GL2
18.75ns
GL3
31.25ns
GL4
43.75ns
GL5
56.25ns
GL6
68.75ns
IP
t = 25.00 ns
Beam2
Collision=2
Beam1
B1
B2
B1
B1
Golden locations:
where it’s easier to discriminate the MIB products from the collisions products based on the fact they are arriving well separated in time.
For the 25ns this maximum timing separation corresponds to 25/2=12.5ns.
Must sit in one of the golden locations.

## Slide 10: Detector Location in CMS cavern
GL1
6.25ns
GL2
18.75ns
GL3
31.25ns
GL4
43.75ns
GL5
56.25ns
GL6
68.75ns
IP
t = 31.25 ns
Beam2
Beam1
B2
B2
B1
B1
B1
Golden locations:
where it’s easier to discriminate the MIB products from the collisions products based on the fact they are arriving well separated in time.
For the 25ns this maximum timing separation corresponds to 25/2=12.5ns.
Must sit in one of the golden locations.

## Slide 11: Detector Location in CMS cavern
GL1
6.25ns
GL2
18.75ns
GL3
31.25ns
GL4
43.75ns
GL5
56.25ns
GL6
68.75ns
IP
t = 37.5 ns
Beam2
Beam1
B1
B2
B1
B2
B1
Golden locations:
where it’s easier to discriminate the MIB products from the collisions products based on the fact they are arriving well separated in time.
For the 25ns this maximum timing separation corresponds to 25/2=12.5ns.
Must sit in one of the golden locations.

## Slide 12: Detector Location in CMS cavern
GL1
6.25ns
GL2
18.75ns
GL3
31.25ns
GL4
43.75ns
GL5
56.25ns
GL6
68.75ns
IP
t = 43.75 ns
Beam2
Beam1
B2
B2
B1
B1
B1
Golden locations:
where it’s easier to discriminate the MIB products from the collisions products based on the fact they are arriving well separated in time.
For the 25ns this maximum timing separation corresponds to 25/2=12.5ns.
Must sit in one of the golden locations.

## Slide 13: Detector Location in CMS cavern
GL1
6.25ns
GL2
18.75ns
GL3
31.25ns
GL4
43.75ns
GL5
56.25ns
GL6
68.75ns
t = 50.00 ns
Beam2
IP
Collision=3
Beam1
B1
B2
B1
B2
B1
Golden locations:
where it’s easier to discriminate the MIB products from the collisions products based on the fact they are arriving well separated in time.
For the 25ns this maximum timing separation corresponds to 25/2=12.5ns.
Must sit in one of the golden locations.

## Slide 14: Detector Location in CMS cavern
GL1
6.25ns
GL2
18.75ns
GL3
31.25ns
GL4
43.75ns
GL5
56.25ns
GL6
68.75ns
t = 56.25 ns
Beam2
IP
Beam1
B2
B2
B2
B1
B1
B1
Golden locations:
where it’s easier to discriminate the MIB products from the collisions products based on the fact they are arriving well separated in time.
For the 25ns this maximum timing separation corresponds to 25/2=12.5ns.
Must sit in one of the golden locations.

## Slide 15: Detector Location in CMS cavern
GL1
6.25ns
GL2
18.75ns
GL3
31.25ns
GL4
43.75ns
GL5
56.25ns
GL6
68.75ns
t = 62.5 ns
Beam2
IP
Beam1
B1
B2
B1
B2
B1
B2
Golden locations:
where it’s easier to discriminate the MIB products from the collisions products based on the fact they are arriving well separated in time.
For the 25ns this maximum timing separation corresponds to 25/2=12.5ns.
Must sit in one of the golden locations.

## Slide 16: Detector Location in CMS cavern
GL1
6.25ns
GL2
18.75ns
GL3
31.25ns
GL4
43.75ns
GL5
56.25ns
GL6
68.75ns
t = 68.75 ns
Beam2
IP
Beam1
B2
B2
B2
B1
B1
B1
Golden locations:
where it’s easier to discriminate the MIB products from the collisions products based on the fact they are arriving well separated in time.
For the 25ns this maximum timing separation corresponds to 25/2=12.5ns.
Must sit in one of the golden locations.

## Slide 17: Golden Location 6
Golden location:
  MIB – pp products maximum time separation
Good environmental conditions
Available space around the rotating shielding.
Absolute MIB flux is higher w.r.t. other golden locations closer to the IP.
+z
IP
Golden Location 6
0deg
φ
GOLDEN LOCATION 6 : the most promising location.
GL7 GL6 GL5 GL4 GL3 GL2 GL1

## Slide 18: Golden Location 6 Environmental Parameters
1)Expected dose for 10 years of operation <1kGy
2)Magnetic Field <200gauss
Radial distance[cm]
from beam axis
Radiation dose in rad for 10years of operation
Bz
Br
Radial distance[m]
Radial distance[m]
Magnetic Field
Free space
Free space

## Slide 19: Golden Location 6 MIB/PP flux ratio & MIB flux
Radial distance[cm] from beam axis
10-3
MIB/PP flux ratio of all charged particles above Cherenkov threshold, Golden Location 6.
MIB(red) & PP(black) fluxes of all charged particles above Cherenkov threshold, Golden Location 6.
Flux (/cm2/sec)
MIB Flux / pp Flux
Two metrics used to conclude to GL6 as the most preferable:
MIB/PP flux ratio 2) Absolute value of MIB flux.
Radial distance[cm] from beam axis
MIB flux ~ 1particle/cm2/sec
MIB/PP ~4e-4 – 4e-3
Results from FLUKA simulations : 20k pp events VS 3e6 MIB particles (N.Mohkov input files produced by MARS).Both simulations for a nominal machine.

## Slide 20: Golden Location 6 MIB/PP flux ratio & MIB flux
Radial distance[cm] from beam axis
10-3
MIB/PP flux ratio of all charged particles above Cherenkov threshold, Golden Location 6.
MIB(red) & PP(black) fluxes of all charged particles above Cherenkov threshold, Golden Location 6.
Flux (/cm2/sec)
MIB Flux / pp Flux
Two metrics used to conclude to GL6 as the most preferable:
MIB/PP flux ratio 2) Absolute value of MIB flux.
Radial distance[cm] from beam axis
Need to suppress the pp signal to 0.1%.
MIB/PP ~4e-4 – 4e-3
MIB flux ~ 1particle/cm2/sec
Results from FLUKA simulations : 20k pp events VS 3e6 MIB particles (N.Mohkov input files produced by MARS).Both simulations for a nominal machine.

## Slide 21: Golden Location 6 MIB/PP flux ratio & MIB flux
Results from FLUKA simulations : 20k pp events VS 3e6 MIB particles (N.Mohkov input files produced by MARS).Both simulations for a nominal machine.
Radial distance[cm] from beam axis
10-3
MIB/PP flux ratio of all charged particles above Cherenkov threshold, Golden Location 6.
MIB(red) & PP(black) fluxes of all charged particles above Cherenkov threshold, Golden Location 6.
Flux (/cm2/sec)
MIB Flux / pp Flux
Two metrics used to conclude to GL6 as the most preferable:
MIB/PP flux ratio 2) Absolute value of MIB flux.
Radial distance[cm] from beam axis
MIB/PP ~4e-4 – 4e-3
Stay in radius less than 220cm to have a succeed in a MIB rate of at least 1 hit/cm2/sec
Need to suppress the pp signal to 0.1%.
MIB flux ~ 1particle/cm2/sec

## Slide 22: Golden Location 6 Properties of the MIB signal
Mostly expected type of particles: Beam Halo Muons produced at the collimators.
Most of the MIB muons
  are concentrated near the 10GeV region.
  arrive pretty concentrated in angle
  (0 -15deg).
Angle vs Energy (for mu above Cherenkov threshold)
MIB Muons /cm2/sec
0.26 muons/cm2/sec are expected to arrive at golden location 6, while the total MIB rate is 0.4particles/cm2/sec.

## Slide 23: Golden Location 6 Background sources
Particles/cm2/sec/dΩ/dE
Fake signal
Expected PP contribution coming on the opposite site
of the signal
Lab polar angle φ (rad)
Fake signal
(Very small)
Particles/cm2/sec/dΩ/dE
Expected PP contribution coming on the opposite site
of the signal
(very small angles)
Lab polar angle φ (rad)
Background sources:
electrons and positrons coming from secondary interactions & multiple scattering from both sides.
muons coming straight from the IP
high energy gammas that could produce delta rays in the material.
Angle vs Energy (for e above Cherenkov thresh)
Golden Location 6 Background source
Angle vs Energy (for m above Cherenkov thresh)
Energy (GeV)
Energy (GeV)

## Slide 24: Principle of Detection: Directionality
Time [ns]
Time [ns]
Amplitude [V]
Amplitude [V]
Tested fused quartz Cherenkov radiators during test beam (July 2012).
forward
backward
DIRECTIONALITY: property of the detector to distinguish between particles coming from different directions => suppress background signal while selecting particles parallel and consistent with the direction of the incoming beam.

## Slide 25: Principle of Detection: Directionality
Goal: suppression of the background signal 1 over 1000.
Proven directionality functionality of the tested fused quartz Cherenkov radiator during test beam (July 2012).
✓
By setting a discrimination voltage such that 95% of the forward signal is accepted, the backward signal acceptance is O(10-3). That means that only 1 out of the 1000 backward moving particles (coming from the pp) would be confused as a MIB particle.
With a small loss of the signal (5%) the backward acceptance less than 0.1% is achievable
Comparable results for muons and protons.

## Slide 26: Principle of Detection: Timing
Fast timing distribution 3.1ns FWHM
TIMING: To benefit from the placement at the golden location the signal needs to be faster than 10ns.
Goal:
rapid signal propagation <10ns
Proven fast timing distribution of the signal = 3.1ns FWHM.
(July 2012 test beam).
✓
FWHM [ns]
R2059 PMT

## Slide 27: The fake signal component
FAKE SIGNAL is the signal that is moving at the same direction of the MIB signal but comes from pp-products.
Directionality cannot be used to suppress this background component.

## Slide 28: The fake signal component
MIB signal rate:
0.4 particles/cm2/sec
FAKE SIGNAL is the signal that is moving at the same direction of the MIB signal but comes from pp-products.
Directionality cannot be used to suppress this background component.

## Slide 29: The fake signal component
MIB signal rate:
0.4 particles/cm2/sec
FAKE signal rate:
45 particles/cm2/sec
FAKE SIGNAL is the signal that is moving at the same direction of the MIB signal but comes from pp-products. Dominated by low energy e- e+.
Directionality cannot be used to suppress this background component.

## Slide 30: The fake signal component
MIB signal rate:
0.4 particles/cm2/sec
FAKE signal rate:
45 particles/cm2/sec
FAKE SIGNAL is the signal that is moving at the same direction of the MIB signal but comes from pp-products. Dominated by low energy e- e+.
Directionality cannot be used to suppress this background component.
Fake signal 100 times more than MIB signal.

## Slide 31: The fake signal component
MIB signal rate:
0.4 particles/cm2/sec
FAKE signal rate:
45 particles/cm2/sec
FAKE SIGNAL is the signal that is moving at the same direction of the MIB signal but comes from pp-products. Dominated by low energy e- e+.
Directionality cannot be used to suppress this background component.
Goal:
Suppress the fake signal to 1%.
Fake signal 100 times more than MIB signal.

## Slide 32: The fake signal component Particle characteristics
Energy spectrum of e-+ from pp collisions
Most of e-+ arriving at GL6 at the same direction with the signal (red spots) have energy less than 100MeV.
FAKE SIGNAL DOMINATED BY LOW ENERGY e-+.
Energy [GeV]
dN/dE [cm-2 sec-1 GeV-1]
Goal:
Suppress the fake signal to 1%.

## Slide 33: Suppression of the fake signal component- Shielding
Shielding of 1cm Al suppresses the signal that the 10MeV e-+ would produce below the threshold, but doesn’t affect the 100MeV signal.
Goal:
Suppress the fake signal to 1%.
Geant4
M.Ambrose
Geant4
M.Ambrose

## Slide 34: Suppression of the fake signal component- Timing
Time(sec)
Distribution of the time of arrival of the 794 e-+
Distribution of the time of arrival of the 70 e-+ with energy >10MeV
10ns
During this time interval contribution of pp is expected.
FLUKA
Based on timing combined with shielding of 1cm Al, suppression 99% of the fake signal component succeeded.
✓
Criteria | Relative number of e-+ arriving at the same direction with MIB | Percentage
Cherenkov threshold | 794 | 100%
Passing the shielding material | 70 | 8%
Outside a 10ns time interval | 8 | 1%
Goal:
Suppress the fake signal to 1%.

## Slide 35: Suppression of the fake signal component- gamma rays
HIGH ENERGY γ are capable of creating delta rays with energy sufficient to produce Cherenkov radiation in the detector.
Energy spectrum of γ from pp collisions
Most of γ arriving at GL6 have energy less than 100MeV.
Goal:
Suppress the HE gammas.
Energy[GeV]

## Slide 36: Suppression of the fake signal component- gamma rays
Shielding of 1cm Al suppresses the signal that the HE gammas would produce under the threshold.
✓
Goal:
Suppress the HE gammas.
Geant4
M.Ambrose
Geant4
M.Ambrose

## Slide 37: Detector Motivation &Feasibility Summary
Golden location 6
  Good environmental conditions
  Free space
  MIB flux rate close to 1hit/cm2/sec.
Need to suppress background signal coming from the opposite side (pp-products) to 1 over 1000.
    ✔ directionality
Need to suppress background signal coming from the same side to 1 over 100.
    timing and shielding for low energy e-+.
Need to suppress high energy gammas.
    ✔ shielding.

## Slide 38: Design Parameters
Cherenkov radiator
  Material choice
  Geometry
    Length
    Radius
    Surface tolerance and roughness
Optical coupling
Photomultiplier choice
  Characteristics and Features
  Performance

## Slide 39: Design: Material Choice
Directionality of quartz proven during test beams.
Transmission in UV area
Wavelength(nm)
Transmission in %
HSQ300 (=HSQ330, not certified %impurities)
HSQ330 (certified %impurities)
Suprasil (synthetic quartz)
Geant4
M.Ambrose
Expected wavelength for 0 deg
Wavelength(nm)
450nm

## Slide 40: Design: Material Choice
Transmission in %
Wavelength(nm)
AFTER 1kGy
450nm
Irradiation of 3cm long samples with a source = Co60 γ rays (E~1MeV), for the expected 1kGy dose at GL6.
HSQ300 (=HSQ330, not certified %impurities)
HSQ330 (certified %impurities)
Suprasil (synthetic quartz)
Degradation of the transmission coefficient for λ<450nm for the HSQ.
No loss for Suprasil but more expensive.

## Slide 41: Design: Length
The longer the bar, the more photons produced by the crossing particle.
Defining roughly a directionality metric as the mean number of photoelectrons at the PMT for a forward particle over respective number for a backward particle.
  Example: [#ph.e. at PMT for 5deg]/[#ph.e. at PMT for 175deg]
Directionality
Geant4

## Slide 42: Design: Length
The longer the bar, the more photons produced by the crossing particle.
Defining roughly a directionality metric as the mean number of photoelectrons at the PMT for a forward particle over respective number for a backward particle.
  Example: [#ph.e. at PMT for 5deg]/[#ph.e. at PMT for 175deg]
Directionality(left) for 0deg (blue top line) is decreasing as the length decreases but not much as the absolute number of ph.e. at the PMT for 0deg.
Length[cm]
[#ph.e. at PMT]
Directionality
0deg
Geant4
Geant4

## Slide 43: Design: Length
  The longer the bar, the more photons produced by the crossing particle
  => Can set a higher discriminator threshold to:
    Suppress more the backward signal to less than 0.1%
    Decrease the effect of the signal produced at the PMT window and not in the bar.

## Slide 44: Design: Length
  The longer the bar, the more photons produced by the crossing particle
  => Can set a higher discriminator threshold to:
    Suppress more the backward signal to less than 0.1%
    Decrease the effect of the signal produced at the PMT window and not in the bar.
  The longer the bar the more exposed to pp.
    Muons from MIB are very angular (0-15deg) while PP is spread in angles.
0deg
MIB
PP
PP

## Slide 45: Design: Length
  The longer the bar, the more photons produced by the crossing particle
  => Can set a higher discriminator threshold to:
    Suppress more the backward signal to less than 0.1%
    Decrease the effect of the signal produced at the PMT window and not in the bar.
  The longer the bar the more exposed to pp.
    Muons from MIB are very angular (0-15deg) while PP is spread in angles.
  => Orientation in the cavern such that the acceptance of MIB increases.
    MIB particles would “see” the projection of the bar.
0deg
MIB
MIB
φ deg
PP
PP
PP
PP

## Slide 46: Design: Length
Work in progress:
  Geant4 simulations to estimate the expected number of ph.e. at the PMT (for the both PMT cases) based on the
    Entry point
      Radius, if front/back face
      Z, if side of the bar
    Entering angle
  Create a LUT based on the above results f(r,θ,z)
  Find the optimal orientation for the input files from FLUKA.

## Slide 47: Design: Radius
Radius depends on
  The acceptance
    The larger radius the more sensitive to MIB.
  The PMT choice
    If the R2059 PMT is chosen (cathode d=4.6cm), and the bar has d=4.5cm, then the whole exiting area of the bar shall be covered by the cathode.
    If the R7600U-M4 is chosen (cathode 1.8cmx1.8cm), and the bar has radius larger than the PMT, then a large portion of the photon yield is lost at the outer radius

## Slide 48: Design: Surface properties
TOLERANCE
Radius[cm]
R
+-5%
+-0.075cm
TOLERANCE
  Manufactures provide a tolerance of +-1.5mm in diameter.
  Geant4 simulations show that tolerance should affect the number of ph.e. no more than 5%.
ROUGHNESS
  Roughness of the PMT window is not exceptional
  No extra polishing other than the default one will be asked, for the moment.
Geant4

## Slide 49: Design: Optical Coupling
From July 2012 test beam data where the PMT were stuck to the bar without any optical material, there was a low angle behavior due to the refraction in air caused by airgap.
Proof of the need of an optical material to couple the PMT with the bar.
Options:
  optical glue
  silicon gel disk.
Low angle behavior verified with Geant4 simulations by M.Ambrose.

## Slide 50: Design: Photomultipliers-Characteristics
Hamamatsu R2059
Hamamatsu R7600-M4
 | R2059 | R7600-M4
Spectral response | 160 to 650nm | 300 to 650nm
Effective area | d= 46mm | Side= 1.8 x 1.8cm2
 | Area= 16.6cm2 | Area=3.24cm2
Rise time | 1.3ns | 1.2ns
#channels | 1 | 2x2
Photocathode shape | circular | square
Window thickness | 1mm-8mm | 0.6mm
Window shape | planoconcave | plane
Due to fake hits in the R2059 window started considering R7600-M4 (also used as an upgrade in HF for R7525 )

## Slide 51: Design: Photomultipliers- Fake hits
R2059
R7600-M4
From December 2012 test beam, below the signals for 0deg and 180deg signal contribution produced in the PMT windows (no bar measurements).
Both photomultipliers give fake hits.
Confirmed also from Geant4 simulations.
Sum of max amplitude of each channel(V)

## Slide 52: Design: Photomultipliers- Output signal
Maximum amplitude plots for several case from December test beam.
Test beam data still under study.
Lower amplitude fake signal but also real signal for R7600M4 compared to R2059.
Longer bar to set higher threshold.
R7600M4
R2059
Sum of max amplitude of each channel(V)

## Slide 53: Design: Photomultipliers- Performance with large R bar
R7600M4
Geant4
M.Ambrose
R2059
Detection efficiency plot for the R2059 PMT, only for particles that went for sure through the r=1.75cm bar (smaller trigger acceptance).
Discrimination Voltage | 1.6V | 4.2V
Backward Acceptance | 0.16% | 0.02%
Forward Acceptance | 99.5% | 94%
Dec.test beam data
From simulations HFPMT seems to lose a lot of photon rate for particles that enter in the outer radius of the bar (r=2.5cm).
R2059

## Slide 54: Design: Photomultipliers- Choice
RATE
  Photocathode area: R2059 (16.6cm2) >> R7600 (3.24cm2)
  Radial acceptance: R2059
FAKE HITS
  Window thickness: R7600 (0.6mm) << R2059 (up to 8mm)
  Both windows contribute (according to test beam and for R2059 confirmed by Geant4).
    R7600 provides the feature to reject based on the 4 channels signal => future upgrade option.
    A longer bar could compensate the high rate of fake hits in R2059 since it provides the benefit to set a higher threshold.

## Slide 55: Design: Summary
The baseline is a 4.5cm diameter, 10cm long bar with R2059 and an optical medium for the coupling.
OPEN QUESTIONS
  R2059 VS HFPMT
    HFPMT, If we consider an upgrade where the feature of rejecting the fake hits could be used.
    HFPMT, if test beam data prove that has good enough directionality.
    HFPMT, if for big radius bar and different orientation the acceptance increases sufficiently.
  Radiation hardness of the material
    Suprasil shows no loss in the UV area but is more expensive.
  Optical material for coupling.

## Slide 56: Plans.
Use full set of test beam data to decide on the efficiencies of the PMTs.
Apply the FLUKA output results (expected fluxes) to the LUT for the response for the two PMTs and compare.
Finalize the choices for the quartz:
  Radius and length depends also on the choice of the PMT and vice versa.
FLUKA activation for Golden Location 6.
Use the rates from FLUKA to decide optimal orientation in the cavern .
Estimate the systematics in Geant4.
Check radiation hardness of optical materials.
Start constructing a prototype.
Test prototype in November.
S
P
R
I
N
G
SUMMER
FALL

## Slide 57: Thank you!

## Slide 58: BACK-UP slides

## Slide 59: MIB-FLUKA

## Slide 60: Angle VS Energy MIB
BGE
BΗ
BGΙ

## Slide 61: Ekin Vs time MIB
There is a high energy tail that it is produced along the LSS (before the TCTs) but with very few entries.

## Slide 62: MIB time- components and particle species. Mostly e-+ and mu.

## Slide 63: WHERE THE MIB MUONS ARE BORN? Beam halo at TCTs
Most of the arriving particles were born ~450-500ns before -> ~150m away -> TCTs

## Slide 64: Pp-products, timing FLUKA

## Slide 65: TIMING for pp products from IP to tunnel-particle species

## Slide 66: TIMING for pp products from IP to tunnel- shielding & rms
Above Cherenkov Threshold
With Shielding (e-+>10MeV)
215 entries,
rms 3.8ns
305 entries,
Rms 18ns
Shielding and timing are also helping at rejecting most of the background coming from the opposite side of the signal.

## Slide 67: TIMING for pp products fron tunnel to IP (fake signal)
PP collision products arriving at the same direciton of the signal (fake signal) sharply in time .
This will allow us to get rid of the fake signal with gating in time.

## Slide 68: TEST BEAM SETUP

## Slide 69: Test beam setup
Scint.tile
Scint.tile
Small
Scint.
beam

## Slide 70: Test beam setup
Small
Scint.
beam
Scint.tile
Scint.tile

## Slide 71: RESPONSE FUNCTION

## Slide 72: RESPONSE function with R2059 PMT entering from the side of the bar

## Slide 73: RESPONSE function with R2059 PMT entering at the front at different radius

## Slide 74: RESPONSE function with R2059 PMT entering at the front at different radius