## Slide 1: Low-Latency 1D Image Detector Realized as an AMC Module
A teamwork of:
Aleksander Mielczarek
Grzegorz Jabłoński
Dariusz Makowski
Piotr Perek
Bernd Steffen
Christopher Gerth
Lodz University of Technology
Department of Microelectronics
and Computer Science

## Slide 2: 1D Image Detector Usage Scenarios
2

## Slide 3: 1D Image Detector Requirements
Operation in MicroTCA crate
1 MHz full-line readout
About 256 pixels
Si and InGaAs photodiode arrays
3
Example commercial solution:
256 pixels
Serial analogue readout over 2 lines
1 MHz readout clock
128 times slower than required!

## Slide 4: 1D Image Detector System Structure
4

## Slide 5: 1D Image Detector Dedicated Sensor Solution
Photodiode Array:
Photodiode size: 50 x 500 μm
Organization: 1 x 256 pixels
Material: InGaAs, ~1300 nm
Readout circuit:
Beetle chip (designed for LHCb)
128 charge sensitive channels
Up to 1.1 MHz full readout rate
Four-port analogue readout
Analogue pipeline
5

## Slide 6: 1D Image Detector Hardware Design
6
Ooops!

## Slide 7: 1D Image Detector DAQ Module + Signal Conditioning
7

## Slide 8: 1D Image Detector Spectrometer Setup
8
Synchronous operation
Diffraction grating
Spectrum analysis
Verified with commercial wavelength analyzer

## Slide 9: 1D Image Detector Preliminary results
9
Smashed bonding
Notes: Basically, it works
Many benefits of AMC/FMC compliance: scalability, performance, RAMI
Some drawbacks, but the module is still very useful

## Slide 10: 1D Image Detector Summary
10
Fast 1D detector (1 MHz full-line readout )
Capable of working with femtosecond light pulses
Can be used as part of the spectrometer
Remember to protect your bond wires
Notes: Basically, it works
Many benefits of AMC/FMC compliance: scalability, performance, RAMI
Some drawbacks, but the module is still very useful

## Slide 11: 1D Image Detector Thank You for Your Attention
11
Your questions are welcome