## Slide 1: Possible Diamond Measurements
CMS/Fcal Meeting
Maria Hempel
Possible Diamond Measurements
Zeuthen, 08.05.2013

## Slide 2: Outlook
Transient Current Technique - TCT
CCE vs HV Measurements
CCE vs Time Measurements
IV- Measurements
I-t Measurements
Thermally Stimulated Current - TSC

## Slide 3: Transient Current Technique
Information about electrical field in diamond
  Polarization effect visible
Equipment:
  Amplifier ü
  Scope ü
  α- source ü
Konstantin is working on the setup
  Sensitive amplifier
  Many noise

## Slide 4: CCE vs HV Measurements
Information about saturation and noise
Equipment:
  Old box of Sergej: diamond in frame, contact with wires ü
  New box of Sergej: metalized diamond, contact with needle ü
  Power supply ü
  β -source ü
  PC ü
  Software to readout ADC ü
  Software for automated readout  has to be installed
Constant HV measurements  polarization effect
Alternating HV measurements  no polarization

## Slide 5: CCE vs Time Measurements
Information about polarization effect
Equipment:
  New box: metalized diamond, contacting with needle ü
  Power supply ü
  PC ü
  Software for ADC readout ü
  β -source ü
  Software for automated readout process  to be checked
Constant HV: with pumping the polarization effect is visible over time
Alternating HV: with pumping an increase of the CCE over time

## Slide 6: IV- Measurements
Information about leakage current
Equipment:
  Probe station of Matthias: metalized diamond, contact with needle ü
  Probe station of Wolfgang: metallized diamond, contact with needle ü
  Box of Konstantin: diamond in frame, contact with frame ü
  PC ü
  Software for readout ü
Can we put the small probe station in the lab?

## Slide 7: I-t Measurements
Information about erratic current
Equipment:
  One box in the lab: diamond in frame, contact with wires ü
  Probe station of Wolfgang: metalized diamond, contact with needle ü
  Software has to be set up
  Probe station software is already installed in the lab ü
  β-source is needed for pumping ü
Best solution:
  probe station in the lab
  Using a β-source
  No frames needed

## Slide 8: Thermally Simulated Current Measurements
Information about traps in diamond
we have an old setup from Martin
Jannis will set it up again

## Slide 9: Summary
Question: Are we making the measurements only without frame?
  Yes: we need the probe station in the lab
  No: we have to make first the measurements with the needle and then bond the diamonds and start the measurements that require the wires
Can we set up the probe station in the lab?
  Yes: Who can help me?
  No: 
we will order the laser diode for making tests of CCE
  Found something on THORLABS
  Order a 850nm VCSL laser diode (26€) and 650nm laser diode (11€)