## Slide 1
The Status of the FADC Firmware
Richard Thalmeier (HEPHY Vienna)
4th Belle 2 PXD/SVD workshop at DESY

## Slide 2: SVD Readout Scheme
Front-end hybrids
with 1748x APV25-chips,
128 analog
channels each, on 172 sensors.
344 x ~2m copper cable
8x Junction boxes with
rad-hard
DC/DC-
converters
172 x copper
cables, ~10m, time multiplexed analog voltages
48x FADC
in 4 crates.
48x Optical data
Links (>20m)
COPPER
Pixel Detector
Data Acquisition (DAQ)
....
48x
FTB

## Slide 3: FADC Block Diagram
Analog & digital level translation between  bias (<  100V) and GND
Digitization, signal conditioning (FIR filter), data processing
Central FPGA is an Altera Stratix IV GX

## Slide 4: FADC Hardware

## Slide 5: The Connectivity-Test June 2013: FADC – FTB - Copper

## Slide 6: The Connectivity-Test June 2013: The ROM- and VHDL-generator
Perl program which generates a VHDL-file and all files needed (including all quartus project files (!), pin definitions and batch files) for Quartus to compile and flash it into the FPGA fully automatized
Command line parameters for data format (raw, transparent, zero-suppressed, zero-suppressed+hit-finding), number of events, channels per event, words per channel, pause ticks, randomization of all relevant parameters, probabilities for APV25-errorbits, etc...
Output of the data additionally as files in different file formats, including ASCII-binary („0101“...), Hex-file, Plain binary, each with and without CRC, for data comparisation.

## Slide 7: The FADC Firmware

## Slide 8: FADC – Firmware-Development: Done:
VME-bus Struck – National- Instruments – command-wrapper
VME-bus-interface in the Cyclone
Communication Cyclone  Stratix (Serial LVDS interface)
Protocols VME  Cyclone  Stratix
7-Segment-Display (SPI-interface)
RGB-LEDs (SPI-interface)
Jitter-Cleaner
Delay25 (I²C-interface)
APV25-programming (I²C-interface)
Readout of the 48 ADCs (Serial LVDS interface)
FIFOs for reading out realtime APVdata to VME
Reordering of the APV25 data
CRC16 calculation
And lots of Hardware-debugging...

## Slide 9: FADC – Firmware-Development: Done:
VME-bus Struck – National- Instruments – command-wrapper
VME-bus-interface in the Cyclone
Communication Cyclone  Stratix (Serial LVDS interface)
Protocols VME  Cyclone  Stratix
7-Segment-Display (SPI-interface)
RGB-LEDs (SPI-interface)
Jitter-Cleaner
Delay25 (I²C-interface)
APV25-programming (I²C-interface)
Readout of the 48 ADCs (Serial LVDS interface)
FIFOs for reading out realtime APVdata to VME
Reordering of the APV25 data
CRC16 calculation
And lots of Hardware-debugging...

## Slide 10: FADC – Firmware-Development: Done:
VME-bus Struck – National- Instruments – command-wrapper
VME-bus-interface in the Cyclone
Communication Cyclone  Stratix (Serial LVDS interface)
Protocols VME  Cyclone  Stratix
7-Segment-Display (SPI-interface)
RGB-LEDs (SPI-interface)
Jitter-Cleaner
Delay25 (I²C-interface)
APV25-programming (I²C-interface)
Readout of the 48 ADCs (Serial LVDS interface)
FIFOs for reading out realtime APVdata to VME
Reordering of the APV25 data
CRC16 calculation
And lots of Hardware-debugging...

## Slide 11: FADC – Firmware-Development: Done:
VME-bus Struck – National- Instruments – command-wrapper
VME-bus-interface in the Cyclone
Communication Cyclone  Stratix (Serial LVDS interface)
Protocols VME  Cyclone  Stratix
7-Segment-Display (SPI-interface)
RGB-LEDs (SPI-interface)
Jitter-Cleaner
Delay25 (I²C-interface)
APV25-programming (I²C-interface)
Readout of the 48 ADCs (Serial LVDS interface)
FIFOs for reading out realtime APVdata to VME
Reordering of the APV25 data
CRC16 calculation
And lots of Hardware-debugging...

## Slide 12: FADC – Firmware-Development: Done:
VME-bus Struck – National- Instruments – command-wrapper
VME-bus-interface in the Cyclone
Communication Cyclone  Stratix (Serial LVDS interface)
Protocols VME  Cyclone  Stratix
7-Segment-Display (SPI-interface)
RGB-LEDs (SPI-interface)
Jitter-Cleaner
Delay25 (I²C-interface)
APV25-programming (I²C-interface)
Readout of the 48 ADCs (Serial LVDS interface)
FIFOs for reading out realtime APVdata to VME
Reordering of the APV25 data
CRC16 calculation
And lots of Hardware-debugging...

## Slide 13: FADC – Firmware-Development: Done:
VME-bus Struck – National- Instruments – command-wrapper
VME-bus-interface in the Cyclone
Communication Cyclone  Stratix (Serial LVDS interface)
Protocols VME  Cyclone  Stratix
7-Segment-Display (SPI-interface)
RGB-LEDs (SPI-interface)
Jitter-Cleaner
Delay25 (I²C-interface)
APV25-programming (I²C-interface)
Readout of the 48 ADCs (Serial LVDS interface)
FIFOs for reading out realtime APVdata to VME
Reordering of the APV25 data
CRC16 calculation
And lots of Hardware-debugging...

## Slide 14: FADC – Firmware-Development: Done:
VME-bus Struck – National- Instruments – command-wrapper
VME-bus-interface in the Cyclone
Communication Cyclone  Stratix (Serial LVDS interface)
Protocols VME  Cyclone  Stratix
7-Segment-Display (SPI-interface)
RGB-LEDs (SPI-interface)
Jitter-Cleaner
Delay25 (I²C-interface)
APV25-programming (I²C-interface)
Readout of the 48 ADCs (Serial LVDS interface)
FIFOs for reading out realtime APVdata to VME
Reordering of the APV25 data
CRC16 calculation
And lots of Hardware-debugging...

## Slide 15: FADC – Firmware-Development: Done:
VME-bus Struck – National- Instruments – command-wrapper
VME-bus-interface in the Cyclone
Communication Cyclone  Stratix (Serial LVDS interface)
Protocols VME  Cyclone  Stratix
7-Segment-Display (SPI-interface)
RGB-LEDs (SPI-interface)
Jitter-Cleaner
Delay25 (I²C-interface)
APV25-programming (I²C-interface)
Readout of the 48 ADCs (Serial LVDS interface)
FIFOs for reading out realtime APVdata to VME
Reordering of the APV25 data
CRC16 calculation
And lots of Hardware-debugging...

## Slide 16: FADC – Firmware-Development: Done:
VME-bus Struck – National- Instruments – command-wrapper
VME-bus-interface in the Cyclone
Communication Cyclone  Stratix (Serial LVDS interface)
Protocols VME  Cyclone  Stratix
7-Segment-Display (SPI-interface)
RGB-LEDs (SPI-interface)
Jitter-Cleaner
Delay25 (I²C-interface)
APV25-programming (I²C-interface)
Readout of the 48 ADCs (Serial LVDS interface)
FIFOs for reading out realtime APVdata to VME
Reordering of the APV25 data
CRC16 calculation
And lots of Hardware-debugging...

## Slide 17: FADC – Firmware-Development: Done:
VME-bus Struck – National- Instruments – command-wrapper
VME-bus-interface in the Cyclone
Communication Cyclone  Stratix (Serial LVDS interface)
Protocols VME  Cyclone  Stratix
7-Segment-Display (SPI-interface)
RGB-LEDs (SPI-interface)
Jitter-Cleaner
Delay25 (I²C-interface)
APV25-programming (I²C-interface)
Readout of the 48 ADCs (Serial LVDS interface)
FIFOs for reading out realtime APVdata to VME
Reordering of the APV25 data
CRC16 calculation
And lots of Hardware-debugging...

## Slide 18: FADC – Firmware-Development: Done:
VME-bus Struck – National- Instruments – command-wrapper
VME-bus-interface in the Cyclone
Communication Cyclone  Stratix (Serial LVDS interface)
Protocols VME  Cyclone  Stratix
7-Segment-Display (SPI-interface)
RGB-LEDs (SPI-interface)
Jitter-Cleaner
Delay25 (I²C-interface)
APV25-programming (I²C-interface)
Readout of the 48 ADCs (Serial LVDS interface)
FIFOs for reading out realtime APVdata to VME
Reordering of the APV25 data
CRC16 calculation
And lots of Hardware-debugging...

## Slide 19: FADC – Firmware-Development: Done:
VME-bus Struck – National- Instruments – command-wrapper
VME-bus-interface in the Cyclone
Communication Cyclone  Stratix (Serial LVDS interface)
Protocols VME  Cyclone  Stratix
7-Segment-Display (SPI-interface)
RGB-LEDs (SPI-interface)
Jitter-Cleaner
Delay25 (I²C-interface)
APV25-programming (I²C-interface)
Readout of the 48 ADCs (Serial LVDS interface)
FIFOs for reading out realtime APVdata to VME
Reordering of the APV25 data
CRC16 calculation
And lots of Hardware-debugging...

## Slide 20: APV25 => Cabling => ADC => Stratix => Cyclone => VME => PC

## Slide 21: FADC – Firmware-Development: Done:
VME-bus Struck – National- Instruments – command-wrapper
VME-bus-interface in the Cyclone
Communication Cyclone  Stratix (Serial LVDS interface)
Protocols VME  Cyclone  Stratix
7-Segment-Display (SPI-interface)
RGB-LEDs (SPI-interface)
Jitter-Cleaner
Delay25 (I²C-interface)
APV25-programming (I²C-interface)
Readout of the 48 ADCs (Serial LVDS interface)
FIFOs for reading out realtime APVdata to VME
Reordering of the APV25 data
CRC16 calculation
And lots of Hardware-debugging...

## Slide 22: FADC – Firmware-Development: Done:
VME-bus Struck – National- Instruments – command-wrapper
VME-bus-interface in the Cyclone
Communication Cyclone  Stratix (Serial LVDS interface)
Protocols VME  Cyclone  Stratix
7-Segment-Display (SPI-interface)
RGB-LEDs (SPI-interface)
Jitter-Cleaner
Delay25 (I²C-interface)
APV25-programming (I²C-interface)
Readout of the 48 ADCs (Serial LVDS interface)
FIFOs for reading out realtime APVdata to VME
Reordering of the APV25 data
CRC16 calculation
And lots of Hardware-debugging...

## Slide 23: FADC – Firmware-Development: Done:
VME-bus Struck – National- Instruments – command-wrapper
VME-bus-interface in the Cyclone
Communication Cyclone  Stratix (Serial LVDS interface)
Protocols VME  Cyclone  Stratix
7-Segment-Display (SPI-interface)
RGB-LEDs (SPI-interface)
Jitter-Cleaner
Delay25 (I²C-interface)
APV25-programming (I²C-interface)
Readout of the 48 ADCs (Serial LVDS interface)
FIFOs for reading out realtime APVdata to VME
Reordering of the APV25 data
CRC16 calculation
And lots of Hardware-debugging...

## Slide 24: What is left to do until the beamtest
Common Mode Correction
Zero-Suppression
Generating the three runtype Data Formats (Raw mode, Transparent Mode, Zero Suppressed Mode)
FADC-Controller: End of November with Katsuro (in Vienna)
Testing, testing, testing, testing, testing, testing, testing, testing, testing...

## Slide 25: Belle II FADC Firmware Development: Milestones and Conclusions
I joined the Belle II project in April 2013
End of June 2013: Connectivity Test FADC  FTB  Copper with APV25 data simulated by the Cyclone on the FADC -successful.
End of November 2013 (right after B2GM): Connectivity Test with real APV25 data.
January 2013: Beam Test at DESY
  I will be there for 1 week in December and full January

## Slide 26: The End...
Thank you for your attention!

## Slide 27: Backup slides...

## Slide 28: The Connectivity-Test June 2013: The ROM- and VHDL-generator (1/2)
Perl program, self-explaining help included
Inputs (per command line parameters):
  Data Format (Run type): raw, transparent, zero-suppressed, zero-suppressed+hit-finding,
  Number of events, channels per event, words per channel, pause ticks,
  Randomization for above numbers,
  Probabilities for APV25-errorbits (for all Run types except raw) and for bad hits (for zero-suppressed mode)

## Slide 29: The Connectivity-Test June 2013: The ROM- and VHDL-generator (2/2)
Output file formats:
  ASCII-binary („0101“...), with and without CRC
  Hex-file, with and without CRC
  Plain binary, with and without CRC
  VHDL-file, pin-definition-file, constraints-file, all ready for compilation and flashing
Batch files
  They create all files needed for Quartus
  They compile and flash them fully automated into the FPGA

## Slide 30: The Connectivity-Test June 2013: The VHDL file
Trigger
Select
Trigger
Output
(2 clks)
Trigger
Edge
Detect
(1 clk)
Trigger
Delay
(8 clks)
Trigger
Count
ROM-
counter
ROM
TestpinO
SPOU1
Testpin1
Clk
Clk
up
Trigger-
Edge
SPin1
Trigger
down
Trailer
&
BsyFTB
ROM-Output-switcher
ROM
out
000...
XD
Trigger-enabled
Addr
Clk
Clk
Clk
Clk
FADCRDY
Trailer,
Header,

## Slide 31: Wave samples (1/5)
One single trigger detected, no BSYFTB:

## Slide 32: Wave samples (2/5)
7 Triggers detected, 4 queued, no BSYFTB:

## Slide 33: Wave samples (3/5)
More than 5 Triggers queued, no BSYFTB:

## Slide 34: Wave samples (4/5)
At most 10 triggers are queued, and BSYFTB:

## Slide 35: Wave samples (5/5)
Unqueuing triggers, entering idle mode:

## Slide 36
48 ADCs AD9222
Main FPGA Altera Stratix IV
VME-controller Altera Cyclone II
Clock-Jitter- Cleaner SI5317
Analog level translators (capacitive
couplers)
Digital level translators (inductive c ouplers)
Analog and digital data from/to 48x APV25
VME bus
To the DAQ
LVDS- Buffers
FIN1108
Gigabit- Ethernet
7-Segm
RGB-LEDs
Delay25