## Slide 1
Optimisation Studies
for the BeamCal Design
Lucia Bortko, DESY – Zeuthen
FCAL Meeting | DESY - Zeuthen | 7-8 Oct 2013

## Slide 2: The Aim and Content
The Aim: • compare 2 types of segmentation of calorimeter
• investigate the characteristics
Content: • Introduction
• Simulation studies
- SNR
- efficiency of reconstruction of showers
- range of charge deposited into the pads
- dependence vs
- energy resolution
- spatial resolution
• Conclusion
Notes: Since one of the tasks of BeamCal is to measure single high-energetic electrons (sHEe), the goal of finding better segmentation of calorimeter for this purpose was made.
Finding an optimum segmentation for better reconstruction of single high-energetic electrons (sHEe).

## Slide 3: Beam Calorimeter for ILC
30 layers
Tungsten absorber
Diamond sensor
Readout plane/air gap
1
Graphite absorber
BeamCal aimed:
Detect sHEe
- Determine Beam Parameters
Masking backscattered low energetic particles
Beam parameters from the ILC Technical Design Report (November 2012)
- Nominal parameter set
- Center-of-mass energy 1 TeV
FE

## Slide 4: BeamCal Segmentation
Uniform
Segmentation (US)
pads size are the same
Proportional
Segmentation (PS)
pads size are proportional to the radius
Similar number of channels
Y, cm
Notes: Skazat chto vsebylo poschitano dlya Diamond??
Find number of channels for each segmentation(~ 70000 in total? And in 1 layer)

## Slide 5: Energy Deposition due to Beamstrahlung
US
RMS
PS
Beamstrahlung (BS) pairs generated with Guinea Pig
Energy deposition in sensors from BS simulated with BeCaS (Geant4)
→ considered as
Background (BG)
RMS of the averaged BG
→ considered as
noise (for SNR)
is the same, but
/pad is different!
Average
10 BX
Figures show sum of all layers
Average
10 BX
Notes: Skazat pro to chto tak kak yadro livnya okolo 2?mm to umenshaya razmer yacheek na malyh radiusah my umenshaem shum ot bg, signal net, sledovatelno ozhidaem luchizhiy SNR
Put pictures for rms?? Or
- Put histo bg(radius) with rms as errors?? For all layers or for layer with maximum energy deposition?

## Slide 6: Shower from Single High Energy Electron
Showers are simulated with BeCaS (Geant4)
Investigated energies: 10, 20, 50, 100, 200, 500 GeV
Shower from 100- GeV electron
Maximum in
10th layer
(average over 10 showers)
= 100 GeV
Longitudinal shower profile

## Slide 7
Proportional
Segmentation
Uniform
Segmentation
The average energy in the pad of the core of shower
RMS of the averaged Background
Signal and RMS for both Segmentations
20 bunch crossings were given
Signal nearly segmentation-independent!
Different distributions!
Proportional
Segmentation
Notes: SIGNAL ALMOST INDEPENDET OF SEGMENTATION!!
Peredelat grafik dlya rms chtob y os’ u PS byla takaya zhe kak u US

## Slide 8
SNR in cell with maximum 𝐄_𝐝𝐞𝐩
SNR =
= 50 GeV
= 100 GeV
PS
US
PS
US
Notes: SDELAT’ v log – shkale!!!!!!

## Slide 9
Efficiency of Showers Reconstruction
PS
US
= 200 GeV
Radius, cm
PS
US
= 50 GeV
Efficiency =
Notes: SDELAT’ v log – shkale!!!!!!

## Slide 10: Charge Range Estimate
Diamond
PS
US
PS
US
Distribution of the collected charge per pad from Background for Diamond
Distribution of the collected charge per pad from 500Gev electron for Diamond
Showers
Background
 | Diamond | GaAs
Charge collected from MIP | 2.44 fC | 4.29 fC
Maximum collected charge from 500GeV electron | 12 214 fC | 21 497 fC
 | Correspond to about 5 000 MIPs | 
For sensor pad thickness 300 µm:
Notes: Ukazat kak rasschety provedeny? T.k energovydeleniye na yacheyku rastet (grubo) lineyno. I my znaem enorgovydeleniye dlya 100GeV – nogo electrona
Sdelat bolshe statistiki -> dodelat kod s ringo chtoby mozhno bylo mnogo input failov podavat’ v programmu bgaver_for_thisto_charge_collection…bla-bla-bla….

## Slide 11
Deposited Energy vs Energy of Electron
Energy deposition (GeV)
Number of events
y = 0,017x + 0,0051
Notes: SDELAT’ v log – shkale!!!!!!

## Slide 12
Energy Resolution vs Energy of Electron
Energy Resolution
Energy of Electron (GeV)
Notes: SDELAT’ v log – shkale!!!!!!

## Slide 13: Spatial Resolution ( In Progress)
Estimation
PS
US
COG
= 2.9%
= 1.65 deg
= 2.21 mm
= 2.16 mm
0
4
5
2
1
3
6
x
y
= 0.609 mm
= 3.97 mm
= 5.14 deg
= 0.848 deg

## Slide 14: Spatial Resolution ( In Process)
Corrected COG
Energy of Electron
Gaussian fit
-
0
∆R
∆R
Parameters

## Slide 15: Conclusion
Performance of BeamCal for two different sensor segmentations is compared
  Number of readout channels is kept similar
  Signal from sHEe nearly independent of the segmentation
  Energy deposition per pad from Beamstrahlung differs significantly
  Proportional segmentation improves the signal-to-noise ratio
  Proportional segmentation gives better reconstruction efficiency
The charge range has been estimated
  Collected charge per pad from sHEe nearly independent of the segmentation
  Collected charge per pad from BS for US in 6 times bigger than for PS
Energy deposition was investigated
  Dependence between energy of electron and deposited in calorimeter energy is linear.
  Deposited in sensors energy is 1,7% from the original energy of electron.
  Dependence energy resolution vs energy of electron is calculated and parameterized.
  Calorimeter gives good energy resolution: 2% for 100GeV electron.

## Slide 16
Thank you for your attention!

## Slide 17
Backup slides

## Slide 18
Layer 7
Layer 11
Shower maximum – Layer 9
PS
US
PS
US
PS
US
SNR for 50 GeV Electron
SNR in cell with maximum

## Slide 19
Layer 6
Layer 10
Shower maximum – Layer 8
PS
US
PS
US
PS
US
SNR for 20 GeV Electron

## Slide 20
Layer 5
Layer 9
SNR for 10 GeV Electron
PS
US
PS
US
PS
US
Shower maximum – Layer 7
Notes: +2 -2 layers – it is kind of testing of stability of our result
Dlya nizkih energiy mozhet byt chto snr v 9 sloe luchshe chem v 7 t.k. v 7om sloye bg vnosit bolshiy vklad.
Переделать все графики снр если останется время.

## Slide 21: Charge range estimate
For Diamond sensor pad thickness 300 µm:
- Charge collected from MIP: 2.44 fC
- Maximum charge collected – for shower from 500 GeV electron: 12214 fC
(correspond to about 5000 MIPs)
Diamond
GaAs
Distribution of the collected charge per pad for 500Gev electron showers
Notes: Ukazat kak rasschety provedeny? T.k energovydeleniye na yacheyku rastet (grubo) lineyno. I my znaem enorgovydeleniye dlya 100GeV – nogo electrona
Sdelat bolshe statistiki -> dodelat kod s ringo chtoby mozhno bylo mnogo input failov podavat’ v programmu bgaver_for_thisto_charge_collection…bla-bla-bla….

## Slide 22
Diamond
GaAs
Blue – Uniform Segmentation
Orange - Proportional
Green – Uniform Segmentation
Blue - Proportional
Distribution of the collected charge per pad for 500Gev electron showers

## Slide 23
Efficiency of Showers Reconstruction
Efficiency for 50 GeV
= 200 GeV
PS
US
Efficiency =
Notes: SDELAT’ v log – shkale!!!!!!

## Slide 24
Proportional
Segmentation
Uniform
Segmentation
The average energy in the pad of the core of shower
RMS of the averaged Background
Uniform
Segmentation
Signal and RMS for both Segmentations
20 bunch crossings were given
Signal nearly segmentation-independent!
Different distributions!
Proportional
Segmentation
Notes: SIGNAL ALMOST INDEPENDET OF SEGMENTATION!!
Peredelat grafik dlya rms chtob y os’ u PS byla takaya zhe kak u US