## Slide 1: Infrastructure for very forward calorimeters TEST BEAM PREPARATION DESY Hamburg 01/2013
7/10/2013
In collaboration with:
François-Xavier Nuiry Szymon Kulis
Andrea Catinaccio Jakub Moron
Konrad Elsener

## Slide 2: Overview
Tungsten plates status
Integration tests summary (services, cooling)
Possible configurations
Transport
Summary
Summary (2) Future electronics
Appendix
-Requirements
-AIDA very forward calorimeter design – reminder –
-Tungsten assemblies in permaglass frames
-Metrology with tungsten plates – Design validation –

## Slide 3: Tungsten plates status
PLANSEE | PLATES | TOLERANCE ASKED | PLANSEE PLATE 1 | PLANSEE PLATE 2 | PLANSEE PLATE 3 | PLANSEE PLATE 4 | PLANSEE PLATE 5
 | Flatness plan A | 10µm | 90 | 10 | 9 | 3 | 7
 | Position opposite plan | 40µm | 40 | 68 | 48 | 56 | 24
MG SANDERS | PLATES | TOLERANCE ASKED | MG SANDERS PLATE 1 | MG SANDERS PLATE 2 | MG SANDERS PLATE 3 | MG SANDERS PLATE 4 | MG SANDERS PLATE 5 | MG SANDERS PLATE 6
 | Flatness plan A | 10µm | 36 | 70 | 108 | 138 | 137 | 37
 | Position opposite plan | 40µm | 214 | 90 | 132 | 288 | 294 | 88
STEEL PLATES | PLATES | TOLERANCE ASKED | Steel plate 1* | Steel plate 2*
 | Flatness plan A | 10µm | 13 | 14
 | Position opposite plan | 40µm | 48 | 46
*Steel plates machined in Belgium in the Britte Mustad company

## Slide 4: Integration tests
2/10/2013
Implementation of a cooling system Checking of the tungsten sandwich
MG Sanders plates

## Slide 5: Integration tests
2/10/2013
Mounting of 2 sensors + their electronic cards Light shielding

## Slide 6: Integration tests
Grounding connections
Cupper cable connected here

## Slide 7: Integration tests
Both orientations tested
-Tungsten plate well supported
-Electronic card well fixed

## Slide 8: Integration tests
Small issue with the sensor support: Very small clash with tungsten supports in certain configurations
Clash here
C=1
A=3.5
Sensor
~10.5
Gap=4.5
Gap=4.5
Gap=4.5
Gap=4.5
Gap=4.5
Gap=4.5
Gap=4.5
~2.5
Electronic board
Gap=4.5
Gap=4.5
Sensor
~10.5
~2.5
Electronic board
Sensor
~10.5
~2.5
Electronic board
BEAM
8
7/10/2013
AIDA Presentation François-Xavier Nuiry
Clash here
Clash here

## Slide 9: Integration tests
Preliminary solution
9
7/10/2013
AIDA Presentation François-Xavier Nuiry
Clash here
C=1
A=3.5
Sensor
~10.5
Gap=4.5
Gap=4.5
Gap=4.5
Gap=4.5
Gap=4.5
Gap=4.5
Gap=4.5
~2.5
Electronic board
Gap=4.5
Gap=4.5
Sensor
~10.5
~2.5
Electronic board
Sensor
~10.5
~2.5
Electronic board
BEAM
9
7/10/2013
AIDA Presentation François-Xavier Nuiry
Clash here
Clash here

## Slide 10: Integration tests
Second solution
Re-machine sensor permaglass supports
Is it really necessary for the next test beam?
10
7/10/2013
AIDA Presentation François-Xavier Nuiry
10
7/10/2013
AIDA Presentation François-Xavier Nuiry
Too thick by ~ 1mm

## Slide 11: Configurations
Tungsten plate 140*140
C=2
A=3.5
Gap=5.5
C=2mm
 We work with an offset of 5.5mm
C=1mm
 We work with an offset of 4.5mm
Tungsten plate 140*140
C=1
A=3.5
Gap=4.5
Distance before next
tungsten
Distance before next
tungsten
BEAM

## Slide 12: 2mm between each tungsten
C=2
A=3.5
Sensor
~10.5
 We work with an offset of 5.5mm
Gap=5.5
Gap=5.5
Gap=5.5
Gap=5.5
Gap=5.5
Gap=5.5
~2.5
Electronic board
Gap=5.5
Sensor
~10.5
~2.5
Electronic board
Sensor
~10.5
~2.5
Electronic board
BEAM
C=2
Gap=5.5
Gap=5.5
C=2
C=2

## Slide 13
Tungsten plate 140*140
A=3.5
Sensor
~10.5
Gap=5.5
Gap=5.5
Gap=5.5
Gap=5.5
Gap=5.5
Gap=5.5
~2.5
Electronic board
Gap=5.5
Sensor
~10.5
~2.5
Electronic board
Gap=5.5
No sensor In this gap
No sensor In this gap
No sensor In this gap
No sensor In this gap
C=2
Electronic board
Sensor
~10.5
~2.5
Electronic board
BEAM
2mm between each tungsten

## Slide 14: 1mm between each tungsten
C=1
A=3.5
Sensor
~10.5
Gap=4.5
 We work with an offset of 4.5mm
Gap=4.5
Gap=4.5
Gap=4.5
Gap=4.5
Gap=4.5
Gap=4.5
~2.5
Electronic board
Gap=4.5
Gap=4.5
No tungsten
Sensor
~10.5
~2.5
Electronic board
Sensor
~10.5
~2.5
Electronic board
BEAM
New set of combs!
C=1
A=3.5
C=1
No tungsten
No tungsten

## Slide 15: Transport CERN – DESY Packaging
First quote got from ORDEM SA
Rigid wood painted box 85 *70 *40 cm
Rigid wood box for tungsten 30 *20 *25 cm
Soft material supplied
Total: 1160 CHF
We are going to ask for a new quote as we want to add dampers / choc absorbers
Vibrations induced by a truck < 30 Hz

## Slide 16: Transport CERN - DESY
Several Possibilities
Standard shipment by truck (Several truck changes)
~ 200 euros Outward + Return
Special shipment by truck (only 1 truck change)
~400 euros Outward + Return
Dedicated transport (fully direct transport)
Outward 580 euros
Return 680 euros
Ourselves (we rent a car)
Expansive
Long travel (1063 km, 10 h)

## Slide 17: Summary
11 tungsten plates ready:
4 with a very good shape
1 correct
6 acceptable for a 1 mm gap configuration, with no guarantee concerning the +/-50µm precision
Several integration tests performed with tungsten and electronics
Mechanical integrity validated in both horizontal and vertical positions
Services supported by the structure
Light shielding (excepted the light coming from the electronic card)
A grounding connection for both tungsten and electronic cards is provided
A cooling system is implemented
A small clash between permaglass frames is detected in 1 configuration.
Could be eventually solved, if necessary?
Which configurations would you like to test during the test beam?
1mm
2mm
both of them
Different tungsten / sensor places…?
What about the Z position of the sensor in between each tungsten?
NEXT STEP
Thin electronic to be installed with the current frame

## Slide 18
Summary (2)
Next electronic generation
Insert a thinner electronic to be able to have a sensor in a 1mm slit (between 2 tungsten plates).
The mechanical infrastructure could be re-used
Modification of the permaglas frame should be done
Any other specific requirements?
Concerning the position of the sensor (X, Y)?
Etc…
Z
X
Y

## Slide 19: APPENDIX

## Slide 20: Requirements
Design and manufacturing of a mechanical structure for tungsten plates and silicon sensors.
A=3.5±0.5mm B=0.32±0.015mm C=2, 1, or 0.5 ±0.05mm D=not really important
Other requirements:
-Necessity to remove sensors and tungsten in a safe and easy way.
-Services have to be held.
-W plates are linked to the ground.
-An electromagnetic + light shielding has to be provided.
-horizontal + vertical position for cosmic muons.

## Slide 21: Global design – reminder –
Cradle, combs, permaglass frames + W plates, hood, services supports
Able to work with 2mm and 1mm gap between tungsten plates

## Slide 22: Tungsten assemblies in permaglass frames
Pneumatic dispenser
Marble
Microscope
Syringe

## Slide 23
Tungsten assemblies in permaglass frames
W
3.5
W
J
A
C
J=C+D-(A+B)
A=3.5 +/-25μm
B=2 +/-2μm
C=5.5 +/-20μm
D=2 +/-2μm
Jmax = 5.520+2.002-3.475-1.998=2.049mm
W
3.5
W
J
A
B
J=B-A
A min=3.475mm
A max=3.525mm
B min=5.480mm
B max= 5.520mm
J max= 5.520-3.470= 2.05mm
J min= 5.480-3.530= 1.95mm
B
D
On the marble
In the calorimeter
1. W plate put on the marble
2. Three red spacer are installed on top of bearings
3. Perm. frame installed around the W plate, supported only on 3 red spacers
4. Glue (Araldite 2011) between W and Permaglass
1. W + Permaglass insertion in combs
2. Accuracy given only by the W machining and the comb machining.

## Slide 24: Metrology with tungsten plates Design validation
9 points are probed on each plate, with the MMT machine.
The distance point-point is measured by the machine.
Only the 1mm gap configuration (1mm gap combs) has been measured.
9 configurations have been tested with 2 plates (each time with 3 different positions)
4 configurations have been tested with 5 plates (each time with 2*2 different positions)
Both orientations were tested (horizontal and vertical beam)
More than 50 measures where done which corresponds to a bit more than 900 probes!
All results are available in the following EDMS document: 1276587

## Slide 25: Metrology with tungsten plates
First example: Measure of the distance between PLANSEE plates 3 and 4
3
4
4
4
Position
Slot 1
Slot 2
Slot 16
Slot 30
1mm
64mm
127mm
Slot | Plate number | Plate average thickness | Theoretical distance – Distance measured
1 | 3 | 3.520 | 
 |  |  | 1.000 – 0.988
2 | 4 | 3.475 | 1.000 – 0.994
 |  |  | 64.000 – 63.981
16 |  |  | 64.000 – 63.993
 |  |  | 127.000 – 126.973
30 |  |  | 127.000 – 126.983

## Slide 26: Metrology with tungsten plates
Second example: Measure of the distance between 5 PLANSEE plates
5
4
3
2
1
Position
Slot 3
Slot 9
Slot 15
Slot 21
Slot 28
23.5mm
50.5mm
77.5mm
109mm
Slot | Plate number | Plate average thickness | Theoretical distance – Distance measured | Distance N / N+1
3 | 5 | 3.490 |  | 
 |  |  |  | 23.526
9 | 4 | 3.475 | 23.500 - 23.526 | 23.508
 |  |  | 23.500 - 23.508 | 23.523
15 | 3 | 3.520 | 50.500 - 50.519 | 23.53
 |  |  | 50.500 - 50.508 | 23.494
21 | 2 | 3.470 | 77.500 - 77.533 | 23.477
 |  |  | 77.500 - 77.505 | 28.049
28 | 1 | 3.505 | 109.000 - 109.052 | 28.023
 |  |  | 109.000 - 108.999 | 

## Slide 27: Metrology with tungsten plates
Third example: Vertical measure of the distance between 5 PLANSEE plates
Slot | Plate number | Plate average thickness | Theoretical distance – Distance measured | Distance N / N+1
3 | 5 | 3.490 |  | 
 |  |  |  | 23.522
9 | 4 | 3.475 | 23.500 – 23.522 | 23.514
 |  |  | 23.500 – 23.514 | 23.507
15 | 3 | 3.520 | 50.500 – 50.507 | 23.499
 |  |  | 50.500 – 50.499 | 23.515
21 | 2 | 3.470 | 77.500 – 77.515 | 23.495
 |  |  | 77.500 – 77.495 | 28.043
28 | 1 | 3.505 | 109.000 – 109.043 | 27.991
 |  |  | 109.000 – 108.991 | 

## Slide 28: Metrology with tungsten plates Conclusions
In most of the configurations the +/-50 microns precision has been respected.
The global shape of each plate is cross check with this 3D measurement
A thin plate will give distances higher than a large plate.
the flatness default can be cross-checked.
Selecting Plansee plates 5, 4, 3, 2, (and 1), in this order, should always give good precision.
An short training of the way to use the calorimeter is necessary.
No measurements were done with MG sanders plates but we should be in nearly all cases out of the +/-50microns asked.

## Slide 29: AIDA very forward calorimeter design Tungsten support
Ground
Spring
Front view
Back view
Material: Epoxy + glass fibres = PERMAGLAS
Tungsten plate is glued inside this frame
3 bearings

## Slide 30
Calorimeter design validation Tests on glued joints
W plate + Permaglas assembly held on 3 points
1Kg
2Kg
During 24 hours
Glued joint
The tungsten plate can be easely removed from the frame while putting it in a methyl chloride bath (the test has been done).

## Slide 31
Silicon sensor
Flexible part
Connector for the read out
Rigid part (PCB)
Next Step...C=0.5 mm
The most important for us:
Realising a flexible link between the sensor and the read out.
Something similar to this example: