RHU-LumiDAQ Integration for BCM1F
Marek Penno, Jessica Leonard
DESY-Zeuthen

---
Scope of LumiDAQ Workshop
- Overview of proposed Lumi DAQ architecture and "lumi- run" control & status of code
- The TTC system upgrade report; Generation & distribution of proposed lumi synchronization signals; schedule for changes in hardware and estimation of dates & procedure for test setup for lumi systems
- Hardware readiness round-table / concerns / clock management, signal distribution / modifications needed to each subsystem backend electronics (HF-lumi, BHM, BCM1F, PLT).
- Estimated data volumes from each system (HF-lumi, BHM, BCM1F, PLT).
- Data publishing and storage
- Planning, synergies & responsibilities

---
RHU Schedule
- 2013-10 - Update PCB Design of RHU
- 2013-10/11 - Production of Prototype
- 2013-11 – TTC Firmware Integration
- 2013-12 - Functional Testing of Prototype
- 2013-12 - Test TTC Input, Firmware Adaption
- 2013-01 - Manufacture all Boards
- 2014-02 - Functional Test of all Boards
- 2014-02 - Full Firmware & Software Adaption
- 2014-04 - Full Test
- 2014-05 - Delivery

---
Firmware Work
2013-11 - Integrate and Test TTC decoding
  - Original TTC firmware is for XILINX  must be adapted for Altera
- 2013-12 Test TTC decoding
- Until 2014-04:
  - Add support for two bunch clock domains (LHC and CMS)
  - Add hardware configuration support for bunch clock selection and switch between LumiDAQ control or legacy DAQ control
  - Integrate TTC LumiDAQ control
    - Extract section and nibble numbers
  - Test TTC LumiDAQ control
  - Test FPGA configuration via CPU to avoid FPGA flash configuration device

---
Bunch Clock Selection
Two clock sources exist:
  - Bunch clock from TTC Signal (CMS clock)
    - Needed for decoding of the TTC signal
  - Bunch clock via NIM input (LHC clock)
    - Needed for DAQ
- RHU DAQ can run on LHC or CMS bunch clock
  - Difficult to implement clock switching in FPGA, need PLL support  need testing first
  - Alternative: two different firmware variants which can be loaded at need (firmware can be switched within some sec. via CPU via network command)

---
TTC Decoding Overview
[Speaker Notes: PLL used for deriving clocks from input clock sources (160Mhz input clock  40Mhz derived with the help of PLL) Phaseshift Controller needed to adjust 40Mhz derived clock phase in 90° steps  must be done to match the original 40Mhz bunch clock of CMS because 40MHz (on the TTC FMC an external clock chip is used for that, which I saved in the RHU design) I²C Interface needed for configuring ADN2818 TTC Data Decoding hopefully original CERN vhdl code can be used for implementation DAQ Clock Selection (see previous slide)  used to choose DAQ clock between LHC and CMS bunch clock. From the TTC Data the b-channel data is extracted and feed to the LumiDAQ Decoder which does manage the Lumi ID and Section ID counting and provides the data to the RHU histogramming DAQ Readout is done via the CPU, data send via network away…. Hope thats all explanary]

---
Data volume for 14256 Bins
Bytes per Histogram (14256 Bins, 2 bytes per bin):	28512.00	bytes
Orbits per Readout (lumi nibble):	4096.00	Orbits
Orbits length in us:	89.90	us
Orbits per Second:	11123.47	Orbits
Histograms per sec:	2.72	hists
Histogram coverage (ms):	368.23	ms
Histogram Data of 48 channels:	668.25	kbytes
Histogram Data of 48 channels/sec:	1814.76	kbytes
- BUT, transferred data will be 3564 bins...
  - -> (1814.76 / 4) kb/s = 453.69 kb/s