## Slide 1
Presented by: Christopher Gerth
Status European XFEL and
Overview on Longitudinal Diagnostics
2nd Mini-Workshop on Longitudinal Diagnostics for FELs
DESY Hamburg
11-12 November 2013
Notes: How to edit the title slide
Fill in the text written in brown

## Slide 2: Civil Construction European XFEL
Three construction sites
5.8 km total length of tunnels
12000 m2 of surface buildings
150000 m3 of underground building volume
3.3 km
We are here
Notes: Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of your talk into this text field 2) The 2 rows in the footer area: Delete the text and write the information regarding your talk (same as on the Title Slide) into this text field.
If you want to use more partner logos position them left beside the DESY logo in the footer area Close Master View

## Slide 3: Layout of European XFEL
20pC | 4.53ps | 1.46ps | 185fs | 5.23fs
100pC | 4.80ps | 1.55ps | 197fs | 11.6fs
250pC | 5.27ps | 1.70ps | 223fs | 25.4fs
500pC | 6.00ps | 1.96ps | 259fs | 43.0fs
1000pC | 6.77ps | 2.23ps | 303fs | 84.0fs
Energy | 130MeV | 600MeV | 2.5GeV | 17.5GeV
Igor Zagorodnov, 2011
  4 accelerating sections
  3 bunch compressor chicanes
tunnel
Injector
building

## Slide 4: Super-Conducting LINAC – Time Structure
RF pulse repetition rate: 10 Hz (up to 25 Hz or cw)
Max. RF flat top length: < 600 μs
Bunch frequency: n*111 ns with n ≥ 2 (1 MHz or 4.5 MHz) => bunch trains with up to 2700 bunches

## Slide 5: Beam Lines and Beam Dumps
3 main beam dumps:
Pave= 300 kW => 1/2 max beam power (1 nC)
beam magnified
slow sweep to distribute heat
Commissioning beam dumps:
To be used as energy spectrometers
Longitudinal Phase Space Measurements with TDS

## Slide 6: Pulse Pattern: Beam Distribution
2 e- beam lines (black), 3 (5) undulator lines (red), 6 (15) instruments
Pulse switching is done with fast kickers: One split per pulse
Both beam lines have same bunch properties
  Arbitrary patterns in each beam line by stopping bunches in pulse picker dump (= commissioning dump)
SQS
SCS
SPB
FXE
MID
HED
e-

## Slide 7: Beam Distribution
SQS
SCS
SPB
FXE
MID
HED

## Slide 8: Beam Distribution
SQS
SCS
SPB
FXE
MID
HED
300 ms

## Slide 9: Beam Distribution
SQS
SCS
SPB
FXE
MID
HED
300 ms

## Slide 10: LLRF – RF pulse for multi modes
RF pulse can be adjusted for 2 (or more) operation modes for different charges. ‘Worst case’ 1nC and 20 pC mode!
Tests at FLASH:

## Slide 11: Overall Time Schedule
Gun Conditioning without beam: December 2013
Injector
  Start Installation diagnostics: mid 2014 (after cryo bypass)
  3.9 GHz module on critical path: installation Feb 2015
  Start injector commissioning: March 2015
Main Linac
  Start installation BC sections: Aug. 2014 (after cryo bypass)
  Start Linac commissioning Jan 2016
  First beam: March 2016
  First SASE: mid 2016

## Slide 12: Longitudinal Diagnostics at the European XFEL
20pC | 4.53ps | 1.46ps | 185fs | 5.23fs
100pC | 4.80ps | 1.55ps | 197fs | 11.6fs
250pC | 5.27ps | 1.70ps | 223fs | 25.4fs
500pC | 6.00ps | 1.96ps | 259fs | 43.0fs
1000pC | 6.77ps | 2.23ps | 303fs | 84.0fs
Energy | 130MeV | 600MeV | 2.5GeV | 17.5GeV
Igor Zagorodnov, 2011
EOD
TDS
EOD
BCM
EOD
BCM
TDS
BCM
BCM
TDS
CRISP4

## Slide 13: TDS: Locations at E-XFEL
BC0
Bunch profile & slice emittance monitor: ‘Steal’ 4 bunches with a fast kicker out of bunch train and deflect them onto view screens
E-spectrometer for Longitudinal Phase Space measurements after FODO section
Disk-Loaded
Travelling Wave
S-Band 2.997 GHz
BC1
BC2
Notes: Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of the EoI for WPnumber 2) The row in the footer area: write the institute name
Close Master View

## Slide 14
Proposal for E-XFEL: Longitudinal phase space monitor
TDS + kicker + septum in BC1: All hardware is developed
Longitudinal Phase Space measurements routinely done at FLASH. However:
Beam operation to be stopped and dipole magnet of E-spectrometer to be switched on/off (and cycled)
To be operated in single-bunch mode (different settings in single- and multi-bunch mode)
No information on actual SASE level during longitudinal phase space measurements
TDS: Longitudinal Phase Space Monitor
BC1
BC2
Simulation of
measurement
Particle
Tracking
M. Yan et al, IPAC’13, MOPME012
Longitudinal Phase Space Monitor for XFEL
Minjie Yan Session 4: TDS and Other

## Slide 15: EOD: Locations at E-XFEL
TDS
TDS
TDS
EOD
EOD
EOD
Only bunch profile monitor after BC0
No EO Diagnostics after BC2 due to limited time resolution (< 150 fs) => Vacuum chamber will be installed for future upgrade option with higher time resolution
=> Session 5: Sub-10fs Diagnostics for fully Compressed Bunches
BC0
BC1
BC2
Notes: Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of the EoI for WPnumber 2) The row in the footer area: write the institute name
Close Master View

## Slide 16: Electro-Optical Diagnostics: Collaborations
16
Beamline Unit
e-
Collaboration between DESY, PSI, KIT for development of EO Diagnostics
Same EO Diagnostics installed at FLASH, SwissFEL Injector and ANKA
SwissFEL Test Injector
=> Session 2: Electro-Optical Diagnostics
Notes: 16
Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of your talk into this text field 2) The 2 rows in the footer area: Delete the text and write the information regarding your talk (same as on the Title Slide) into this text field.
If you want to use more partner logos position them left beside the DESY logo in the footer area Close Master View

## Slide 17
EOD: Laser to RF Synchronization based on LLRF
New: Laser synchronization scheme based on LLRF down-conversion scheme in MTCA.4 standard
EO Laser
MTCA
Experience with RF locking of EO laser based on MTCA.4
Bernd Steffen Session 2: Electro-Optical Diagnostics

## Slide 18: BCM / THz Spectrometer : Locations at E-XFEL
EOD
CRISP4
BCM
BCM
BCM
BCM
TDS
TDS
TDS
EOD
EOD
BC0
BC1
BC2
Notes: Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of the EoI for WPnumber 2) The row in the footer area: write the institute name
Close Master View

## Slide 19: BCM: Bunch Compression Monitor
Layout under development for XFEL
e-
FLASH
SwissFEL Test Injector
Coherent Radiation Diagnostics for European XFEL
Peter Peier Session 3: Coherent Radiation Diagnostics
Fast detectors required (XFEL: 220 ns, SwissFEL: 36 ns)
=> Session 3: Coherent Radiation Diagnostics

## Slide 20
20
THz spectrometer (CRISP4) developed by B. Schmidt (FLA):
2 x FLASH, 1 x FLASH2, 1 x E-XFEL
Reconstruction of bunch profile possible with Kramers-Kronig Relation
Works best with compressed bunches and at high beam energies: => installation behind collimator section with diffraction screen
e-
THz Spectrometer (CRISP4)
E. Hass et al, IBIC’13, MOPC37
Notes: 20
Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of your talk into this text field 2) The 2 rows in the footer area: Delete the text and write the information regarding your talk (same as on the Title Slide) into this text field.
If you want to use more partner logos position them left beside the DESY logo in the footer area Close Master View

## Slide 21: Longitudinal Diagnostics – What is not covered!
time
energy
Arrival Time
BAM
Beam Energy
BPMs in BC (EBPM)
2 BAMs
E-Spectrometer
Energy Spread
VIS SR Monitor (SRM)
E-Spectrometer
Longitudinal Phase Space
TDS + E-Spectrometer
E0
DE
t0
Dt
Bunch Profile / Length
TDS
EOD
BCM
THz Spectrometer
Incoherent radiation
THz Streaking
21
Notes: Electron bunches and x-ray pulses can be represented in longitudinal phase space diagram shown here7
The distribution looks different for different positions in the FEL
The bunches or pulses are located in time t0 and energy E0
They have a temporal width Dt and an energy distribution DE
The longitudinal diagnostic components have to provide full information about longitudinal phase space.

## Slide 22
Thank you for your attention

## Slide 23: 2.7 Summary Longitudinal Diagnostics: Properties
 | Measurement | Pros | Cons
TDS | Longitudinal beam profile Longitudinal phase space slice emittance | Direct method | Single bunch resolution Destructive to measured bunch
EOD | Longitudinal beam profile | Multi bunch resolution | Limited resolution (> 150 fs)
THz Spectr. | Spectral dist. of THz radiation (Longitudinal beam profile) | Multi bunch resolution High resolution | Reconstruction depends on profile Only compressed bunches (< 1ps) Works best at high beam energies
BCM | Integrated THz radiation Compression | Multi bunch resolution Simple RF phase monitor | Only compressed bunches (< 1ps) No reconstruction of profile possible
BAM | Arrival time Beam energy | Multi bunch resolution High resolution | Requires laser-based synchronization Small dynamic range
EBPM | Beam energy | Multi bunch resolution Large dynamic range | Large dynamic range Requires absolute energy calibration
SRM | Beam energy profile | Energy profile | Limited resolution Requires absolute energy calibration
View Screen (WP17) | Beam energy profile | Absolute reference | Destructive Method Single Bunch Operation
All devices to be designed as monitors with single bunch resolution
Most diagnostics is to be installed in XTL and not accessible during operation
Suite of diagnostics to cover all requirements
Notes: Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of the EoI for WPnumber 2) The row in the footer area: write the institute name
Close Master View

## Slide 24: 1. Introduction: Overview on WP-18 Devices
femtosecond optical
timing distribution
3.1 LbSync
Laser-based Synchronization
3.2 REFM
RF
Synchronization
L2L
Laser
Synchronization
2.6 BAM
Bunch Arrival
Monitor
SRM
Synchrotron
Radiation
Monitors
2.5 EBPM
Energy BPM
Bunch arrival
Beam energy
Beam Energy
Energy profile
Beam energy
(Bunch arrival)
Beam energy
Bunch arrival
2.2 EOD
EO
Diagnostics
2.3 BCM
Bunch
Compression
Monitor
2.1 TDS(1)
Transverse
Deflecting
Structure
Bunch profile
Compression
Bunch profile
Slice emittance
Phase space
Bunch length/profile
1)
High-Power RF system and TDS are part of contract between European XFEL GmbH and Inst. for Nuclear Research (INR).
Most diagnostics is to be installed in accelerator tunnel XTL and not accessible during beam operation (reliability, remote diagnosis, maintainability, …)
To reduce R&D costs, ease maintenance and number of spare parts => re-use hardware where possible
BAM, BCM and EBPM to be used for fast intra bunch-train Beam-Based Feedback (BBFB)
2.4 CRD
THz
Spectrometer
Bunch profile
Notes: Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of the EoI for WPnumber 2) The row in the footer area: write the institute name
Close Master View

## Slide 25: 2.7 Summary Longitudinal Diagnostics: Locations
EBPM
SRM
SRM
EBPM
THz
BAM
BAM
BAM
BAM
EOD
BCM
BCM
BCM
BCM
TDS
TDS
TDS
EBPM
EOD
EOD
Notes: Before you start editing the slides of your talk change to the Master Slide view: Menu button “View”, Master, Slide Master:
Edit the following 2 items in the 1st slide: 1) 1st row in the violet header: Delete the existent text and write the title of the EoI for WPnumber 2) The row in the footer area: write the institute name
Close Master View

## Slide 26
Controller
MO
WP-02 LLRF
Beam direction
e-spectrometer:
Energy
Long. PS
Diagnostic Sections:
Bunch Compression (BCM)
Bunch-Arrival Time (BAM)
Long. Bunch Profile (EOD)
BC chicane:
Energy (EBPM)
Energy spread (SRM)
Matching into chicane
BC1
BC0
L1
L2
REFM
Matching Section:
FODO Lattice
Slice Emittance (TDS)
Long. Bunch Profile (TDS)
Pump-Probe Laser n
Experimental Hall:
Pump-Probe Laser 1
SLO
~ 3.5km
MLO
Links
x 24
* MLO/SLO: master/slave laser oscillator
BAM
BAM
Beam Based FB
BCM
BCM
EBPM
2.9 General Layout of Diagnostics Section

## Slide 27: Beam Distribution
SQS
SCS
SPB
FXE
MID
HED

## Slide 28: Beam Distribution
SQS
SCS
SPB
FXE
MID
HED

## Slide 29: Beam Distribution
SQS
SCS
SPB
FXE
MID
HED

## Slide 30: Beam Distribution
SQS
SCS
SPB
FXE
MID
HED
Dedicated kicker not baseline
Might use beam distribution system

## Slide 31: TDS: Longitudinal bunch profile / slice emittance
Long bunch trains can be exploited for on-line bunch profile & slice emittance measurements:
‘Steal’ 1- 4 bunches with a fast kicker out of the bunch train and deflect them onto view screens
Challenge: Small beam sizes in FODO section => screen resolution of 10 μm sufficient
Screen 3
TDS Voltage => Powerful commercial klystron
TDS Frequency => As high as possible
Wakefields => Iris > 40 mm => TDS Frequency < 4GHz
Streak 1 - 4 bunches within bunch train => short filling time
=> S-Band at 2.997 GHz (fTDS = 332 * fMO)
=> Travelling-wave structure
Location | Length | Resolution | Fill Time | No. of cells | Klystron
Injector | < 0.7 m | < 200 fs | 140 ns | 16 | 3 MW
BC1 | < 1.7 m | < 20 fs | 360 ns | 46 | 24 MW
BC2 | < 3.6 m | < 14 fs | 720 ns | 2 x 46 | 24 MW
Screen 2
Screen 1
Screen 4
Kicker
TDS
Exit BC
Kicker
Kicker
Kicker