## Slide 1: Longitudinal Phase Space Monitor for E-XFEL
Minjie Yan
Deutsches Elektronen-Synchrotron (DESY)
2nd Mini-Workshop on Longitudinal Diagnostics for FELs
12. Nov. 2013

## Slide 2
Idea: TDS + Kicker + Septum
Simulation with tracking codes: 3D and 1D
Flexibility for different operation modes

## Slide 3
Longitudinal Phase Space Measurement
Transverse Deflecting Structure (TDS)
  Longitudinal profile y ̴ z

## Slide 4
TDS + Dipole
  Longitudinal Phase Space: y ̴ z x ̴ energy
Longitudinal Phase Space Measurement
Transverse Deflecting Structure (TDS)
  Longitudinal profile y ̴ z

## Slide 5
Longitudinal phase space diagnostic (SDUMP) has been routinely used for machine-setup and during SASE tuning.
However
  Dipole magnet has to be switched on/off (and cycled)  The operation has to be stopped
  It can only be operated in single-bunch mode.
  The machine behaves differently in the single- and multi-bunch mode. (FLASH is operated with 10Hz macro repetition rate, each RF macro pulse can be filled with up to 800 bunches )
  No information on actual SASE level during measurements in 6SDUMP.
Experience from FLASH
S. Wesch

## Slide 6
Experience from FLASH
Online bunch profile monitor at SMATCH finally working.
  Delivers single-shot current profile, rms bunch length at 10Hz during SASE operation.
  No information on the bunch energy.

## Slide 7
Idea for E-XFEL
TDS + fast kicker magnet + Septum
  Online longitudinal phase space diagnostic
  Pulse-stealing mode (lost one bunch in the bunch train)

## Slide 8
BC0
BC1
BC2
with septum
Idea for E-XFEL
I. Zagorodnov
Location of TDS diagnostics at E-XFEL

## Slide 9
Simulation for the scenario TDS + Kicker + Septum
One bunch for diagnostic
  Longitudinal resolution ̴ (sin(µx, TDS->septum ) * * VTDS) -1
  Energy resolution ̴ /Dy,screen
  Reasonable kick strength of the kicker magnet
  Reach 20mm offset at the entrance of the septum
  Small streaked beam size at the septum
  No influence of the dispersion from the kicker magnet
  Simultaneous matching for the FODO section
Remaining bunches for SASE
  Simultaneous matching into LINAC
Requirements on the accelerator optics

## Slide 10
Slice Emittance Monitor
Matching into linac
LPS Monitor
Simulation for the scenario TDS + Kicker + Septum
Example for E-XFEL: after BC1
Expectations
  Assumming εN=1µm and TDS operated at maximum power (24MW ~ 15MV) Time resolution: 16fs Energy resolution: 6.3·10-5 Dx,screen from kicker: 1.8mm

## Slide 11
Simulation for the scenario TDS + Kicker + Septum
Parameters
  Input distribution: S2E simulation with CSRtrack + ASTRA
  Tracked beamline: entrance TDS to the screen
  1nC, 200k particles, 700MeV
Comparisons
  ‘TDS + dipole’ vs. ‘TDS + kicker magnet + septum’ with the same optics
Simulation with elegant

## Slide 12
Monitoring the Longitudinal Phase Space
100pC, 1M particles
S2E Simulation with 1D-code RFTweak from M.Dohlus
BC0
BC1
BC2

## Slide 13
100pC, 1M particles
S2E Simulation with 1D-code RFTweak from M.Dohlus
BC0
BC1
BC2
 | ACC1 phase (degree)
(a) | working point
(b) | +0.35
(c) | -0.35
Monitoring the Longitudinal Phase Space

## Slide 14
100pC, 1M particles
S2E Simulation with 1D-code RFTweak from M.Dohlus
BC0
BC1
BC2
 | ACC1 phase (degree)
(a) | working point
(b) | +0.35
(c) | -0.35
Monitoring the Longitudinal Phase Space

## Slide 15
100pC, 1M particles
S2E Simulation with 1D-code RFTweak from M.Dohlus
BC0
BC1
BC2
 | ACC1 phase (degree)
(a) | working point
(b) | +0.35
(c) | -0.35
Monitoring the Longitudinal Phase Space

## Slide 16
  Information on the energy spread without disturbing SASE delivery
  Monitor the linear energy chirp, which is very crucial to the final compression
  Could measure the longitudinal phase space after BC1 and BC2 at the same time  compression studies
Conclusion

## Slide 17
Thanks.

## Slide 18
Flexibility
SASE-mode & Setup-mode
  SASE-mode: use the kicker to kick one bunch out of bunch train into the dispersive section.
  Setup-mode: use the steerer to direct the all bunches into the dispersive section.
Quad
Kicker
Steerer
Septum
e-beam

## Slide 19
Flexibility
Septum-on & Septum-off
  Septum-off the bunches should pass through in the middle of the D=40mm beam pipe
  Septum-on straight-bunch and kicked-bunch are directed into two beam pipes and separated by 20mm  movable bellows
e-beam
Kicker
Septum