## Slide 1: Procurement Readiness Review WP02 - LLRF
Software

## Slide 2: Development of digital LLRF@DESY
DSP based LLRF
  Basic controller functionality
    Feedback and feed forward drive
    VS feedback concept
VME based LLRF
  Integration complex controller structure
  Beam based feedback system
  Restructuring server + firmware layout
Switching to MTCA.4
  Layout change (ADC + main controller)
  September 2011  test setup ACC1
  Permanent FLASH operation since Aug.
  Implementation of all commissioned software components from SIMCON
Known procedures, new features

## Slide 3: Software Layers
Finite state machine
  Sequencing operation procedures
    gentle startup, change of operating points
Preprocessing and automation server
  Quench detection, Cavity parameter computation
  Evaluation of controller performance
Front End server / LLRF controller server
  Data acquisition / manipulate controller parameters
  Pulse to pulse control loops
Firmware ( FPGA implementation )
  Preprocessing AMCs, master and slave controller
  Fast digital data processing with 9 MHz
    Direct connections to subsystems using optical links

## Slide 4: Schematic Firmware Layout
RTM Level
AMC Level
FE Server
RF Station
Master
Slave
Control of external modules by AMC boards ( Drift compensation, Piezo control )

## Slide 5: Low Level Software Integration
Driver support package
  Generic hardware interface
Modular design
  Master and slave configuration
  Gun control interface
Remote maintenance
  Programmable firmware
  Frequent server updates
DOOCS compatibility
  jDDD as GUI
Clear interface definition
  Separate firmware and server development possible

## Slide 6: Front End Architecture
MTCA crate of SC RF station
  Inter- board communication
  Main controller architecture
  Separate master/slave configuration
Front end server level
  Firmware communication
  Timing Information Interface
  Control remote Firmware upgrade
Application functions
  Internal communication protocol 0MQ
  Preprocessing steps, DAQ
  Performance evaluation
User interface
  LLRF station as client
  Graphical display jddd
  Middle layer interface

## Slide 7: Server Property Naming convention
Already being introduced with LLRF@FLASH upgrade
  prepared / scalable to XFEL
Following DOOCS specific separation
  Facility / Device / Location / Property
  Location separation between master and slave
    Specific to generic
  Consistent for all facilities
  Waveform is generated inside:
    Server: FF_AMPL.TD
    RBV from Firmware: FF_AMPL.HW
XFEL.RF
AMTF.RF
FLASH.RF
LLRF.CONTROLLER
QUENCHDETECT
LLRF.INFO
C1.M4.A9.L3
PVS.M12.A9.L3
CTRL.GUN.I1
PROBE.CAL_ROT
AMPL.SAMPLE
FB.ENA

## Slide 8: Safety and Protection of Connected Systems
Limiters, Pre-limiters triggering at defined thresholds
  Separately applied for all cavities
Quench detection and protection
  Measure changes in Ql and eventually stop RF
  jitter -> soft quench, drop -> hard quench
Connection to fast interlock system (MPS)
  RF inhibit RX/TX for LLRF system
  Piezo operation cryogenic interlocks
Gun lifetime management
  Monitoring of forward and reflected signals
    Fast RF stop intra-pulse
    Gun recovering in consecutive pulse
  Outlook  merge temp control
Quench detection
QUENCH
Gradient ramp-up
Cavity coupler protection

## Slide 9: Limiter Functionality
Limiters applied on all critical stages inside controller chain
  Cavity Amplitude detection with two thresholds
    Set point reduction
    Fast main controller output switch
  Controller input and output + set point modulation from BBF
  All controller tables loaded from server
C1
C32
Ampl. detection
…
Limit
Pre-Limit
Vector
Sum
Beam based
Feedback
Set point
Tables
Setpoint
Correction
Tables
Reduction
Ctrl
Controller Input
Limiter
Feed Forward
Tables
Learning Feed Forward
Controller Output
Limiter
RF pulse cut
DAC
Beam Loading
Compensation
Inside
Firmware

## Slide 10: Automation Routines
Piezo actuators for resonance frequency control
  LFD compensation
  Adaptation to changing operating conditions
  Outlook  coarse tuning using stepper motors
Loop gain and phase correction
Adjustment of desired Ql settings
Cryomodule warm up / cool down
Klystron linearization
….
Klystron Linearization

## Slide 11: Automation prerequisites -> characterize
  cavity piezos (sensor/actuator)
  cavity frequency tuner
  cavity coupling motor
  cavity quench profile
  cavity fundamental modes
  cryomodule performance for nominal operation
Motor position
Measured loaded Q
negative
end switch
positive
end switch
Frequency Tuner Scan
Coupler Motor Scan
Sub- Modes Scan
suppression
Complex routines  special test server development

## Slide 12: Interfaces to other Subsystems
Timing system interface (except triggering events)
  A-priori distribution of pulse pattern
    Multi beamline support
  A-priori distribution of expected bunch pattern
    Effective beam loading compensation
Receiving of beam based information's
  BAM, BCM, BPM (Energy)
  Charge detection with toroid system
    Necessary for BBF and BLC

## Slide 13: Summary
LLRF main software and control structure designed
  Further improvements can be easily integrated
  Hardware capability for future extension
Software had been evaluated trough last LLRF systems
  Further developed and improved
  New automation and protection routines
Currently implemented at FLASH/AMTF/REGAE
  Also mirror platforms for bug finding and fixes
    Most new functionalities can be fully tested here
  Characterization of modules / LLRF automation tools
Some interfaces to be optimized
  Transmission of beam based data (BAM, BCM, Toroid)
  Global energy management and control

## Slide 14: Outlook
Correction of cross coupling effects
  Corrected Forward and Reflected signals
    Virtual probe calculation
    In suite cavity model
    Observer based control methods
  Real time detuning and QL measurement
    Fast quench detection
Single bunch transient measurements
  Optimization VS calibration
    Online calibration check
Restructuring server architecture
  Plain C++ / Real time capable
  Multi control system capable
Hardware is designed to support this upgrades
Firmware designed modular