## Slide 1: WP 33 –Tunnel Installation Magnet Suspensions
Norbert Meyners, MEA1/WP33
for
Roland Platzer, Peter Talkovski, ZM1

## Slide 2: Content
Where?
Why?
Solutions
Status

## Slide 3: Where?
XTL, R 37-41
XTL, R 28-36
XTD2, R 13-16

## Slide 4: Why? In XTL R37 – 41 (and XTD2 R13 -16)
Transport way crossing below the beam lines
In XTL
(and in
XTD2)
XTL R 37-41

## Slide 5: Why? In XTL R28 -36
Our standard solution (adjustment units on concrete columns) did not meet the vibration requirements!
Remark: Beam height 2.2m plus floor slabs  lowest: 25Hz (Calculated; Required: > 50Hz)
Part of T4/R9

## Slide 6: Solution
Frames suspended from ceiling
Dump beam line (TLD) above with separate frames
BV magnets (TLD) hanging for maintenance and installation reason
e+
e+

## Slide 7: Old Position of U-Beam ./. Survey Marks
Found using laser scan data
 Move U-beam up

## Slide 8: XTL R39 | front view
Horizontal and vertical Eigen frequencies >=~50Hz (calc.)
T1 --- x
x --- T2
x --- TLD

## Slide 9: XTL R39 | mole view
TLD
T1
T2

## Slide 10: XTL R39 | frame only

## Slide 11: XTL R39 | frame only

## Slide 12: XTL R39 | TLD Quadrupole w/ BPM and Steerer
Eigen frequencies: 10 Hz (long.), XBD (hor.): 25 Hz, XQF (hor.): 35 Hz

## Slide 13: XTL R40 | Suspension BV-Magnets (TLD)
Installation by lifting from below possible
Eigen frequencies
  1. Ef 12.5Hz
  2. Ef: 16Hz
  Waiting for approval by MLC

## Slide 14: XTD2 R 13 – 16 | Proposal
XTD2 R 13 overview
XTD2_Tragrahmen_OTR
XTD2_Tragrahmen_QE
Frames bolded to in-casted rails!

## Slide 15: XTD2 R 13 – 16 | Eigen frequencies
Stiffer design nearly impossible (Load of screws at limit)
 Approval by MLC needed
Frame 13a: 1.Ef (hor.): 47Hz
Frame 13c: 1.Ef (hor.): 52Hz
Frame 16b: 1.Ef (hor.) 43Hz

## Slide 16: Adjustment Units
Different versions
Design: ready
Fabrication drawings: in production
BPM fixed to
adjustable
vacuum pump

## Slide 17: Adjustment Units | Vibration Requirements
To achieve the vibration requirements both plates will be fixed fix glue after adjustment
Glue

## Slide 18: Status
XTL R 37 – 41
  Top steel plates ready for welding (in-house)
  Positions marked
  Lights needs to be move
  Call for tender (nearly) out
  Fabrication drawing under production
XTD2 R 13 – 16
  Design ready
  Vibrations need approval
XTL R28 – R36
  Design started

## Slide 19: End
Thank you
for your
attention!

## Slide 20: XTD2 | Feet Position
Lage der Anschraubbleche an der Tunneldecke

## Slide 21: XQH w/ BPM, Pump & Steerer

## Slide 22: XTIN | Pylon 705 hoch 950 tief

## Slide 23: XTIN | Pylon 630 hoch 950 tief

## Slide 24: XTIN | Pylon 705 hoch 500 tief

## Slide 25: BB und QM-Stein

## Slide 26: XTL | BC-Pylon

## Slide 27: XTL | Tunnelstein 750x1000 tief

## Slide 28: XTL | Tunnelstein 600x600 tief