## Slide 1: Update Photon beam systems
European XFEL Collaboration Meeting
Hamburg, April 7-9, 2014
Thomas Tschentscher
thomas.tschentscher@xfel.eu
Notes: How to edit the title slide
Upper area: Title of your talk, max. 2 rows of the defined size (55 pt)
Lower area (subtitle): Conference/meeting/workshop, location, date, your name and affiliation, max. 4 rows of the defined size (32 pt)
Change the partner logos or add others in the last row.

## Slide 2: Overview

## Slide 3: Overview

## Slide 4: Overview
Undulators /
Theory
Optics /
Beam transport /
Diagnostics
Instruments /
Detectors /
DAQ+controls /
Lasers /
Sample env. /
Exp. Hall Infra.

## Slide 5: Content
  Some general remarks
  Update photon beam system work packages
  Time planning

## Slide 6: Photon energy ranges
200 eV
1 keV
10 keV
284 eV - C K
410 eV - N K
543 eV - O K
12.4 keV
Electron
energy sets
Soft x-ray undulator
SASE 3 (68 mm)
20 keV
7112 eV - Fe K
25 keV
water window
Diffraction
(DAC, etc.)
4992 eV - Ti K
4038 eV - Ca K
2470 eV - S K
2145 eV - P K
500-1300 eV
2p TM, 3d RE
500 -1300
6 -14 keV
18 - >25 keV
12.0 GeV
8.5 GeV
17.5 GeV
14.0 GeV
0.25 – ≥3 keV
Hard x-ray undulators
SASE 1 & 2 (40 mm)
3.0 – ~25 keV

## Slide 7: Update photon beam system work packages
  WP-71 – Undulator systems
  WP-72 – FEL simulations
  WP-73 – X-ray optics & beam transport
  WP-74 – X-ray diagnostics
  WP-75 – Detectors
  WP-76 – DAQ & controls
  WP-78 – Optical lasers
  WP-79 – Sample environment
  WP-81-to-86 – Scientific instruments
  Experiments hall installations & infrastructure
  (non-exhaustive !)

## Slide 8: WP-71 Undulator systems
Design, construction, assembly, measurement , installation of SASE undulators, phase shifters & intersection units
Undulator assembly & measurement (Bldg 36)
Phase shifter measurement (IHEP)

## Slide 9: WP-72 FEL & SR simulations / theory
Seeding techniques & applications
  HXRSS (coll. with Kocharyan, Saldin, Serkez, Zagorodnov (DESY), Barty and Yefanov (CFEL))
  SXRSS (coll. with Kocharyan, Saldin, Serkez (DESY))
  Maximize FEL brilliance
  Prepare HXRSS/SXRSS implementation
FEL operation techniques
  Tapering (coll. with Kocharyan, Saldin, Serkez, Zagorodnov (DESY))
  Maximize FEL pulse energy/peak power
Software development
  Development and integration of various codes (coll. with Dohlus, Zagorodnov (DESY), Tomin (Kurchatov Inst.))

## Slide 10: WP-73 X-ray optics & beam transport Offset and distribution mirrors
9 flat mirrors (3 adaptive)
  Key specs: 2 nm PV
  Prototype tested
  Delivery end 2014-2016
Mirror chambers need to be extremely stable and low-vibration
  Key specs: 20 nrad rms
  First two chambers arrived

## Slide 11: WP-73 X-ray optics & beam transport Slits and Shutters
Delivery June 2014
Delivery May 2014

## Slide 12: WP-73 X-ray optics & beam transport SASE3 Gas Attenuator
15m long, N2 (and Xe), gas pressure range 10-4 - 25mbar, aperture size 25mm, attenuation up to 10-4
Prototype (first half) now under testing

## Slide 13: WP-73 X-ray optics & beam transport Grating Monochromator for SASE3 beamline
Delivery March 2015 (FMB Berlin)

## Slide 14: WP-74 X-ray photon diagnostics
X-ray photon diagnostics units
  XGM  measurement of x-ray pulse intensity & position
    XGMs from K. Tiedtke (DESY)
    Girder design by xfel.eu
  Tests of new methods
    Circular polarization meas. (coll. with DESY & other)
    Spectrum measurement (coll. with PSI & SLAC)
Beam transport monitors
  Technical designs complete
  Fabrication contracted

## Slide 15: WP-75 Detectors
LPD
  First beam tests with 2-tile
  0.25 MPx system in test
AGIPD
  Full scale ASIC delivered
  First tests with beam
DSSC
  Redesign for phase-I
Other developments
  Gotthard (1D) – MHz
  MCP (2D, sX) – MHz
  Fast-CCD not yet arrived
  pn-CCD to be tested
1.0 ASIC
P-III tests
v1
MCP
Fast-CCD

## Slide 16: WP-76 DAQ & controls Karabo 1.0 control and DAQ usage examples
Initial time scans macro for PID characterization
WP83: measurement of PID parameterization of a furnace using Lakeshore heater and Agilent DVMs
Feedback very useful
WP75 2D detector integration
Started with LPD 2-Tile system
  K0.1 control of LpdFem and DAQ to standalone Python receiver & image viewer
  July: K1.0 control and DAQ to LpdFemSink with embedded pixel reorganization and output to HDF5
AGIPD and DSSC test stand setup in progress and ¼ Mpx test stand coming soon!
Karabo is a major effort, it is converging and exposure to use cases is essential
Digitizer DAQ and control at beamlines
WP81-FXE: measurement of fluorescence yield of X-ray hitting liquid jet target (8MHz), with and without laser pump (4MHz), using an APD at PETRA-3
WP74-PES: measurement of multi-channel eTOF signal digitization at PETRA-3 and FERMI (10Hz)

## Slide 17: WP-76 DAQ & controls Electronics development
What WP76 gets from the joint WP75/76 electronics group in brief
FPGA framework and implementations – reduce data volume, provide VETO triggers, enable scientists…
Interface Timing and synchronization – interface machine-instruments, electrical triggers, data tagging...
Standard solutions – MTCA and ATCA crates, digitizers, CPUs, interfaces PCIe, GbE, 10GbE and VETO
Detector interfacing electronics – digital and analog, filtering and shaping, level conversion…
Detector and DAQ electronics coordination with WP75 – documentation, external projects…
Name | Description | Status – since last DAC
Train builder | Build complete trains of pulse ordered data from large-2D detectors, multiplex 10GE in to out links | f/w development and K1.0 integration on-going
Clock and Control | MTCA.4 timing and synchronization board for large-2D detectors | Production boards distributed to 2D test stands.
VETO | Evaluates fast information and distributes reuse storage cell command to 2D FEE f/w | Setting up test system on DAMC2 digital board
SP-Devices digitizer family | General purpose MTCA.4 digitizer (1.6 – 8 GS/s; 14 – 8 bits; 10GE + VETO; user defined algorithms in FPGA) | Passed performance testing, small improvements requested
External Timing Adapter | X2 timing board interface adapter distributing 10Hz trigger, clocks and serial metadata | 30 boxed versions produced
Fast ADC | General purpose Fast ADC system on MTCA.4 for 0D sensors used for Diagnostics, VETO, etc. | 10 channel delay line shaper RTM sent to manufacture
FPGA framework | High-Level FPGA Programming Framework on Simulink | On-going, see P. Gessler talk
Laser FEE systems | Laser timing drift compensation | Test failed due to motor control, modifying for new test
WP76 projects

## Slide 18: WP-76 DAQ & controls Experiment and beam line Control status
Changes made since the last DAC
Clarification of standards
  Beckhoff PLC terminal rail system used to control motor, vacuum.
    acceptance test with WP73 as DeltaTau replacement +ve.
  Use of a single f/w framework with
    defined safety interlock, pending, etc. design
    use and interchangeability of f/w blocks from different authors
    single service implementations (communication, messaging, startup initialization, self description)
  Connectors and cable standards being defined with WP73, CIE…
  Use of E-plan for cable wiring (not KDS) with CIE
Confirmation of roles
  f/w is written and integrated with control system by WP76
  WP73 organizes building beam line tunnel crates
  WP76 builds test stand crates
  WP76 and CIE organizes experiment crate systems
More manpower and update of roles
  J.Reifschlaeger technician, cable and connector standards, crates, +
  G.Giambartolemei user-f/w-s/w glue, documentation, worrier
Overhaul of s/w
s/w – f/w connectivity
Motor
Pump
Gauge
BeckhoffCom
karabo s/w devices
TCP/IP
Motor
Pump
Gauge
EtherCAT
PLC f/w
TCP server
Device drivers
Serial
Digital
Analog
Changes in-progress
These changes are being made to ensure that “working” systems are delivered.

## Slide 19: WP-78 Optical lasers Pump-probe laser concept and status of prototype development
Burst-mode multi-stage NOPA with 3 operating points
Burst-mode output 800nm: 15 - 80fs, 4.5MHz ↔ 0.2mJ, 1MHz ↔ 1mJ, 200kHz ↔ >3mJ
Burst-mode output 1030nm: sub-ns and/or sub-ps, 1030nm, up to 100mJ
Current status:
400W pumped 2-stage NOPA fully characterized: 15 … 75fs, up to 180µJ, 0 … 4.5MHz
20kW boosters installed
1030nm
Soliton
seeder
Dt =
0-5ns
burst-mode
all-fiber CPA
front-end
super-
continuum
var.
prechirp
AOM
PC
SHG
NOPA 1
NOPA 2
NOPA 3a
Compressor
SHG
SHG
SHG
NOPA 3b
sync via fiber
and OBC
x-ray - optical
laser overlap
800nm, 0.2 … 3mJ,
4.5 ... 0MHz,
15 … 100 fs
Yb-booster 1
(burst-mode)
7 kW
Yb-pre-amp
(burst-mode)
400 W
Yb-booster 2
(burst-mode)
20 kW
1MHz
200kHz
4W @
4.5, 1 or 0.2MHz
20W @
4.5MHz
Compressor
188kHz
4.5MHz
4.5MHz
sub-ps
1030nm, 4 … 100mJ, 4.5 … 0MHz
sub-ns
1
2
3
Notes: Main messages:
- Sub-ps pumped multistage NOPA with 3 working points
- Also 1030nm output with sub-ps and sub-ns
Status LAC 3:
400W pumped NOPA performing as expected and fully characterized
20kW booster installed

## Slide 20: Pulse properties in short pulse mode
Compressed pulse 14.9 fs
Spectrum corresponds to
13.8 fs Fourier limited pulse
High contrast 14.9 fs compressed pulse (SPIDER)
Pulse energy 180 uJ @ 188 kHz rep. rate
Contrast: ca. 20dB
Notes: Main message:
Clean 15fs pulses, nearly transform limited, 180µJ

## Slide 21: Long pulse mode
Flexible pulse duration selection
Good compressibility, close to Fourier limit for sech^2 pulses
assuming sech2-deconvolved Autocorrelation
Compressed pulses: 25 … 75fs
25fs
50fs
75fs
Notes: Main message:
Longer pulses are possible, as demanded, close to transform limited.

## Slide 22: NOPA beam quality
Near field
Far field
2mm
180 um
Ellipticity 0.9
Very close to diffraction limited Gaussian beam
M2<1.15
Notes: Main message:
Diffrection limited beam from NOPA

## Slide 23: Burst and arbitrary pulse selection
Burst: 10Hz, 600µs.
Burst: 10Hz, 188kHz intra-burst , 180µJ per pulse.
Amplified burst: 10Hz, 2.5% dc
Arbitrarily selected pulses
Free of transients
Notes: Main message:
Burst performance:
- Clean burst, no transients, arbitrary pulse selection

## Slide 24: WP-79 Sample environment
Development activities
  Versatile liquid jet setup
    5 – 100 µm glass nozzles
    <1µm gas dynamic jets
    microfluidic systems for reproducibility & lab-on-the-chip approach
    Sample recovery catcher
    First tests showed that protein nano-crystals can be recovered
  Fast sample scanner
    Fast scanning (10 Hz, ~1mm)
    µm accuracy
    Add.: heat, cold, contacts
    Exchange of sample holder
    Vacuum load-lock system

## Slide 25: WP-79 sample preparation laboratories in XHQ
Room for sample preparation
2x23m² chemistry wet labs
30m² X-ray lab for crystallography, SAXS, and reflectometry
30m² vacuum labs
44m² dry sample preparation
2x22m² electron microscopy and nano-fabrication lab

## Slide 26: WP-81 FXE instrument
Special, as large contribution through IKC from Denmark
  Design, manufacture, installation, techn. commissioning
Collaboration with DTU, JJ X-ray

## Slide 27: WP-82 HED instrument
DIPOLE laser

## Slide 28: WP-83 MID instrument
Sample
chamber
Detector
arm

## Slide 29: WP-84 SPB instrument – Layout
Integration of SFX User Consortium into SPB instrument
4-mirror integration
Detector arm &
SFX integration

## Slide 30: WP-85 SQS instrument – Layout
SQS Optical Laser
Control
PP Laser
SQS
Exp.
NQS
AQS
REMI
Diagn.
Diagn.
KB
Versatile end-station
Exchange of 3 chambers
- AQS: Atomic-like Quantum Systems
- NQS: Nano-size Quantum Systems
- REMI: Reaction Microscope
SASE 3 beam
Pink beam (1 mm)
Monochromatic beam
Circular polarization
SQS Instrument Laser
Wavelength tuneable
2nd/3rd harmonic
THz

## Slide 31: WP-85 SQS instrument – Special developments
Focus in F1
100nrad slope error
50nrad slope error
Focus FWHM (mm)
Photon energy (keV)
KB focussing optics
Piezo benders (3 interaction regions)
Small surface errors (1 micron focus)
80 cm length
Extension to baseline equipment
XUV 1D Imaging spectrometer
Non-linear Phenomena
J. Nordgren, J-E. Rubensson, Uppsala University, Sweden
Reaction Microscope (REMI)
Angle-resolved electron-ion multi-coincidence
R. Dörner, R. Moshammer, Uni. Frankfurt, MPI Heidelberg

## Slide 32: WP-86 SCS instrument - Layout

## Slide 33: Experiment hall installations & infrastructure
PSPO(T. Haas, G. Wellenreuther), TS(B. Becker-de-Moos), ext. companies

## Slide 34: Experiment hall installations & infrastructure
PSPO(T. Haas, G. Wellenreuther), TS(B. Becker-de Mos), ext. companies
Control areas
SPB/SFX Präparationslabor

## Slide 35: XHQ laboratory floor definition & infrastructure
TS(B. Becker-de Mos), ext. companies
Side view
Top view

## Slide 36: Content
  Some general remarks
  Update photon beam system work packages
  Time planning

## Slide 37: Critical elements in time planning
Highly specific components
  X-ray optics, in particular long, extremely flat mirrors
    First mirrors will be available for installation
    Mitigate risk by using other optics
  2D detectors
    First detectors will be available
    Mitigate risk by using ‚standard‘ detectors
  Complex mechanics
    So far no show stoppers identified
Installation sequence
  Need to build up infrastructure first (rooms, media/TGA, conditioning)
    In principle okay, but complexity can lead to delays
Resources
  Manpower to advance design, prepare procurement, follow-up, installation

## Slide 38: Stagged installation
SASE 1 – FXE & SPB instruments (t0)
  First hutch installations
  First undulator & x-ray beam transport
SASE 3 – SQS & SCS instruments (t0 + 1 month)
  Next set of hutches
  Next undulator & x-ray beam transport
SASE 2 – MID & HED instruments (t0 + 4 month)
  Final set of hutches
  Final undulator & x-ray beam transport
Additional instrumentation
  Detectors, DAQ & control, optical lasers, sample environment occurs in parallel and according to needs by the above listed areas