## Slide 1: First Thoughts on Undulator Commissioning
Y. Li , WP71
Materials of undulator characters for commssioning
Aiming at FIRST lasing.

## Slide 2
The XFEL Undulator Systems

## Slide 3
e -
e -
SASE2
SASE2 SASE1/3
Downstream View
Tunnel Installation of SASE2 Undulator System – Final WP71 Deliverables
e -
Intersection 1.1 m
Undulator Segment 5m
Undulator Cell 6.1m
W.Tscheu
Local Control Systems
 | SASE1/2 | SASE3
0 [mm] | 40 | 68
Operational Gap Range [mm] | 10-20 | 10-25
K-Range | 3.9–1.65 | 9.0-4
Radiation Wavelength Range [nm] |  | 
@ 17.5 GeV | 0.147-0.040 | 1.22-0.27
@ 14.0 GeV | 0.230-0.063 | 1.90-0.42
@ 8.5 GeV | 0.625-0.171 | 5.17-1.15
# of Segments | 35 | 21
System Length [m] | 213.5 | 128.1

## Slide 4: SASE2 Type Intersection
WP71
Quadrupole Movers
WP71
Phase Shifters
Re-entrant Cavity BPMs+ Electronics
WP17
WP71
Support Bases Adjustors Concrete Pillars
WP71
Air Coil Correctors
Beam Loss Monitors
WP17
WP19
Vacuum System
Status 4/2014:
Delivered:
  Quadrupoles, WP12
  Air Coil Correctors, WP71
  Base Plates, WP71
  Adjustors, WP71
  Concrete Pillars , WP71
In Production 91 Intersections:
  Phase Shifters, WP71
  BPMS, WP17
  BLMs, WP17
  Vacuum systems, WP19
  Quadrupole Movers, Ciemat
WP12
Quadrupoles

## Slide 5
Plan for Day 1

## Slide 6: Undulator Plans for Day One
Day One: Focus is to achieve first Lasing
  Straight Trajectory ;
  Good Phase Matching.
Install only well characterized equipment (Undulators, Phase Shifters)  Limits & reduces error sources
Trust the equipment ! Trust the magnetic measurements!
Avoid, if possible sophisticated diagnostics, which require commissioning  later
Basic controls for undulator must be available
Sophisticated controls for undulators come later,

## Slide 7: Performance Criteria
Magnetic Performance
Undulators are in specs and well characterized magnetically:
  K(gap): Target accuracy: K/K10-4
  Phase jitters are sufficiently small for all working gaps.
  Correction Tables for Air Coil Correctors, 2-Wire Corrector are well known
Phase Shifters well characterized: PI(gapPhaseShifter)
  Phase Shifter Settings are known: GapPhaseShifter (Gap Undulator)

## Slide 8: Minimum Undulator Controls for Day One
Individual controls of all parameters, Status Information of any of the 35 (21) undulator segments of SASE1/2 (SASE3) via DOOCS (machine control):
  K/gap (±1μm) K/K10-4
  Phase Shifter gap
  Air Coil settings
  Quadrupole movers (±1μm)
  Temperature measurement & compensation (±0.1°C)
  Vacuum Chamber Temperature (3-Way Value) to 0.1°C
Sychronized motion (Undulator-Phase Shifter, Air Coils, 2-Wire Correctors) using lookup tables
Static control of undulator systems:
  Set Ks/gaps using lookup tables, Taper Profiles
  Update mode for lookup tables

## Slide 9
Magnetic Device Characterization

## Slide 10: Magnetic Measurements
Undulator Segments:
  Evaluate from field scans at 40 gaps (Final Table)
  RMS Orbits, Straightness
  Entrance/Exit kicks
  Phase Jitter
  K-Parameter / Gaps
  Phase Integrals
Phase Shifter
  Gap dependence of 1st Field Integrals
  Evaluate from field scans at 40 gaps (Final Table)
  Phase Integral (PI)

## Slide 11: Undulator Example: U40-X046-K006 Final Table

## Slide 12: X047 RMS Error / Phase Jitter
RMS Orbit Error  Reduced transverse Overlap  reduced FEL Power
Phase Jitter  Reduced longitudinal Overlap  reduced FEL Power
U40 Specs:
120Tmm2 ÷ 2μm
Specs: 8° ÷0.14rad

## Slide 13: X047 Kick Errors / Air Coil Correctors
Air Coil Correctors
Gap dependent Kick Errors ≤±0.15 Tmm
Effect of Air Coils on Trajectory
M. Yakopov

## Slide 14: Phase Shifter Characterization
1st Field Integrals:
Important for independent
operation, no corrections
required
Phase Integrals:
Adjust Phase delay

## Slide 15
Commissioning Strategy

## Slide 16: Strategy ( Elletra approach)
Assumptions:
Inside Undulator, properties are accurately known :
  Internal orbit is straight within specs (RMS criterion)
  Phase Jitter is in specs
  K-Parameters are consistent within K/K ≤1-2 ˣ10-4
Exact Phase Shifter settings are known from Magnetic measurements
No beam is required! Trust the magnetic measurements!
Undulator Entrance /Exit Kicks :
  Accuracy only  ±0.03Tmm ÷ 30% of ‘=1.6μrad
  XFEL specs: ±0.004 Tmm ÷ 5% of ‘
  Needs improvement using BBA  straight orbit

## Slide 17: Step 1: Global Orbit Correction
Correctors & BPMs
Before BBA
After BBA
6.1m
Precondition: Working BBA, well collimated beam, low losses
Establish straight large gap orbit (LGO) with Quadrupole Movers (eventually large corrections)
Establish straight orbit in operational gap range using Air Coils (small corrections <0.15 Tmm), update look-up tables

## Slide 18: Step 2: Set undulator segment gaps
Set Ks / gaps of undulator Segments statically trusting the magnetic measurements Suggestion: Use tuning gaps with lowest errors
  SASE1/2 gap 14mm, K=2.7
  SASE3 gap 15mm, K=6.9
Use the Phase Shifter settings from magnetic measurements
This should be good for First Lasing

## Slide 19: Outlook
Refine operation of undulator system, taper profiles,optimize laser power
Implement / make use of Hardware capabilities:
  Fully continuously synchronized gap/K changes.
  Change K while laser stays ON
Synchronize undulator with external sources (Monochromator) via EtherCAT bus

## Slide 20: Summary
For 1st lasing Undulator Systems sufficiently characterized
Basic control of Undulator systems will be available
BBA alignment is essential for a straight global orbit
K parameters and Phase Shifter setting will be taken from magnetic measurements
From the undulator side this should be sufficient for 1st lasing

## Slide 21
The End