## Slide 1
BeamCal Energy and Spatial Resolution for the ILC
Lucia Bortko, DESY – Zeuthen
Group Meeting | DESY - Zeuthen | 13 Dec 2013

## Slide 2: Beam Calorimeter for ILC
Tungsten absorber
Diamond sensor
Readout plane/air gap
1
Graphite absorber
FE
Selected ring
US
PS
30 layers
Size of pads:
US - similar, ≈7.65x7.65 mm
PS - ~R, min 2.2x2.2, max 14.4x14.4mm
Number of pads:
For US and PS similar

## Slide 3: Energy Deposition due to Beamstrahlung
US
Beamstrahlung (BS) pairs generated with Guinea Pig
Energy deposition in sensors from BS simulated with BeCaS (Geant4) → considered as background (BG)
Average
10 BX
PS
Average
10 BX
Maximum in
7th layer
Longitudinal background profile
Notes: Skazat pro to chto tak kak yadro livnya okolo 2?mm to umenshaya razmer yacheek na malyh radiusah my umenshaem shum ot bg, signal net, sledovatelno ozhidaem luchizhiy SNR
Put pictures for rms?? Or
- Put histo bg(radius) with rms as errors?? For all layers or for layer with maximum energy deposition?

## Slide 4: Shower from Single High Energy Electron
Shower from 200- GeV electron
Longitudinal shower profile
Example for 200 GeV electron:
Maximum in
11th layer
Electron energy | Shower maximum
10 GeV | 7 layer
20 GeV | 8 layer
50 GeV | 9 layer
100 GeV | 10 layer

## Slide 5: Reconstruction Algorithm
Longitudinal 200GeV- shower profile
Selection layers - from 5th to 20th
Selection pads – only first circle around the maximum
Cluster
Reconsrtuction algorithm output:
, ,

## Slide 6: Cluster Energy. PS. wo BG
Reconstructed only showers, without BG
Energy of electron 200 GeV
En_resolution ≈ 11%
En_resolution ≈ 4.5%

## Slide 7: Cluster Energy. PS. with BG
+
Reconstructed showers, considering BG
Energy of electron 200 GeV
En_resolution ≈ 13%
En_resolution ≈ 6%

## Slide 8: Residual Histo. PS. wo BG
Reconstructed only showers, without BG
Energy of electron 200 GeV

## Slide 9: Cluster Energy. US. wo BG
Reconstructed only showers, without BG
Energy of electron 200 GeV
En_resolution ≈ 5.7%
En_resolution ≈ 3.8%

## Slide 10: Cluster Energy. US. with BG
+
Reconstructed showers, considering BG
Energy of electron 200 GeV
En_resolution ≈ 5.4%
En_resolution ≈ 6 %

## Slide 11: Residual Histo. US. wo BG
Reconstructed only showers, without BG
Energy of electron 200 GeV

## Slide 12
Deposited Energy vs Energy of Electron
Energy deposition (GeV)
Number of events
y = 0,017x + 0,0051
Notes: SDELAT’ v log – shkale!!!!!!

## Slide 13
Energy Resolution vs Energy of Electron
Energy Resolution
Energy of Electron (GeV)
Notes: SDELAT’ v log – shkale!!!!!!

## Slide 14: Conclusion and proposals
The small software package was written, which
- goes through reconstruction algorithm and calculate COG coordinates and energy of cluster
- calculate true coordinate and center of corresponding pad coordinate
- calculate residual and plot its histogram. Plot cluster energy histogram.
This software made with options easily switching:
- reconstruct with/without background
- change number events
- choose segmentation
With this software were gotten cluster energy and residual histograms with different parameters: with/wo BG, whole/far-from-edges calorimeter area.
For US energy resolution depends on selected calorimeter area a little and for PS – a lot.
Energy resolution reconstructed (200GeV)showers Energy resolution of calorimeter for
(layer 5-20, 3x3 pads) wo BG, area far from edges: whole shower energy calculated:
PS: 4.5 %, US: 3.8 % 1.5 %
Proposals
Change reconstruction algorithm: only for small radii of PS or for all cases for both segmentations?
Look on the dependence energy resolution vs number discard layers
What else can influence on resolution??...
Discard layers number
Energy resolution
3x3 pads
whole shower

## Slide 15
Danke für Ihre Aufmerksamkeit!


## Slide 16
Backup slides

## Slide 17: Spatial Resolution ( In Process)
Estimation
PS
US
COG
= 2.9%
= 1.65 degrees
= 2.21 mm
= 2.16 mm
0
4
5
2
1
3
6
x
y
= 0.609 mm
= 3.97 mm
= 5.14 deg
= 0.848 deg

## Slide 18: Shower from Single High Energy Electron

## Slide 19: Spatial Resolution ( In Process)
Corrected COG
Energy of Electron
Gaussian fit
-
0
∆R
∆R
Parameters

## Slide 20
Layer 7
Layer 11
Shower maximum – Layer 9
PS
US
PS
US
PS
US
SNR for 50 GeV Electron
SNR in cell with maximum

## Slide 21
Layer 6
Layer 10
Shower maximum – Layer 8
PS
US
PS
US
PS
US
SNR for 20 GeV Electron

## Slide 22
Layer 5
Layer 9
SNR for 10 GeV Electron
PS
US
PS
US
PS
US
Shower maximum – Layer 7
Notes: +2 -2 layers – it is kind of testing of stability of our result
Dlya nizkih energiy mozhet byt chto snr v 9 sloe luchshe chem v 7 t.k. v 7om sloye bg vnosit bolshiy vklad.
Переделать все графики снр если останется время.

## Slide 23: Charge range estimate
For Diamond sensor pad thickness 300 µm:
- Charge collected from MIP: 2.44 fC
- Maximum charge collected – for shower from 500 GeV electron: 12214 fC
(correspond to about 5000 MIPs)
Diamond
GaAs
Distribution of the collected charge per pad for 500Gev electron showers
Notes: Ukazat kak rasschety provedeny? T.k energovydeleniye na yacheyku rastet (grubo) lineyno. I my znaem enorgovydeleniye dlya 100GeV – nogo electrona
Sdelat bolshe statistiki -> dodelat kod s ringo chtoby mozhno bylo mnogo input failov podavat’ v programmu bgaver_for_thisto_charge_collection…bla-bla-bla….

## Slide 24
Diamond
GaAs
Blue – Uniform Segmentation
Orange - Proportional
Green – Uniform Segmentation
Blue - Proportional
Distribution of the collected charge per pad for 500Gev electron showers

## Slide 25
Efficiency of Showers Reconstruction
Efficiency for 50 GeV
= 200 GeV
PS
US
Efficiency =
Notes: SDELAT’ v log – shkale!!!!!!

## Slide 26
Proportional
Segmentation
Uniform
Segmentation
The average energy in the pad of the core of shower
RMS of the averaged Background
Uniform
Segmentation
Signal and RMS for both Segmentations
20 bunch crossings were given
Signal nearly segmentation-independent!
Different distributions!
Proportional
Segmentation
Notes: SIGNAL ALMOST INDEPENDET OF SEGMENTATION!!
Peredelat grafik dlya rms chtob y os’ u PS byla takaya zhe kak u US