## Slide 1: Towards Attosecond RF Controls for Accelerators
Apply substantial new detector concepts for 1/f-noise reduction
Overcome ADC noise limitation by RF amplification before IQ-detection using a carrier suppression
knock
on table
Detectors for Attosecond LLRF controls
time
RF-virtual gnd
null Re & Im
Attosecond LLRF subcomponent requirements
Master reference:
 -10dB…-15dB above unity gain
 DRO, SCLOs + passive filtering
High power actuator chain:
 -10dB by removing spurious
 -10dB by IOTs, semiconductors
Field detectors:
 -15dB…-25dB
 Interferometer
 Superscaling
 Analog and digital hybrids
ARD-ST3 Picosecond and Femtosecond Electron and Photon Beams
Matthias Hoffmann, DESY
State of the Art LLRF controls
State of the art digital LLRF (low-level radio frequency) controls
Single detector performance : Phase resolution < 1.5mo (3fs) (Short-term, 1.3GHz)
Amplitude resolution < 2.6E-5 (Short-term, 1.3GHz)
Beam energy stability : 5E-5 (Shot-to-shot)
Arrival time jitter : <30fs (Intra-bunch)
MTCA.4 ACC1 installation
dE/E<0.005%(rms)
Single receiver performance
Simplified modular LLRF regulation scheme
PM: < 1.5m°, 3fs
AM: < 2.6E-5
Beam energy stability (out of loop)
General limitations of todays field detectors
Non-IQ field detector (noise balanced)
Limited spectral density of available best ADCs
- 10 channel field detection
- S-band (700MHz - 4.0GHz)
- Resolution, 0.003%, 0.003deg, < 10fs
- 10 channel ADCs (125Msps, 16-Bits)
- FPGA (V6) pre-processing partial cavity vectors
- Low latency links via MTCA-backplane
1.6fs [10Hz,1MHz]
4.3fs [10Hz,1MHz]
360° phase detection :
Saturated mixer :
-165dBc/Hz, <0.5fs resolution, 0.5V/rad
Interferometer :
-176dBc/Hz, < 50as resolution, 15V/rad
Carrier suppression
-> reduced 1/f-noise of the rf-amplifier
How to use analog small signal detectors in a digital LLRF system?
 Automated carrier suppression tracking (compensates small drifts, gradients)
 Combine interferometer and non-IQ detector (AM, PM 360o detection)
 Iteratively or using complementary filters
 Needs drift calibration, efficient for continuous wave (CW) operations
 Single cavities: Analog bypassed digital system (hybrids) using complementary filters
 Multi cavities: ~√3 (passive receivers) x √8 (VS-scaling) x √8 (8 receivers per cavity)
General Requirements
‘E. Rubiola et. al. “Advanced Interferometric Phase and Amplitude Noise Measurement,” Rev. Sci. Instrum., vol. 73 no.6 pp 2445-2457, 2002.
T. Berenc et. al. “An Interferometric Residual Phase Noise Measurement System at S-Band”, Low Level RF Workshop 2013, Lake Tahoe, California, USA.
Attosecond LLRF controls
Feedback model for cavity
phase jitter simulations
low-pass filtered
high-pass filtered
F.Ludwig et. al. ‘Phase Stability of the Next Generation RF Field Control for VUV- and X-ray Free Electron Laser’, EPAC 2006, Edinburgh, UK.
Courtesy of T. Berenc
Courtesy of T. Berenc
PM: < 0.032m°,31as
AM: < 0.6E-6
S-Band 2.815GHz, 100kHz BW
Courtesy of T. Berenc
Special acknowledgments to: Frank Ludwig, Uros Mavric, Holger Schlarb, Christian Schmidt, Sven Pfeiffer, Tim Berenc
dE/E < 0.005% (rms)
RTM
AMC
<200as (rms)
Field instability:
Subcomponent contributions
Q
I
Simplified block diagram
Linear Technology (2007)
LTC220x, 10nV/Hz
Analog Devices (2009)
AD9268-125, 9nV/Hz
Texas Instruments, (2012)
ADC12D800RF, 9nV/Hz
Texas Instruments, (2012)
ADS42LB69 , 14nV/Hz
1.3GHz