## Slide 1: Heavy Ion high intensity linac developments
Winfried Barth, GSI&HIM

## Slide 2: Heavy Ion high intensity linac developments
Motivation
28 GHz-ECR ion source (ST2)
H-type Cavity Developments (ST1, ST2)
cw-LINAC-Demonstrator (POF2)
Pushing the limits: cw-heavy ion beams at Coulomb barrier (ST1)
Outlook
Heavy ion high intensity linac developments, W. Barth, 4.2.14

## Slide 3
Heavy ion high intensity linac developments, W. Barth, 4.2.14
Motivation
Preperation for civil construction, 2012
(Upgraded) existing facility... provides
ion-beam source and injector for FAIR
Primary beams:
protons to 238U
Accelerator Components & Key Characteristics
Ring/Device Beam Energy Intensity
SIS 100 (100Tm) protons 30 GeV 4x1013
238U 1 GeV/u 5x1011
(intensity factor 100 over present)
SIS 300 (300Tm) 40Ar 45 GeV/u 2x109
238U 34 GeV/u 2x1010
CR/RESR/NESR ion and antiproton storage and
experiment rings
HESR antiprotons 14 GeV ~1011
Super-FRS rare isotope beams 1 GeV/u <109
Secondary beams: RIBs, pbars
New future facility: ... provides ion and anti-matter
beams of highest intensities and up to high energies
Preperation base plate with pillars, 2013

## Slide 4: Ultimate heavy ion intensities...
Recent status:
0.1 pmA, p (from MUCIS)
1 pmA, 48Ca (from ECR)
1 pmA, 50Ti (from PIG/ECR)
0.2 pmA, 238U (from MeVVa)
Alvarez (1975)
HLI
28 GHz-ECR
ion source
7.5 MeV/u cw- heavy ion linac
36 MHz HSI
U4+
U28+
Transport Line
(Space for Future Upgrades)
108 MHz HE-Linac
(Booster LINAC -> FAIR-SIS100-Direct Injection)
Heavy ion high intensity linac developments, W. Barth, 4.2.14

## Slide 5: 28 GHz-ECR ion source
Heavy ion high intensity linac developments, W. Barth, 4.2.14
RF injection side
Beam extraction side
GM-refrigerator
Solenoid coil
Iron yoke
Courtesy of T. Nakagawa, RIKEN Nishina Center, Japan
Upgrade to increase pulse intensities for medium and heavy ions (FAIR and cw-heavy ion beams) by a factor of 10-15!
I(Aq+)  ECR2
  Increase of RF = ECR  B
  Higher magn. flux density (sc magnets; up to 4.5 T)
SCECRIS – High Versatility
  Adjustable axial and radial magnetic fields  adaptation to different working points
  High charge state beams  LINAC-injection without postacceleration
  Cw-mode/special pulsed mode for high pulse intensities
  Low material consumption  high efficiency
  High stability and low beam noise
Roadmap
  Acquisition of SC-magnet system, …
  Commissioning/Optimization existing test facility
  Further R&D@test facility; achieving optimum operating conditions
  Transfer to the GSI-HLI

## Slide 6: H-type Cavity Developments I
Heavy ion high intensity linac developments, W. Barth, 4.2.14
325 MHz-CH-prototype (nc), commissioning@FAIR-p-LINAC test stand (2014)
Prototyping of HE-LINAC and cw-LINAC H-type accelerator cavities
325 MHZ-Crossbar H-cavity (HE-LINAC-Booster)
Cold model
sc-prototype
nc-IH-cavity
nc-CH-cavity
sc-CH-cavity
β=0.1565

## Slide 7: H-type Cavity Developments II superconducting Crossbar H-mode cavity (CH)
CH-prototype cavity (360 MHz,  = 0.1, 19 cells)
Heavy ion high intensity linac developments, W. Barth, 4.2.14
Measured Q-value as function of the accelerating gradient
Vertical test setup of the sc-CH-prototype cavity
U. Ratzinger, H. Podlech (Univ. of Frankfurt)
325 MHz CH (Booster linac)
217 MHz CH (cw linac)

## Slide 8: cw-LINAC-Demonstrator
Heavy ion high intensity linac developments, W. Barth, 4.2.14
High Charge State Injector (existing)
CH-cavity (5.1 MV/m
2014 (delivery)
Cryostat
2014 (delivery)
delivered
sc solenoids (9.3 T)
2013: Test environment assembled
2014: 1st tests (warm & cold)
2015: First beam tests @GSI

## Slide 9: Pushing the limits: cw-heavy ion beams@coulomb barrier
Heavy ion high intensity linac developments, W. Barth, 4.2.14
He-reservoir
Advanced Demonstrator
High Charge State Injector
Wkin = 4.6 MeV/u (heavy ions)
Wkin  5.8 MeV/u (medium ions)
VENUS/Berkeley: 400 µA, Ca11+ (CAPRICE/GSI: 50 µA, Ca10+)
SuSI (MSU), 18 GHz): 200 µA Ni12+, 180 µA, Ni17+ (CAPRICE(GSI: 50 µA, Ni9+)
SECRAL/IMP Lanzhou, 24 GHz: 40µA, Ni19+ ), limited by oven technology
Step 1 (2016)
Step 2 (2019)
Power Supplies, rf-amplifiers and controls

## Slide 10: Outlook
Heavy ion high intensity linac developments, W. Barth, 4.2.14
New HIM building@campus/JGU-Mainz provides Infrastructure (>2016):
preparation of superconducting rf-cavities
rf testing (warm&cold cavities)
cleanroom environment for entire mounting of accelerator string
infrastructure available for different accelerator facilities

## Slide 11: Backup: Integration studies/cw-linac@FAIR/GSI

## Slide 12: Backup
Chart: 
| sc ECRIS | Prototyping (HE-LINAC) | Advanced sc-Dem.
Verkauf | 160 | 160 | 5000
Chart: 
| sc ECRIS (GSI) | Prototyping/HE-LINAC (GSI, GUF) | Advanced sc-Dem. (GSI, HIM, GUF)
Verkauf | 5 | 20 | 6
Budget
Personell
Heavy ion high intensity linac developments, W. Barth, 4.2.14