## Slide 1: CMS Level 1 Track Trigger for HL-LHC
DTS - An AM-based Trigger Approach
Tanja Harbaum (KIT)
System Overview
10000 tracks per collision
400 billion tracks per second
Pattern Recognition
  Generated Pattern Bank of interesting tracks
  One pattern defines a road into the tracker
  Compare the incoming data to the Pattern Bank
128 Bits per Pattern
  Set of 8 layers
  16 Bits per superstrip address
  Specify a low granularity tracker strip
~100 M Patterns overall
  > 1 Gbyte data has to be loaded and compared within microseconds
  DDR3-SDRAM: bit rate 34 Gbyte/s is not enough
Pattern Recognition - Approach
Content Addressable Memory (CAM)
  Provide hit result within one clock cycle
Efficient utilization of FPGA structure
Port Associative Read only Memory features
Minimization by logic
  Decrease number of LUTs per Pattern
  Depends on the composition of the Pattern Bank
  Utilise FGPA vendor tools
Extensive minimization accessible
15000 pattern -> 7300 LUTs
3.5% of xc7v330t
How can we find a needle
in this haystack within 10
?
We know how interesting particles look like:
Let‘s make some pictures of them
!
Implementation
FPGA based Approach
Detector
Frontend Pipelines
Readout Buffers
Level 1
100 kHz
40 MHz
Latency
Actions
Data Transfer
Trigger Tower Formation
Pattern Recognition
Track Fitting
Vertexing
track
One pattern
Pattern Bank
  SRAM cell
  CAM cell
L1 Track Trigger Board
FPGA CAM Board Architecture