## Slide 1: Compact Laser Synchronization
MTCA.4 Based Laser to RF Synchronization
Peter Peier
Compact Laser Synchronization
Dresden, 26. February 2014

## Slide 2: Contents
Motivation
Electro-Optic Bunch Length Measurement
Laser Synchronization Scheme
MTCA.4 Components
Data Transmission
Short and Long Term Measurements

## Slide 3: Motivation – Lasers at Accelerators
Accelerator
Timing and Synchronization
Gun
Laser
Laser
Heater
Laser
Diagnostic
Seeding
Laser
Pump-Probe
Laser
e-

## Slide 4: Motivation – Electro-Optic Bunch Length Measurement
Synchronized Ytterbium fiber laser is modulated by Coulomb field of the electrons (ETHz) in EO crystal (GaP)
oscillator
amplifier
AOM
synchronization
compact
EO Monitor
detector
timing
RF
timing signal

## Slide 5: Synchronization of EOD Laser

## Slide 6: EOD Laser
Optimized laser for electro-optical bunch length measurement at XFEL
Mode locked Yb fiber laser developed at PSI and assembled at DESY
Specifications:
  Wavelength: 1030nm
  Bandwidth: 25-50nm (amplified: 100nm)
  Pulse length: 5ps (compressible to <100fs)
  Pulse energy: 1-2nJ (amplified: 100nJ)
  Repetition rate: 54MHz (amplified: 4.5MHz)
  Temperature stabilized to 0.1°C

## Slide 7: RF Generation and Detection
LO
RF
IF
DRTM-DWC10
RF generation Box (19”) to generate sinusoidal RF signals from laser pulses
10 channel high-frequency down-conversion from 1GHz – 4GHz
Merge 19” RF box and downconverter board to a single RTM unit

## Slide 8: Digitizing and Signal Processing
PCIe & PtP
IF in
ADC
FPGA
DAC
SIS8300-L
10 channel, 16 bit digitizer (AC or DC coupled) – low noise design
10 MS/s to 125 MS/s
Virtex 6 FPGA
Two 16bit DACs

## Slide 9: MTCA.4 4-Channel Piezo Driver
4 power amplifier with 0-100V, -85V/+85V
DAC outputs +/-5V, +/-10V, 0/5V, 0/10V
Each power amplifier can drive up to 10uF capacitance.
Applications:
  Cavity fine tuning
  Laser to RF synchronization
  Link Stabilization
DAC
DAC
PA 1
PA 3
PA 2
PA 4
EXT. PS Input
DRTM-PZT4

## Slide 10: Blockdiagram of Signal Processing
PI: PI controller
PCIe: Peripheral Component Interconnect express
MGT: Multi-gigabit transceiver
LLL: Low Latency Link
SPI: Serial Peripheral Interface

## Slide 11: Integration in Control System – Server and Panel

## Slide 12: Phase Noise and Baseband Noise

## Slide 13: Long Term Locking

## Slide 14: Conclusion and Outlook
Laser to RF synchronization with MTCA.4 components successfully tested!
Short and long term measurements carried out on the EOD Laser.
Competitive jitter numbers measured.
System was also tested with commercial laser (Gun Laser 3).
Second revision of Piezo driver board will arrive in March.
EOD measurements at FLASH planned.
Merge RF Box and downconverter RTM to a new RTM.
Control motor with DFMC-MD22 on DAMC-FMC20.

## Slide 15: “Laser Synchronization Task Force”
Uroš Mavrič
Konrad Przygoda
Lukasz Butkowski
Hans-Thomas Duhme
Matthias Felber
Michael Fenner
Christopher Gerth
Tomasz Kozak
Paweł Prędki
Holger Schlarb
Bernd Steffen

## Slide 16
Thank you for your attention!