## Slide 1
Micro-Pattern Gaseous Detectors
Fabio Sauli
TERA Foundation and CERN
Bethe Forum on Particle Detectors
Bonn, March 31-April 11, 2014

## Slide 2
THE ANCESTORS
PART 1

## Slide 3: HISTORICAL BACKGROUND
The first proportional counter:
Thin anode wire centered in a cylindrical cathode:
Charge
Collection
Charge
Multiplication
E. Rutherford and H. Geiger,
Proc. Royal Soc. A81(1908)141
Charge-voltage characteristics:
G.C. Montgomery and D.D. Montgomery
J. Franklin Inst. 231(1941)447

## Slide 4
Georges Charpak (1968)
Grid of thin anode wires between two cathode planes:
The first MWPC (10x10 cm2)
G. Charpak et al, Nucl. Instr. and Meth. 62(1968)262
Roger Bouclier
MULTIWIRE PROPORTIONAL CHAMBERS (MWPC)

## Slide 5
Prototype for the Split Field Magnet detector
G. Charpak et al, Nucl. Instr. and Meth. 97(1971)377
Charpak
Sauli
EARLY LARGE MWPC (1970)
Santiard
Georges Charpak
1992 Nobel Laureate for Physics
1992

## Slide 6
CMS muon end-cap detectors (2007)
~ 2000 Cathode Strip Chambers
SPLIT FIELD MAGNET (1973)
40 large MWPCs
R. Bouclier et al,
Nucl. Instr. and Meth. 115 (1974)235
D. Acosta et al,
Nucl. Instr. and Meth. 453(2000)182
MWPC-BASED LARGE TRACKING DETECTORS

## Slide 7
David Nygren, 1976
Full 3-D localization:
x: Anode wire
y: Center of Gravity (COG) on charge induced on Pad Rows
z: Drift Time
D. Nygren and J, Marx, Phys. Today 31 (1978) 46
TIME PROJECTION CHAMBER (TPC)

## Slide 8
3-D Tracking:
Particle Identification from dE/dx:
PEP4 TPC, D. Nygren personal communication
PEP-4 TPC AT SLAC

## Slide 9
5 m Ø - ~ 100 m3
J. Alme et al,
Nucl. Instr. and Meth. A622(2010)316
Pb-Pb interaction at 2.76 TeV:
ALICE TPC AT CERN LHC (2007)

## Slide 10
WIRE CHAMBER
LIMITATIONS

## Slide 11
LOCALIZATION ACCURACY
Y: Wire spacing
~ 5 mm
Z: Drift time
electrons diffusion
W. Atwood et al,
Nucl. Instr. And Meth. A306(1991)446
ACCURACY VS DRIFT LENGTH
X: COG on Pad rows
200 µm
500 µm
ACCURACY VS ANGLE
200 µm
160 µm

## Slide 12
VOLUME RESOLUTION
Z: Drift time
Signal width ~ 200 ns
DZ ~ 10 mm
Y: Wire spacing
DY ~ 10 mm
0
4
8 mm
-4
-8
8 mm
X: Charge induction on pad rows:
DX ~ 10 mm
Volume resolution
DV~ 50 mm3

## Slide 13
Space charge near the anode:
Slow Positive Ions buildup modifies the electric field
RATE-DEPENDENT GAIN REDUCTION
e-
~ 100 ns
I+
~ 100 µs
Relative gain as a function of rate:
A. Breskin et al, Nucl. Instr. and Meth. 124(1974)189
~ 104 mm-1s-1

## Slide 14
SLOW POSITIVE IONS ACCUMULATE IN THE DRIFT VOLUME AND MODIFY THE FIELD RESULTING IN TRACKS DISTORTIONS:
POSITIVE IONS BACKFLOW
PERCENTAGE DRIFT FIELD MODIFICATION (ALEPH MWPC-TPC)
ION BACKFLOW FRACTION:
DRIFT CURRENT/ANODE CURRENT
ID
IA
MWPC-TPC TYPICAL: IBF~30%
ONLY POSSIBLE AT SMALL RATES:
Max electron drift time
< Time between events
GATING:
ADD A WIRE MESH WITH VOLTAGE-CONTROLLED TRANSPARENCY

## Slide 15
DISCHARGES AND BREAKDOWN
High gains: Transition from proportional amplification to streamer and/or breakdown
N. Koori et al, Jap. J. Appl. Phys. 25(1986)986
Spark damages in MWPCs:
Fabio’s Museum of Horrors

## Slide 16
THE RAETHER LIMIT
Maximum avalanche size before transition or breakdown:
QMAX=(Primary ionization)x(Gain) ~ 107 e
Multiwire structures:
Cathode pre-amplification of field emitted electrons
103
104
P. Giubellino et al, Nucl. Instr. and Meth. A245(1986)155
Fast particles DE ~ 2 keV:
Q=(100)x(104)=106
Neutrons DE ~ 2 MeV
Q=(105)x(104)=109
MC
MA
M=MC x MA
Typical proportional gain ~ 104

## Slide 17
GASEOUS COUNTERS AGING UNDER IRRADIATION
Counting rate plateau degradation after long term irradiation:
~ 108 counts
E. Farmer and S. Brown, Phys. Rev. 74(1948)902
T=0
Gradual loss of the energy resolution:

## Slide 18
MWPC: ORGANIC DEPOSITS AND AGING
Polymerization of organic compounds with formation of deposits on thin wires:
O. Ullaland, LBL-21170 (1986)107
I. Juric and J. Kadyk, LBL-21170 (1986)141
I. Juric and J. Kadyk, LBL-21170 (1986)141
M. Binkley et al,
Nucl. Instr. and Meth. A515(2003)53

## Slide 19
MICROPATTERN:
THE NEW APPROACHES

## Slide 20
MICRO-STRIP GAS COUNTER (MSGC)
Anton Oed, 1988
A. Oed, Nucl. Instr. and Meth. A263(1988)351
10 µm wide anode strips, 50 µm cathode strips at 100 µm pitch on glass substrate:

## Slide 21
MSGC CONSTRUCTION
J. Bohm et al, Nucl. Instr. and Meth. A360(1995)34
MSGC prototype
400 anode strips at 200 µm pitch:
R. Bouclier et al,
Nucl. Instr. and Meth. A367(1995)163

## Slide 22
MSGC PERFORMANCES
R. Bouclier et al, Nucl. Instr. and Meth. A367(1995)163
Single track signal width (two-track resolution):
200 µm pitch
Position accuracy (fast particles):
106 mm-2 s-1
~ 40 µm rms
FW ~ 400 µm
Volume resolution
DV ~ 1 x 1 x 2= 2 mm3
Fast signals ~ 30 ns (1.5 mm)
Rate capability: 1 MHz/mm2

## Slide 23
MSGC DISCHARGE PROBLEMS
Pre-amplification of electrons emitted by cathode strip edges
T. Beckers et al, Nucl. Instr. and Meth. A346(1994)95
“Normal” gain 2000
PA gain 20000
Fabio’s Museum of Horrors

## Slide 24
NEW MICRO-PATTERN GAS DETECTORS (MPGD)
R. Bellazzini et al,
Nucl. Instr. Meth. A424(1998)444
A. Ochi et al,
Nucl. Instr. and Meth. A478(2002)196
P. Rehak et al
IEEE TNS-47(2000)1426
MICRO-PIN ARRAY
F. Bartol et al
J. Phys.III France 6(1996)337
COMPTEUR A TROUS
MICRO-PIXEL CHAMBER
MICRO-GROOVE CHAMBER

## Slide 25
Y. Giomataris et al,
Nucl. Instr. and Meth. A 376(1996)29
HIGH/LOW FIELD REGIONS SEPARATED BY A MESH
GAP UNIFORMITY:
SPACERS OR PILLARS
MICRO-MESH GASEOUS STRUCTURE (MICROMEGAS)
50-100 µm
200 V/cm
50 kV/cm

## Slide 26
BULK MICROMEGAS MANUFACTURING
I. Giomataris et al,
Nucl. Instr. and Meth. A560(2006)405
Laminated Photoimageable coverlay
Frame
Stainless steel
mesh on frame
Exposure
Development
+ cure+ cut
Read-out board
pillar
pad
J. Bouchet et al,
Nucl. Instr. and Meth. A574(2007)425

## Slide 27
MICROMEGAS PERFORMANCES
100 µm pitch
Signal distribution: 200 µm fwhm
J. Derré et al,
Nucl. Instr. and Meth. A459(2001)523
Fast electron signal with slow ion tail:
A. Delbart et al, Nucl. Instr. and Meth. A461(2001)84
Energy resolution:

## Slide 28
C. Bernet et al, Nucl. Instr. and Meth. A536(2005)61
9 ns rms
MICROMEGAS FOR THE COMPASS EXPERIMENT AT CERN
SPACE RESOLUTION:
TIME RESOLUTION:
12 planes in 3 stations X,Y, U, V
40x40 cm2 active
350 µm strips with digital readout
70 µm rms

## Slide 29
LARGE SIZE MICROMEGAS
ATLAS Forward muon upgrade:
1024 mm
J. Wotschack, RD51 Meeting (CERN 2013)
T. Alexopoulos et al,
Nucl. Instr. and Meth. A717(2010)161
J. Wotschack, JINST 7, C02021 (2012)

## Slide 30
GAS ELECTRON MULTIPLIER (GEM)
F. Sauli, Nucl. Instr. and Meth. A386(1997)531
Thin (50 µm) metal-coated polymer foil with high density of holes:
SINGLE GEM WITH 2-D READOUT BOARD
A. Bressan et al, Nucl. Instr. and Meth. A425(1999)254

## Slide 31
GEM MANUFACTURING
70 µm
55 µm
5 µm
Standard GEM:70 µm Ø at 140 µm pitch
50 µm Kapton
5 µm Cu
Metal etching
Kapton etching
Second masking
Metal etching
and cleaning
Photoresist coating, masking and exposure to UV light
DOUBLE MASK PHOTOLITHOGRAPHY

## Slide 32
GEM DETECTOR PERFORMANCES
30 ns ~ 1.5 mm
10 ns
FAST ELECTRON SIGNAL ONLY
ON ANODE STRIPS
GEM
INDUCTION
M. Ziegler, PhD Zürich Univ. (2002)
DRIFT
TWO-TRACK RESOLUTION (DRIFT TIME):
TWO-TRACK RESOLUTION (PROJECTION):
400 µm fwhm
VOLUME RESOLUTION
~ 1 mm3
A. Bressan et al, Nucl. Instr. and Meth. A425(1999)262

## Slide 33
Triple-GEM (TGEM):
Cascaded GEM electrodes
C. Büttner et al, Nucl. Instr. and Meth. A409(1998)79
MULTI-GEM DETECTORS
HIGHER GAIN, LOWER VOLTAGE ON EACH GEM

## Slide 34
31x31 cm2 active 2-D strip readout
Total thickness in active area ~ 0.7% X0
TRIPLE-GEM DETECTORS FOR COMPASS
2-D readout board: 400 µm pitch strips
Honeycomb
plates
GEM foils
Readout
board
80 µm
350 µm
C. Altumbas et al,
Nucl. Instr. and Meth. A490(2002)177

## Slide 35
GEM SECTORING
COMPASS TRIPLE-GEM DETECTORS:
12 SECTORS WITH PROTECTION RESISTORS
CENTRAL BEAM KILLER
SECTOR SEPARATION
VOLTAGE-CONTROLLED
CENTER

## Slide 36
TRIPLE-GEM DETECTORS FOR COMPASS
22 DETECTORS, OPERATIONAL 2002-2012

## Slide 37
GEM DETECTOR PERFORMANCES
65 µm rms
12 ns rms
SPACE ACCURACY
TIME RESOLUTION
RATE CAPABILITY
J. Benlloch et al, IEEE NS-45(1998)234
C. Altumbas et al, Nucl. Instr. and Meth. A490(2002)177

## Slide 38
TOTEM TRIPLE-GEM DETECTOR
SEMI-CIRCULAR MODULES
M.G. Bagliesi et al, Nucl. Instr. and Meth. A617(2010)134

## Slide 39
CYLINDRICAL GEM DETECTORS
KLOE-2 Inner Tracker: Three layers of Triple-GEM detectors
A. Balla et al, Nucl. Instr. and Meth. A732(2013)221
SPATIAL RESOLUTION
(X: Bending Plane):

## Slide 40
COMPASS UPGRADE: TGEM WITH PIXEL AND STRIPS READOUT
CENTER: 32x32 PIXELS, 1 mm2 SIDES: 512x512 STRIPS, 400 µm pitch
B. Ketzer et al, 2007 IEEE Nucl. Sci. Symp. Conf. Rec.
M. Krämer et al, 2008 IEEE Nucl. Sci. Symp. Conf. Rec.
MEASURED FLUX IN HADRON BEAM:
1.2 105 Hz/mm2

## Slide 41
SINGLE MASK PROCESS
LARGE GEM MANUFACTURING
M. Alfonsi et al, Nucl. Instr. and Meth. A617(2010)151

## Slide 42
LARGE TRIPLE-GEM
CMS Muon Detector Upgrade
M. Tytgat, MPGD 2013
990 x (220-455)mm2
Radial Readout Strips
0.6 to 1.2 mm pitch

## Slide 43
LARGE TRIPLE-GEM
990 mm
TRIPLE GEM
~ 260 µm
D. Abbaneo et al, JINST 9(2014)C01053
EFFICIENCY
POSITION ACCURACY

## Slide 44
THICK GEM (THGEM)
MECHANICAL DRILLING OF METAL-CLAD PC BOARD:
SELF-SUPPORTING
HIGH GAIN
P. Janneret, Thesis at Neuchatel University (2001)
ALSO NAMED LARGE ELECTRON MULTIPLIER (LEM)
R.Chechik et al,
Nucl. Instr. and Meth. A535(2004)303
Breskin et al,
Nucl. Instr. And Meth. A623(2010)132
A. Badertscher et al, Nucl. Instr. And Meth. A617(2010)188

## Slide 45
THICK GEM (THGEM)
LARGE RIM:
HIGH GAIN
CHARGING UP
GAIN
V (kV)
0
10 µm
100 µm
0.1 mm rim
No rim
RIMLESS:
LOW GAIN
STABLE
M. Alexeev et al, Nucl. Instr. and Meth. A695(2012)159