## Slide 1: Status of data management and data storage
Krzysztof Wrona, WP76
16th XFEL DAC meeting
May 26th, 2014, Hamburg

## Slide 2: Outline
  Data management big picture, scientific data definitions and policies
  DAQ and DM architecture, prototype implementation
  Data formats
  Offline data storage and access
  Catalogs and web applications
  IT services for test stands

## Slide 3: Data management – functional overview
Data management “Big Picture” (common view WP75 and WP76)
  Detailed description of calibration data handling on WP75 session by S.Hauf
  Details and implementation status on WP76 session by K.Wrona/D.Boukhelef
Drawing by S.Hauf
Figure describes:
  Data types
  Data flow
  Components
  Functionality
  Actors

## Slide 4: Scientific Data – definitions & policies
Raw data, […], represents digitized signals captured by detectors and not altered by detector-specific corrections or calibrations, […]. Vetoing, either by hard- or software triggers and zero-value suppression, […], may have been performed and are irreversible. […]. Raw data is the main archival data product at the European XFEL. It is not foreseen to be exported outside the facility, and is not meant to be directly user accessible.
Calibrated data is generated from raw data, by applying detector-specific corrections and transformation to physical units (calibration) […]. Calibrated data is the standard data product users will be provided with. It is not archived though; […], it will be reprocessed on the fly from the raw data repository using the appropriate calibration parameters provided by the calibration database.
Extracted from a draft for a special issue of Synchrotron Radiation News (and in similar wording for a IEEE NSS/MIC 2014 contribution)

## Slide 5: DAQ and DM architecture
Layered architecture focusing on scalability and flexibility
Allows for data processing on each layer
Addresses issue of simultaneous reliable data recording and fast user access
Includes offline data analysis at the facility
Architecture
Main DAQ stream
Fast feedback stream

## Slide 6: Slice test (prototype)
Prototype
Demonstrated sufficient performance of DAQ chain for ½ Mpxl detector from train builder to online data storage using prototype system
Easily scalable to 1Mpxl – requires more hardware
16 streams per 1Mpx det., 1GB/s per data stream
Final acceptance tests when detectors are available

## Slide 7: Prototype implementation
Network setup
Definition of data formats
PC layer software
Data flow in DAQ
Details in D.Boukhelef presentation – WP76 review
Writing data to disks

## Slide 8: Ongoing work
Generic data sink
  Generalization of PC layer to cope with data format from all different data sources, not only 2D detectors
  Data format description language and API for encoding binary data at source and decoding data format on sink device
  Prove of concept has been demonstrated,
  Data description specification and API will be released after selected use cases (i.e. 2D, digitizers, commercial cameras) are implemented and tested (estimated for July)
Naming convention for raw data files
  Naming scheme for files defined
  Raw data repository structure
  Calibration data repository structure
  raw.rXXXX.sXXXXXX.h5
  r – run number, s – sequence number, X – digit

## Slide 9: HDF5 Data format
HDF5 is chosen as a container to store experiment data
  Structure of HDF5 file resembles the file system view with HDF5 groups and datasets corresponding to folders and files
  XFEL API for HDF5 implemented in Karabo and used at slice test and calibration pipeline
  Organize data according to the data source
  Provide the same high level data organization scheme
  Provide HDF5 data navigation and correlation scheme using simple relational database model (data are written as records)
  Use simple data dataset types to maximize portability between different tools and languages
  FLASH and LCLS expressed the interest to implement this model for the next stage of their experiments i.e. FLASH-II and LCLS-II
Data converter – xtc to XFEL hdf5 format
  Converter for CFEL data collected at LCLS developed and files made available to FLASH DM experts and CFEL users – waiting for feedback
  CFEL scientist will start using it mid-June for ‘data reduction’ developments
Discussion on high level data format with LCLS, Flash and CFEL ongoing

## Slide 10: Export and transformation tool
Tool for exporting calibrated, slow/fast data to external users
  Selective, i.e. allow users to select which data parameters they want in the export file.
  Personalized view: users may rearrange data groups in the new dataset according to their own needs
  Predefined templates (for major use-cases) can be provided
Actual physical layout
User’s desired view
Mapping
Data repository
Exported dataset
From D.Boukhelef presentation – WP76 review

## Slide 11: Preparation for ¼ Mpxl test stand
¼ Mpxl detector test stand
  Initially PC layer and storage servers combined – 4 servers
    Per host: 24 CPU cores, 128GB RAM, 30TB disk space, 2 x 6Gbs SAS, 2 x 10GE
    Servers purchased, installed and waiting to be moved from CC to Hera-South
    Network configured according to the slice test design
  Software
    PC layer, data formatting, integration with calibration pipeline, storing data
Slice test network setup
¼ Mpxl test stand network setup

## Slide 12: Offline data storage & processing
Offline data storage classes
  Raw and calibration data repositories – commodity storage, distributed system (dCache) with parallel NFS (pNFS) access protocol. Raw data files will be organized according to experiment runs and appropriate ACL will be defined using NFS4.1 ACL. Initially ~10PB capacity
  Archive – tape backend for data repositories (e.g. LTO6 technology)
  Scratch space – cluster file system, ~1-2PB, used for hot data processing, export of calibrated data, no backup, fast access
  Space for user data, e.g. 5TB per beamtime, backup
Offline Computing
  1000 CPU cores per 1PB

## Slide 13: Data storage and archive – current status
Service provided to XFEL scientists:
  data import using Globus Online, rsync, scp, USB media
Data stored on dCache system
  Distributed over 18 servers with 120TB allocated to XFEL
  Tape archive
Access
  Webdav interface (simple browsing)
  NFS4.1 (parallel NFS)

## Slide 14: Calibration catalog
Calibration catalog
  Manages calibration data and defines which constants to use
  Calibration database concept defined (presented on the last DAC meeting)
  Technical design including database model – done
  Implementation: web application + Restful API for constants management and access – in progress (advanced)
  First tests and validation with ¼ Mpxl test stand (July)
Details in L.Maia presentation – WP76 review

## Slide 15: Metadata catalog
Decided for in-house implementation
  Pros for in-house development
    Easy integration with calibration database and other services already implemented at XFEL (e.g. authentication)
    Much easier to include new features if required
    Usage of the same technology as for the other apps (rapid development, easier maintenance)
  Cons
    Will consume developer resources
Development plan
  1st stage: Simple database model (beamtime, investigation, runs, files)
    Fulfills all current requirements, cross-checked with WP75 and LCLS developer
    1st stage implementation estimated to be ready in few months (i.e. first results next DAC)
    Recruitment of additional man power for web application in progress
  Next stage:
    Define exact requirements for facility operation phase (in 2017)
      Enhance authorization
      Integration with karabo (e.g. insertion of experiment parameters)
      Possibly implementation of log book according to LCLS model

## Slide 16: Status of web applications deployment
General concept for web applications deployment
  Single entry point via F5 switch
  Each application running on separate Virtual Machine
    Allows for independent applications deployment
    Allows for load balancing and redundancy (i.e. high availability)
Next step:
  implement full redundancy (including DB replication) and load balancing (where appropriate) according to the existing concept
Similar setups for development and testing exist

## Slide 17: Test stands management
Tool | Function | Status (Dec 2013) | Status ( May 2014)
Puppet | Basic computer installation and configuration | In preparation | In production
Asset Management | Describe physical devices, link documentation, firmware and software compatibility | Prototype | In production
ePlan | Planning and documentation of wiring | Installed | Definition of templates, first usage by CIE group, Integration with asset management required
Package repository | Collection of software packages | Partially | In production
Karabo Configuration DB (KCDB) | Defines needed hardware and software resources for installation | In preparation, currently using XML | Prototype database
Karabo-server-control | Installation of karabo device servers and devices according to KCDB | Not exist yet, currently manual | Interface to KCDB defined, prototype exists
eLog | Provide history of the Test Stand | Production | In production
Alfresco | Documentation, definition | Production | In production
Redmine | Project management and issue tracker | Mantis was used for bug tracking | In production
Services required for test stands management (later for instruments)
Details in J.Szuba presentation – WP76 review

## Slide 18: Summary
Export data policies defined
¼ Mpxl test stand will be used to further validate DAQ developments using real detectors
Work is progressing on data formats
Development of web applications in good shape. Decision on in-house development of metadata catalog
Services supporting “test stand” management improved

## Slide 19: Acknowledgments
Acknowledgments
  D.Boukhelef
  S.Hauf
  B.Heisen
  L.Maia
  J.Szuba
  C.Youngman
  WP76 members
  DESY IT group

## Slide 20: Backup slides

## Slide 21: Metadata catalog
Justification for in-house implementation
  iCat does not fulfill XFEL requirements
    Desy experience shows this project is very complex and difficult to setup
    Production level service would require a lot of effort (administration, close collaboration with STFC would be required)
    Doesn’t fulfil all our requirements, this means we would have to try to influent it’s future developments (as discussed in last XDAC)
  LCLS catalog – much closer to the needs, but:
    many dependencies on other LCLS internal services
      direct dependencies on database level
      difficult to extract required parts
    Implements processes specific to LCLS (e.g. conversion from xtc to hdf5, cable management)
    no user defined parameters (is planned)
    would require additional developments using different technology
    no software release management
      LCLS tool developed by single person
      continues changes and enhancements according to current LCLS needs and internal schedule