## Slide 1: Review of last year's firmware developments
Lukasz Butkowski
MSK Firmware development team

## Slide 2: Statistics Redmine
Chart: 
| bugs : 30 | features:21 | improvement:21 | new implementations :52 | others:7
reported issues | 30 | 21 | 21 | 52 | 7
Chart: closed issues
| bugs : 20 | features:8 | improvement:10 | new implementations :24 | others:2
reported issues | 20 | 8 | 10 | 24 | 2
Reported issues: 131
Closed issues: 65
In progress: 18
Redmine data: since (02.2013)

## Slide 3: Statistics SVN
SVN data:
17 developers (6 with minimum of 5% of input)
600 commits
Around 19000 changes committed

## Slide 4: Main development points:
Boards in framework:
SIS8300
SIS8300L
uTC v1.3
uVM v1.2, v2.0
DAMC - TCK7
TMCB v1.0
DAMC2 v1,v2
uFMC20 rev.A
PZ16M
RTMs: DWC10, DWC8VM1, PZT4, AD84
Application in framework:
LLRF slave and master controllers
LLRF slave and master controllers for CW operation
Single cavity controller
Toroid detection
DCM
REFM
Laser locking controller
PIEZO controller
Radiation monitor
KLM
Test application
All shares the same libraries:
PCIe with DDR DMA access, MIG (DDR) arbiter, DAQ components, LLL – optical links supervisor, generic FIFO, Internal Interface (address management), I2C controller + chips support, etc.

## Slide 5: Main development projects:
LLRF for FLASH installation
Most of functionality works in operation since January 2014, projects included:
  SIS8300L – field detection application for LLRF controller
  uTC v1.3 – main LLRF controller application
  uVM v1.2 – VM part of LLRF controller
  SIS8300 – toroid detection application for beam loading compensation
  PZ16M – PIEZO controller firmware
Single cavity controller
Field detection and main LLRF controller on one board.
  SIS8300L – single cavity controller for GUN
  SIS8300L – single cavity controller for HZDR
  SIS8300L – single cavity controller for REGAE

## Slide 6: Main development projects:
LLRF for CW operations at CMTB
  SIS8300, SIS8300L – field detection application for CW LLRF controller
  uTC v1.3, TCK7, uVM2.0 – main LLRF controller application for CW operations
Laser locking controller
  SIS8300L – controller based on Simulink
  uFMC20, PZT4 – PIEZO controller
BSP for DAMC TCK7
  Board support package with basic functionality for external company
Test application for SIS8300L
  Implementation of functionality for post production tests of board,
…
In total around 20 projects in many facilities to support.

## Slide 7: General framework improvements
TCL scripting
  Automation of generation of projects,
  Auto versioning of firmware, repository revision of firmware and compilation timestamp visible in firmware registers,
  Independent of platform, supported by Xilinx tools,
  Build and map file creation automation,
  Ready to be used on build server,
Simulink integrating
  Scripts makes possible to build application from Simulink and generate firmware for selected board (currently only SIS8300)
  Based on TCL scripts
DOXYGEN
  Scripts in the repository allows for generation of documentation based on the code comments

## Slide 8: Repository structure
SVN repository: main development tool
Framework structured:
separation of applications, libraries, boards and modules support (FMC,RTM)
All together is combined into the projects,
Main development is done in branches, when done moved to the trunk.

## Slide 9: Framework structure
adapter
IO
ENT_TOP - top entity
PKG_BOARD
Board configuration
PKG_APPLICATION
Application configuration
ENT_BOARD_PAYLOAD
ENT_APPLICATION_TOP
User logic
Application interface
Board interface
ENT_BOARD_TOP
Interfaces:
Logic,
ADC,DAC,
DDR,
PCIe,
LLL,
SPI, I2C etc…
project.tcl
( board name + application name + board configuration + application configuration)
board.tcl
application.tcl
FMC,RTM module
module.tcl

## Slide 10: Build Server
Build server under test (currently Jenkins solution under test)
  Every project has a specified job,
  Compiles firmware on the server using scripts,
  Checks integrity of repository,
  Provides bit, map file and reports as a build output
  Automated deployment: Able to load build output to the station
  Able to run testing scripts,
  Possibility to connect Redmine issue to the build number,
Still need to write many scripts,

## Slide 11: Current development
General:
  PCIE update: payloads with more then 1DWORD, new DMA schemes, DMA for all memory space, AXI4 bus, and others,
  Change of Internal interface library, AXI4lite, separate read/write transactions, map file in XML format
  Build server, TCL improvements,
Boards in framework:
  uFMC25
  uFMC20revB
  DS800
Applications
  LLRF controller for XFELL/FLASH on TCK7 and uVM2.0
  Beam based feedback , BCM+BAM
  DCM integration,

## Slide 12: Conclusion
Number of issues are growing faster then we can close them,
  Missing manpower assign only for firmware development
Framework ready for automation,
  Projects scripts,
  Builds, deployment,
  Tests of solution in progress
Universal modules and libraries components that can be used in many projects,

## Slide 13
Thank you for your attention