## Slide 1: Safety Training of Users
Dr. Pouneh Saffari
Safety and Radiation Protection Group (SRP)
Senior Laser Safety Officer
Prague , 22.09.2017

## Slide 2: Outline:
Introducing the Safety & Radiation Protection Group (SRP) at Eropean XFEL
Safety requirement for user proposal submission
Successful user proposal & safety letter
Policy regarding samples & substances
  Biological
  Nanomaterial
  Laser
  User safety training
  Answer to some questions

## Slide 3: Safety & Radiation Protection Group (SRP)

## Slide 4: Safety requirement for user proposal submission
Queries concerning the technical or safety feasibility of an experiment should be clarified with the instrument staff before the proposal submission
Detailed safety aspects of the experiment, resources, instrumentation, experimental set up information, samples & requirements for running the experiments must be declared in the proposal
Experiments requiring special safety precautions must be clearly stated in all proposal sections.
Safety group evaluates the proposal with regards to the safety:
Green: feasible
Yellow: feasible with cautions
Red: feasible with strict procedures required
Rejected: not feasible
Depending on the proposal evaluation further test or modification to the equipment may be required

## Slide 5: Successful Proposal & Safety Letter
If the beam-time is awarded, the safety group “may” need further information on the experiment in safety letter.
In safety letter main proposer is asked for :
  Experimental safety risk assessment due to additional safety hazards which include
  Step by step description of experimental set up if it is different from standard beam-line experimental setup
  Full description of all activities related to the experiments
  Operation instructions
Safety letter should be answered as soon as possible ; latest by one week before the beam-time to avoid delay in scheduling the experiment
Responsibility of all material, samples and equipment brought to European XFEL by users remain entirely to the proposer

## Slide 6: Samples & Substances
Following must be declared electronically in the proposal form:
  Each sample / substances brought by users
  Entire sample composition , chemical formula, CAS number (if available)
  How samples arrive to the European XFEL : brought by users / send to European XFEL
  Special requirements for using the sample at the instrument, reception & storage (fridges, humidity control, keeping in dark, etc) must be declared
  Associated danger with the reception of the sample/ substance and risks associated with
  sample/ substance disposal must be described by users
Standard samples/ substances must be ordered on user account directly to European XFEL
Storage containers must be clearly & permanently labelled with name of the owner, name of the substance, proper hazard labels according to Globally Harmonized System of Classification and Labelling of Chemical (GHS)
All samples and substances must be removed by users after completion of the experiment

## Slide 7: Samples & Substances
Onsite disposing of samples / substances must be followed by waste disposal policy of European XFEL
Disposal collective vessels and procedures are provided by safety group or lab support staff.
Biological agents are classified into 4 different risk categories according to the infection risk originating from them and following the technical rules in the EU’s legal classifications (Annex III to Directive 2000/54 EC) & additional national ordinance (TRBA 460-468):
Risk Group 1: Unlikely to cause human disease
Risk Group 4: Cause sever human disease and are serious hazards to employees, spread into the society ,no effective prophylaxis or treatment available
Hazard to human increases

## Slide 8: Permitted Biological Samples
Only biological samples from risk group 1 can be used at experiment station
Biological agent from risk group 2 can only be handled in the support laboratory but not at the experiment stations
Genetically Modified Organisms (GMO) samples from risk group 2 require notification towards the authorities prior to start the work, therefore the following is required:
  Brief summary of the research project+ purpose of experiment, work description + flow diagram explaining procedure to produce GMO , list of used vectors.
Biological safety officer may ask for extra info ; the complete doc is sent to genetic engineering authority accompanied by a letter from European XFEL managing directors for approval

## Slide 9: Nanomaterials / Radioactives
The most important measure to protect worker’s health is to minimize exposure to hazardous substances in the workplace
To minimize the exposure to nanomaterials, users must indicate all required engineering & personal protective equipment to carry out the experiment under safe conditions
Using radioactive samples/ substances is NOT feasible; external radioactive sources are not allowed in our facility.

## Slide 10: Laser
Users are not allowed to entre the instrument laser hutches at any time.
Bringing lasers to European XFEL is NOT feasible in early user operation
Laser operation by users is NOT feasible in early user operation
In steady operation later:
If users intend to operate the laser, they must :
1- Bring a document from their employer stating that they have necessary technical and safety knowledge in this field
2- Take the online experiment safety containing laser safety training slides
3- Upon their arrival to European XFEL attend an onsite laser safety training
If users intend to bring a laser, the supplier’s certificate indicating type, class, power, wavelength of the laser is mandatory to be declared

## Slide 11: Laser
All equipment brought by users to European XFEL must be checked by safety group.
All equipment brought and supplied by users must conform to the appropriate European and German safety regulations and accompanied by their user manual.
  All Class 3B or 4 laser for use at European XFEL must be registered with the senior LSO of the safety group at least 4 weeks before its arrival.
  Laser interlocks are required for class 3B & 4 lasers brought by users; the requirements must be discussed by the designated LSO and approved by the senior LSO of safety group.
  For European XFEL lasers, the instrument group will provide the appropriate Personal Protective Equipment (PPE).
  For lasers brought by users that are different in wavelength with the instrument’s lasers, PPE must be brought by users and it must be with full description declared and approved by safety group. Upon the users’ arrival the PPE must be checked by designated LSOs.

## Slide 12: Start of Experiment: Safety Approval Form (SAF)
Based on the proposal the necessary safety rules are described in SAF
SAF is posted at the beamtime with the following information:
  The period of validity
  List of people carrying out the experiment
  Information on measures to be taken during the experiment
  The risk analysis including comments from safety group
  A safety color code :
        Green SAF for experiments which present no risk; unattended operation is allowed
        Yellow SAF for experiments which need a particular check by safety group at the beginning of the experiment but after that the unattended operation mode is allowed
        Red SAF for experiments which present a risk so unattended operation mode is forbidden; at least one person must be present at all times (24h a day); users must not commence a red experiment on a weekend or on bank holiday

## Slide 13: Start of Experiment: Safety Approval Form (SAF)
  To modify the SAF (eg a change in the name, validity or sample), users must immediately contact safety group to revalidate the SAF.
  If the experiment rated yellow or red users must contact safety group:
  When they are ready to start the experiment, to obtain SAF
  At the end of experiment, so safety group may need to check the experiment station
  For the early users, colors have not been implemented. Strictly all experiments rated RED & users are all the time supervised by local contacts / instrument group

## Slide 14: Safety Training
Users must take the online safety training before their arrival
Once users successfully accomplished the online safety training, a certificate must be printed & emailed to the user office for validation of access control management system
Each users will receive a personal badge card once arriving on site
Additional training requirements may be identified for users planning to perform particular types of work at the European XFEL
Before getting access to the labs / laser rooms users must take an onsite training given by local contact or room responsible
In future the instrument group leader or the instrument local contact will give an onsite training to the users before starting the experiment. This include the permission to carryout the area search in the experiment hutch & knowledge of the control system.

## Slide 15: Some Other Questions?
Who is providing the equipment and materials (e.g. gas cylinders, chemicals, radioisotopes, biological samples etc.) ?
Gas cylinders, standard lab chemicals, sealed radioactive sources are usually provided by European XFEL
  Biological & chemical samples are provided by users
How is the equipment evaluated against the national/EU requirements?
Equipment must be CE certified, or bringing letter of conformity according to European and German
safety legislation when it is feasible. In exceptions the machinery safety specialist from safety group
= inspections, different risk assessments.
How to ensure the safety rules are followed (procedures, experiences)?
Extended safety organization ; Frequent monitoring by safety group, constant supervision by instrument group, local contacts and lab support staff

## Slide 16: Some Other Questions?
How to proceed in case of violations of safety rules?
When there is an imminent danger safety group (in fact any staff member) can force the user to leave the area immediately; All safety violations must be immediately reported to the instrument group leader and he/ she must take action ASAP.
How to be sure that nobody takes any object that might be activated outside of the controlled area?
Portal radiation monitoring system for vehicles at the vehicle exit. If the vehicle containing the activated objects exits the controlled area a bollard system will come out of the ground and stops the vehicle.
Waste management – ownership of the dangerous waste generated by the user during the experiment, recommended procedures for disposal (fees for the disposal by ELI BL?)
For onsite disposing the dangerous waste, disposal collective vessels and procedures of disposal are provided by SRP. SRP specialist, will categorize the waste according to the European union catalogue& contact a special company to collect the waste. At the moment, European XFEL pay for this process .

## Slide 17
Thank you for your attention!