## Slide 1: SRF Cavity and Cryomodule Conceptual Design for eRHIC
Douglas Holmes
February 7, 2019

## Slide 2: Outline
eRHIC general layout and Electron Storage Ring (eSR) cryomodule location
Pre-Conceptual cavity mechanical design/analysis
Pre-Conceptual Cryomodule Configuration
Power Couplers R&D
Beamline HOM Absorbers R&D

## Slide 3: eRHIC Layout
eRHIC is BNL’s proposed Electron-Ion Collider
Utilizes the existing ion accelerator systems of RHIC
Add Electron Rapid Cycling Synchrotron (RCS) Injector and Electron Storage Ring (eSR)
eSR SRF Systems are located at IR10

## Slide 4: eRHIC IR10
eSR Cryomodules
RCS Ring
Existing
Hadron Ring
1.4 m
1.5 m
0.5 m
1.27 m

## Slide 5: eSR Cryomodule
Single 2-cell 563 MHz SRF cavity per cryomodule
V = 8 MV/cavity
2x 500 kW adjustable Fundamental Power Couplers (FPCs).
4x SiC Beamline HOM Absorbers (BLAs)
4 cryomodules in total (upgradeable to 12 for full luminosity and energy reach)
2K operating temperature
Top loading design
563 MHz Cavity Cryomodule

## Slide 6: Cavity Concept Design
Helium Vessel Interface
Cavity wall thickness: 4mm
FPC Ports
Stainless Steel Flanges
w/ Knife Edge Seals
Tuner Interface Ring
RF Pickup Port
Iris Stiffener
1.24 m
270 mm ID

## Slide 7: Mechanical Resonance Modes
Mode 1
Mode 5
Mode 4
Mode 3
Mode 2
No Iris Stiffener
With Iris Stiffener
No Iris Stiffener
With Iris Stiffener

## Slide 8: Cavity Tuning
Total Cavity Compression = -0.41 mm
Total He Vessel Extension = +0.24 mm
He Vessel Edge Fixed
910 kg Tuner load
Spring rate:
  2,270 kg/mm iris stiffened
  1,500 kg/mm unstiffened
Tuning Coef. est.:
  300 kHz/mm iris stiffened
  190 kHz/mm unstiffened
For 100 kHz Tuning (stiffened cavity):
  Stroke= 0.33mm
  Force=730 kg
  Induced Stress= 35 MPa (5,100 psi )
Load Conditions:
Max Cavity Stress 43.9 MPa (6,360 psi)
Max Cavity Deflection 0.41mm

## Slide 9: Helium Vessel, Tuner, FPC Concept
Helium Vessel
Cutaway view
Tuner Bellows
Cavity
Tuner Frame
FPCs
Tuner
Actuation
Tuner Flexure
Tuner Struts
Helium Vessel Hangers

## Slide 10: Cavity String and Top Plate Assembly
FPC
Supply/Return Helium Bayonets
2K Helium Vapor Return
Pressure Safety Release
Tuner Motor Interface
Cavity Tuner
2K/4.5K Heat Exchanger
FPC Window
2-phase Helium Header
String Support
Beam pipe Thermal Transition
Cryo Valves
Helium Liquid Level Tube
Instrument Feedthroughs

## Slide 11: Cryomodule Build-up Sequence
Helium Header Integration
Top Cover Integration
Inner Magnetic Shield Installation
Thermal Shield Installation
Outer Magnetic Shield Installation
FPC Wave Guide Integration
Vacuum Closure, BLA and gate valve Integration

## Slide 12: Cryomodule with BLAs
~5 m
BLAs
BLAs

## Slide 13: FPC R&D
Investigating the use of a stub tuner as impedance transformer in the fixed waveguide section for FPC Qext adjustment
FPC Qext has to be adjusted from 4E4 to 2.75E5 for various operation scenarios
Two fixed coupling 500 kW FPCs ordered for testing
Impedance transformer is currently under development
Stub Tuner
Stub Tuner

## Slide 14: Stub Tuner Power Loss
Initial analysis shows maximum ~4 kW heat load from stub tuners before optimization
Varies with Qext adjustment
Total Power Loss for both tuners
500 kW forward power
Q-Factor (external (mode 1)
Tuning Height

## Slide 15: FPC R&D Status and Plans
Existing Waveguide
Conditioning Box
Stub Tuner
Two 500 kW fixed FPCs have been ordered, delivery Spring 2019
The impedance transformer design and optimization is ongoing
Plan to condition the FPCs up to 500 kW in standing wave late 2019, with and without impedance transformer
Adjustable Short
Waveguide Conditioning Box

## Slide 16: BLA R&D
RF model of the two-cell cavity with the SiC based BLAs*
*Physics design by Philipp Kolb
Manufacture of a scaled up version of the BLAs developed at ANL for the APS upgrade
Qty 4 BLAs per cavity
80 kW HOM power/cavity  20 kW each BLA
BLAs are at room temperature and are water cooled
Plan to test at high power (704MHz)
CoorsTek SC-35 SiC Cylinder
(~308 mm ID)
304 Stainless Steel Housing
OFE Copper Sleeve

## Slide 17: BLA Fabrication Plan
304mm ID
308.6mm ID
Weld Assembly
(~20 lbs.)
Machined Details
Machined Details
Braze Assembly
(~140 lbs.)
Machined Assembly
(~95 lbs.)
Shrink-fit Assembly
(~120 lbs.)
SiC Cylinder
(~25 lbs.)

## Slide 18: Shrink Fit Analysis Details
0.005” radial gap
0.0025” radial
interference fit
304 Stainless Steel
9.449” long
0.400” Thick OFE Copper
0.220” Thick SS
20 °C
100 °C
0.563” Thick SiC

## Slide 19: Shrink-fit Induced Stress
Elastic analysis:
Copper peak stress = 7,000 psi
Stainless Steel peak stress = 8,000 psi
SiC peak stress = 10,900 psi
Elastic-plastic analysis:
Copper peak stress = 5,000 psi
Stainless Steel peak stress = 7,000 psi
SiC peak stress = 9,240 psi
Material properties:
Annealed Cu yield ≈ 5,000 psi
S. Steel yield = 30,000 psi
SC-35 compressive strength = 98,000 psi

## Slide 20: Shrink-fit Induced Copper Strain
Elastic analysis
Simulated elastic-plastic analysis
Small change in strain  Minimal plastic deformation in copper

## Slide 21: Shrink-fit Induced SiC Surface Pressure
Elastic analysis
Simulated elastic-plastic analysis
Surface pressure range is 100 to 1,000 psi
 Plan to increase copper and/or stainless thickness to increase surface pressure for increased conductive heat transfer

## Slide 22: Heat Transfer Analysis Details
CoorsTek SC-35 SiC
12.125” ID x 13.250” OD
Helical Cooling Channel
0.50” wide x 0.225 high
X 33 ft long
9.449” Long
0.400” Thick
OFE Copper
0.220” Thick
304 Stainless
Water Cooling Specifications:
20 kW heat load, Q
20 °C water temperature rise, dT
20 °C inlet temperature, 40 °C outlet temperature (use 30 °C for calculations)
Minimum Mass flow rate, M(water) = Q/(Cp*dT) = (20,000J/s)/(4070.2J/kg-K*20K)= 0.246 kg/sec
Volumetric flow rate V(water) = M(water)/ρ = (0.246kg/s)/(.0009952kg/cc)= 247.2 cc/sec (3.92 gpm)
Flow velocity= 3.5 m/s  Heat Transfer Coefficient = 12,418 W/K-m^2

## Slide 23: Heat Transfer Analysis Details
@ 22 °C
@ 24 °C
@ 26 °C
@ 28 °C
@ 30 °C
@ 32 °C
@ 34 °C
@ 36 °C
@ 38 °C
W on inner surface
4.0 gpm @ 20 °C In
Surface Conductance between SiC OD and Copper ID: 1x10^4 to W/K-m^2 *
4.0 gpm @ 40 °C Out
X4 = 20 kW Total Heat Load
26 psi pressure drop
*S.H. Kim, et. al., “Beam Pipe HOM Absorbers in Bunch Lengthening Harmonic Cavity Cryomodule for Advanced Photon Source Upgrade”, Collaboration Meeting with BNL, 4/27/2017

## Slide 24: Thermal Analysis Results
77°C Max SiC Temp
60 °C Max Flange Temp
6 to 10 °C ΔT across SiC-Copper interface
Plan to divide water cooling into two channels to symmetrize SiC cooling and reduce peak temperatures

## Slide 25: Summary
eRHIC cavity and cryomodule design will continue to evolve as beam physics requirements mature
High power FPC testing planned for later in 2019
BLA manufacturing to begin Spring 2019 with high power testing planned for 2020

## Slide 26: Thank you for listening!
Acknowledgements:
ANL: Sang-hoon Kim, Michael Kelly
BNL: Cliff Brutus, Philipp Kolb, Gary McIntyre, Scott Seberg, Kevin Smith, Wencan Xu, Alex Zaltsman
CERN: Eric Montesinos